## Slide 1
PY2021 LI Evaluation of California Capacity Bidding Programs
Date: May 4, 2022 Prepared for: 2022 DRMEC Load Impact Workshop

## Slide 2: Agenda
Program Descriptions
Program Results by IOU
Key Findings
Overall Description
Ex-Post Load Impacts
Statewide Summaries
Descriptions by IOU
Monthly Nominations
Dispatch Summary
Ex-Ante Forecast Assumptions
Ex-Ante Load Impacts

## Slide 3
3
Program Descriptions

## Slide 4
Program Basics
Statewide aggregator-managed DR program offered by PG&E, SCE, and SDG&E
Aggregator Responsibilities
Recruitment and contracting with eligible customers,
Capacity Payments
Aggregators receive monthly capacity payments based on nominated load + energy payments based on kWh delivered reductions during events.
Capacity payments may be adjusted based on performance.
Aggregators receive the full monthly capacity payment according to their nominations if no events are dispatched for that month.
Monthly resource nominations to IOU programs,
Customer/resource delivery to dispatched events,
Customer disbursement of program incentives.
Report definition of “program” is IOU + Customer Class + Notification Type
Program Description
Applied Energy Group, Inc. | appliedenergygroup.com

## Slide 5: Program Descriptions by IOU
 | PG&E | SCE | SDG&E
Active Programs | Residential Day Ahead Non-Residential Day Ahead | Non-Residential Day Ahead Non-Residential Day Of | Non-Residential Day Ahead Non-Residential Day Of
Products | Prescribed DA Elect DA Elect+ DA | DA 1-6 Hour DO 1-6 Hour | DA 11-7 Hour DA 1-9 Hour DO 11-7 Hour DO 1-9 Hour
Dispatch Window | 1 PM – 9 PM | 3 PM – 9 PM | 11 AM – 7 PM or 1 PM – 9 PM
Event Trigger | CAISO Market Awards | CAISO Market Awards | CAISO Market Awards
Eligible Days | May – October non-holiday weekdays, option for weekends | Year-Round non-holiday weekdays | May – October non-holiday weekdays
Event duration | 1-4 hours, 2-6 hours, 1-8 hours or 1-24 hours | 1-6 hours | 2-4 hours
Event day limit | 6 events per month | 5 events per month | 6 events per month
Event hour limit | 30 hours per month | 30 hours per month | 24 hours per month

## Slide 6
6
PG&E
Programs

## Slide 7
PG&E
Monthly Nominations
Applied Energy Group, Inc. | appliedenergygroup.com
Month | Residential DA |  | Non-Residential DA | 
 | Enrolled Accounts | Nominated Capacity (MW) | Enrolled Accounts | Nominated Capacity (MW)
May | - | - | 701 | 34.2
June | - | - | 750 | 41.6
July | - | - | 938 | 61.3
August | - | - | 942 | 60.8
September | 23 | XXX | 980 | 56.0
October | 19 | XXX | 960 | 47.0
Avg. Summer | 21 | XXX | 879 | 50.1
Chart: Average Summer Nominations by Program Year
| 2019 | 2020 | 2021 | 2019 | 2020 | 2021 | Res DA | Non-Res DA
MW | 0 | 0.16667 | 0.025 | 24.8878 | 33.1812 | 50.1365
Participants | 0 | 563 | 21 | 689.8333 | 912.6667 | 878.5
Chart: Non-Res DA by Size & Industry
| Medium Agriculture | Large Agriculture | Medium Wholesale | Large Wholesale | Small Retail | Medium Retail | Medium Offices | Large Offices | Medium Government | Other
 | 222 | 125 | 71 | 53 | 63 | 363 | 39 | 35 | 25 | 102

## Slide 8: Key Definitions: Nomination v. Dispatch
 | Nomination (July) | Dispatch (July Event 1) SubLAP 2; HE20 | Dispatch (July Event 2) SubLAP 1 & 3; HE20-HE21
Aggregator 1 | Resource 1 (SubLAP 1) |  | Resource 1 (SubLAP 1)
 | Resource 2 (SubLAP 2) | Resource 2 (SubLAP 2) | 
 | Resource 3 (SubLAP 3) |  | Resource 3 (SubLAP 3)
Aggregator 2 | Resource 4 (SubLAP 2) | Resource 4 (SubLAP 2) | 
 | Resource 5 (SubLAP 3) |  | Resource 5 (SubLAP 3)
Aggregator 3 | Resource 6 (SubLAP 2) | Resource 6 (SubLAP 2) | 
Aggregator 4 | Resource 7 (SubLAP 1) |  | Resource 7 (SubLAP 1)
 | Resource 8 (SubLAP 2) | Resource 8 (SubLAP 2) | 
 | Resource 9 (SubLAP 3) |  | Resource 9 (SubLAP 3)

## Slide 9
PG&E
Dispatch Summary
Applied Energy Group, Inc. | appliedenergygroup.com
Chart: MW
| May | Jun | Jul | Aug | Sep | Oct | May | Jun | Jul | Aug | Sep | Oct | Res DA | Non-Res DA
MW (Nom) | 34.178 | 41.582 | 61.329 | 60.81 | 55.97 | 46.95
MW (Disp) | 7.19 | 16.6437 | 9.9454 | 1.0421 | 16.0141 | 0.83125
Participants (Disp) | 23 | 19 | 86 | 358.6667 | 415.1143 | 22.7143 | 612.7143 | 15.5
Month | Residential DA |  | Non-Residential DA | 
 | Total Event Days | Total Event Hours | Total Event Days | Total Event Hours
May |  |  | 3 | 3
June |  |  | 3 | 5
July |  |  | 13 | 31
August |  |  | 7 | 16
September | 6 | 18 | 7 | 22
October | 6 | 13 | 9 | 18
Total Summer | 12 | 31 | 42 | 95

## Slide 10: Average Event Day
PG&E
 | HE14 | HE15 | HE16 | HE17 | HE18 | HE19 | HE20 | HE21
Event 1 |  |  |  |  |  |  |  | 
Event 2 |  |  |  |  |  |  |  | 
Event 3 |  |  |  |  |  |  |  | 
Event 4 |  |  |  |  |  |  |  | 
Event 5 |  |  |  |  |  |  |  | 
Event 6 |  |  |  |  |  |  |  | 
Event 7 |  |  |  |  |  |  |  | 
Event 8 |  |  |  |  |  |  |  | 
Event 9 |  |  |  |  |  |  |  | 
Event 10 |  |  |  |  |  |  |  | 
Event 11 |  |  |  |  |  |  |  | 
Event 12 |  |  |  |  |  |  |  | 
Event 13 |  |  |  |  |  |  |  | 
Event 14 |  |  |  |  |  |  |  | 
Event 15 |  |  |  |  |  |  |  | 
Non-Res DA
*Shaded blocks represent event hours dispatched.
**HE20 is the reporting hour.

## Slide 11: Key Definitions: Delivery Performance v. Adjusted Delivery Performance
 | Dispatched MW | HE20 Dispatched | HE14 | HE15 | HE16 | HE17 | HE18 | HE19 | HE20 | HE21
Event 1 | 7.0 | Yes |  |  |  |  |  |  |  | 
Event 2 | 24.4 | Yes |  |  |  |  |  |  |  | 
Event 3 | 24.7 | Yes |  |  |  |  |  |  |  | 
Event 4 | 0.9 | Yes |  |  |  |  |  |  |  | 
Event 5 | 10.5 |  |  |  |  |  |  |  |  | 
Event 6 | 11.0 |  |  |  |  |  |  |  |  | 
Event 7 | 11.0 |  |  |  |  |  |  |  |  | 
Event 8 | 9.3 | Yes |  |  |  |  |  |  |  | 
Event 9 | 11.0 | Yes |  |  |  |  |  |  |  | 
Event 10 | 11.0 |  |  |  |  |  |  |  |  | 
Event 11 | 2.3 |  |  |  |  |  |  |  |  | 
Event 12 | 0.1 | Yes |  |  |  |  |  |  |  | 
Event 13 | 5.8 | Yes |  |  |  |  |  |  |  | 
Event 14 | 9.3 | Yes |  |  |  |  |  |  |  | 
Event 15 | 0.1 | Yes |  |  |  |  |  |  |  | 
Total Dispatch MW | 138.5 |  |  |  |  |  |  |  |  | 
HE20 Dispatch MW | 92.6 |  |  |  |  |  |  |  |  | 

## Slide 12
PG&E
Ex-Post Load Impacts
Applied Energy Group, Inc. | appliedenergygroup.com
Chart: MW
| May | Jun | Jul | Aug | Sep | Oct | May | Jun | Jul | Aug | Sep | Oct | Res DA | Non-Res DA
Overall Dispatched | 7.19 | 16.6437 | 9.9454 | 1.0421 | 16.0141 | 0.83125
HE20 Dispatched | 0.2 | 16.6437 | 9.9454 | 0.78571 | 6.3391 | 0.30521
Ex-Post Impacts | 4.4251 | 18.6783 | 7.1658 | 0.63056 | 10.0436 | 0.26011
Program | Month | Ex-Post Estimate (MW) | Dispatched |  | HE20 Dispatched | 
 |  |  | MW | % Delivered | MW | Adj % Delivered
Res DA | Avg. Event (2021) | XX | XX | XX | XX | XX
 | Avg. Event (2020) | XX | XX | XX | - | -
 | Avg. Event (2019) | XX | XX | XX | - | -
Non-Res DA | Avg. Event (2021) | 13.0 | 13.5 | 96% | 12.4 | 105%
 | Avg. Event (2020) | 10.0 | 15.6 | 64% | - | -
 | Avg. Event (2019) | 9.8 | 9.2 | 106% | - | -

## Slide 13
PG&E
Ex-Ante Forecast Assumptions
Applied Energy Group, Inc. | appliedenergygroup.com
 | Res DA | Non-Res DA
Program Changes | No program changes impacting forecast assumptions | No program changes impacting forecast assumptions
Nomination Forecast | 4 MW for August 2023 2.5 MW for 2022 Flat forecast from 2023-2032 | 55 MW for August 2022 Flat forecast from 2023-2032
Delivery Performance | 61% min delivery threshold for penalties | 100% based on PY2021 Ex-Post
Impact Degradation Rate* | N/A due to absence of historical performance data | Based on PY2020-2021 historical data.
Max Load Impact | Used % impacts from HE20 results due to solar customers with less available load during earlier hours of the RA window | HE20 per-customer impacts from Ex-Post
RA Window Response | 4-hour max response based on historical preference to the 1-4-hour event duration option; assume no response in HE21 (5th hour) | 4-hour max response based on historical preference to the 1-4-hour event duration option; assume no response in HE21 (5th hour)
*Represents how customers maintain impacts through events called for longer durations, similar to the 5-hour RA Window.

## Slide 14: Ex-Ante Hourly Load Profiles
PG&E
Non-Res DA
PG&E 1-in-2, August Peak Day, 2022
Res DA
PG&E 1-in-2, August Peak Day, 2023

## Slide 15
PG&E
Ex-Ante Load Impact Forecast
Applied Energy Group, Inc. | appliedenergygroup.com
Chart: Number of Participants
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
Non-Residential DA | 1505 | 1505 | 1505 | 1505 | 1505 | 1505 | 1505 | 1505 | 1505 | 1505 | 1505
Residential DA | 0 | 6972 | 6972 | 6972 | 6972 | 6972 | 6972 | 6972 | 6972 | 6972 | 6972
Chart: Load Impact (MW)
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
Non-Residential DA | 37.0788 | 37.0788 | 37.0788 | 37.0788 | 37.0788 | 37.0788 | 37.0788 | 37.0788 | 37.0788 | 37.0788 | 37.0788
Residential DA | 0 | 1.2866 | 1.2866 | 1.2866 | 1.2866 | 1.2866 | 1.2866 | 1.2866 | 1.2866 | 1.2866 | 1.2866
PG&E 1-in-2, August Peak Day
Program | Estimate | # of Accounts | Aggregate (MW) |  | Per-Customer (kW) |  | % Impact
 |  |  | Impact | Ref. Load | Impact | Ref. Load | 
Res DA* | PY2021 Forecast | 4,357 | 0.9 | 2.7 | 0.2 | 0.6 | 32%
 | PY2020 Forecast | 16,494 | 4.9 | 23.6 | 0.3 | 1.4 | 21%
Non-Res DA | PY2021 Forecast | 1,505 | 37.1 | 214.5 | 24.6 | 142.5 | 17%
 | PY2020 Forecast | 2,258 | 44.7 | 292.8 | 19.8 | 129.7 | 15%
*Shown for 2022 Typical event day due to zero forecasted August 2022 enrollments.

## Slide 16
16
SCE
Programs

## Slide 17
SCE
Monthly Nominations
Applied Energy Group, Inc. | appliedenergygroup.com
Month | Non-Residential DA |  | Non-Residential DO | 
 | Enrolled Accounts | Nominated Capacity (MW) | Enrolled Accounts | Nominated Capacity (MW)
May | 416 | 10.2 | 278 | 4.2
June | 414 | 9.9 | 279 | 4.4
July | 403 | 10.6 | 266 | 4.1
August | 379 | 8.7 | 265 | 3.4
September | 373 | 9.0 | 270 | 3.6
October | 364 | 7.2 | 259 | 3.3
Avg. Summer | 392 | 9.3 | 270 | 3.8
Chart: Average Summer Nominations by Program Year
| 2019 | 2020 | 2021 | 2019 | 2020 | 2021 | Non-Res DA | Non-Res DO
MW | 4.2688 | 7.1263 | 9.2602 | 6.8851 | 5.3927 | 3.8302
Participants | 245 | 414.6667 | 391.5 | 350.3889 | 382.8333 | 269.5
Chart: Non-Residential by Size and Industry
| Medium Wholesale | Large Wholesale | Small Retail | Medium Retail | Large Retail | Other
 | 13 | 28 | 32 | 517 | 84 | 41

## Slide 18
SCE
Dispatch Summary
Applied Energy Group, Inc. | appliedenergygroup.com
Chart: MW
| May | Jun | Jul | Aug | Sep | Oct | May | Jun | Jul | Aug | Sep | Oct | Non-Res DA | Non-Res DO
MW (Nom) | 10.206 | 9.886 | 10.584 | 8.651 | 9.012 | 7.222 | 4.183 | 4.42 | 4.06 | 3.418 | 3.593 | 3.307
MW (Disp) | 10.206 | 9.886 | 7.56 | 8.651 | 5.07 | 4.045 | 4.183 | 2.6717 | 2.4421 | 2.6553 | 2.567 | 0
Participants (Disp) | 416 | 414 | 287.8571 | 379 | 192.2 | 189.8 | 278 | 171.125 | 174.2857 | 213.5 | 214 | 0
Month | Non-Residential DA |  | Non-Residential DO | 
 | Total Event Days | Total Event Hours | Total Event Days | Total Event Hours
May | 5 | 7 | 5 | 7
June | 5 | 20 | 8 | 38
July | 7 | 21 | 7 | 23
August | 5 | 26 | 6 | 28
September | 5 | 30 | 1 | 4
October | 5 | 22 | 0 | 0
Total Summer | 32 | 126 | 27 | 100

## Slide 19: Average Event Day
SCE
 | HE16 | HE17 | HE18 | HE19 | HE20 | HE21
Event 1 |  |  |  |  |  | 
Event 2 |  |  |  |  |  | 
Event 3 |  |  |  |  |  | 
Event 4 |  |  |  |  |  | 
Event 5 |  |  |  |  |  | 
Event 6 |  |  |  |  |  | 
Event 7 |  |  |  |  |  | 
Event 8 |  |  |  |  |  | 
Event 9 |  |  |  |  |  | 
Event 10 |  |  |  |  |  | 
Event 11 |  |  |  |  |  | 
Event 12 |  |  |  |  |  | 
Event 13 |  |  |  |  |  | 
Event 14 |  |  |  |  |  | 
Event 15 |  |  |  |  |  | 
Non-Res DA
Non-Res DO
*Shaded blocks represent event hours dispatched.
**HE20 is the reporting hour.

## Slide 20
SCE
Ex-Post Load Impacts
Applied Energy Group, Inc. | appliedenergygroup.com
Chart: MW
| May | Jun | Jul | Aug | Sep | Oct | May | Jun | Jul | Aug | Sep | Oct | Non-Res DA | Non-Res DO
Overall Dispatched | 10.206 | 9.886 | 7.56 | 8.651 | 5.07 | 4.045 | 4.183 | 2.6717 | 2.4421 | 2.6553 | 2.567
HE20 Dispatched | 10.206 | 9.886 | 7.56 | 8.197 | 5.07 | 4.045 | 4.183 | 2.6717 | 2.4421 | 2.4457 | 2.567
Ex-Post Impacts | 6.3 | 5.5743 | 4.2538 | 4.9276 | 1.8059 | 0.99711 | 2.9036 | 1.6852 | 2.2827 | 1.5457 | 1.5328
Program | Month | Ex-Post Estimate (MW) | Dispatched |  | HE19 Dispatched | 
 |  |  | MW | % Delivered | MW | Adj % Delivered
Non-Res DA | Avg. Event (2021) | 4.0 | 7.6 | 53% | 7.5 | 53%
 | Avg. Event (2020) | 3.9 | 6.0 | 65% | - | -
 | Avg. Event (2019) | 2.7 | 3.8 | 72% | - | -
Non-Res DO | Avg. Event (2021) | 2.0 | 2.9 | 70% | 2.8 | 71%
 | Avg. Event (2020) | 2.9 | 4.4 | 67% | - | -
 | Avg. Event (2019) | 2.4 | 4.6 | 52% | - | -

## Slide 21
SCE
Ex-Ante Forecast Assumptions
Applied Energy Group, Inc. | appliedenergygroup.com
 | Non-Residential Day Ahead & Day Of
Program Changes | No program changes impacting forecast assumptions
Enrollment Forecast | Flat enrollment forecast based on average PY2021 summer enrollment
Delivery Performance | 53% for DA summer; 71% for DO summer 0% delivery performance for non-summer months Based on PY2021 findings
Impact Degradation Rate* | Based on PY2019-2021 historical data.
Max Load Impact | HE20 per-customer impacts from Ex-Post
*Represents how customers maintain impacts through events called for longer durations, similar to the 5-hour RA Window.

## Slide 22: Ex-Ante Hourly Load Profiles
SCE
Non-Res DO
SCE 1-in-2, August Peak Day, 2022
Non-Res DA
SCE 1-in-2, August Peak Day, 2022

## Slide 23
SCE
Ex-Ante Load Impact Forecast
Applied Energy Group, Inc. | appliedenergygroup.com
SCE 1-in-2, August Peak Day
Program | Estimate | # of Accounts | Aggregate (MW) |  | Per-Customer (kW) |  | % Impact
 |  |  | Impact | Ref. Load | Impact | Ref. Load | 
Non-Res DA | PY2021 Forecast | 410 | 4.2 | 32.1 | 10.1 | 78.3 | 13%
 | PY2020 Forecast | 410 | 2.6 | 36.2 | 6.2 | 88.3 | 7%
Non-Res DO | PY2021 Forecast | 290 | 1.7 | 30.4 | 6.0 | 104.7 | 6%
 | PY2020 Forecast | 380 | XXX | XXX | XXX | XXX | XXX
Chart: Number of Participants
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
Day Ahead | 410 | 410 | 410 | 410 | 410 | 410 | 410 | 410 | 410 | 410 | 410
Day Of | 290 | 290 | 290 | 290 | 290 | 290 | 290 | 290 | 290 | 290 | 290
Chart: Load Impacts (MW)
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
Day Ahead | 4.1549 | 4.1549 | 4.1549 | 4.1549 | 4.1549 | 4.1549 | 4.1549 | 4.1549 | 4.1549 | 4.1549 | 4.1549
Day Of | 1.7352 | 1.7352 | 1.7352 | 1.7352 | 1.7352 | 1.7352 | 1.7352 | 1.7352 | 1.7352 | 1.7352 | 1.7352

## Slide 24
24
SDG&E
Programs

## Slide 25
SDG&E
Monthly Nominations
Applied Energy Group, Inc. | appliedenergygroup.com
Month | Non-Residential DA |  | Non-Residential DO | 
 | Enrolled Accounts | Nominated Capacity (MW) | Enrolled Accounts | Nominated Capacity (MW)
May | 40 | 1.4 | 134 | 2.9
June | 48 | 1.2 | 126 | 3.2
July | 36 | 1.0 | 133 | 3.3
August | 48 | 1.0 | 133 | 3.3
September | 35 | 0.8 | 130 | 3.4
October | 48 | 1.0 | 131 | 3.1
Avg. Summer | 43 | 1.1 | 131 | 3.2
Chart: Average Summer Nominations by Program Year
| 2019 | 2020 | 2021 | 2019 | 2020 | 2021 | Non-Res DA | Non-Res DO
MW | 0.50433 | 0.53467 | 1.0701 | 3.4898 | 3.0275 | 3.1955
Participants | 10.8333 | 18.6667 | 42.5 | 183.5 | 158.5 | 131.1667
Chart: Non-Residential by Size and Industry
| Medium Retail | Large Retail | Medium Offices | Medium Government | Other
 | 101 | 44 | 12 | 12 | 15

## Slide 26
SDG&E
Dispatch Summary
Applied Energy Group, Inc. | appliedenergygroup.com
Chart: MW
| May | Jun | Jul | Aug | Sep | Oct | May | Jun | Jul | Aug | Sep | Oct | Non-Res DA | Non-Res DO
MW (Nom) | 1.3757 | 1.1901 | 1.0347 | 0.991 | 0.8048 | 1.0244 | 2.8669 | 3.1905 | 3.2747 | 3.3402 | 3.3716 | 3.1292
MW (Disp) | 1.1901 | 0.6945 | 0.6508 | 0.8048 | 1.0244 | 3.1655 | 3.1497 | 3.3402 | 3.3716 | 3.1292
Participants (Disp) | 0 | 48 | 18 | 30 | 35 | 48 | 0 | 124 | 123 | 133 | 130 | 131
Month | Non-Residential DA |  | Non-Residential DO | 
 | Total Event Days | Total Event Hours | Total Event Days | Total Event Hours
May | 0 | 0 | 0 | 0
June | 6 | 25 | 5 | 13
July | 7 | 16 | 5 | 12
August | 3 | 8 | 2 | 6
September | 6 | 17 | 6 | 19
October | 6 | 18 | 5 | 11
Total Summer | 28 | 84 | 23 | 61

## Slide 27: Average Event Day
SDG&E
 | HE12 | HE13 | HE14 | HE15 | HE16 | HE17 | HE18 | HE19 | HE20 | HE21
Event 1 |  |  |  |  |  |  |  |  |  | 
Event 2 |  |  |  |  |  |  |  |  |  | 
Event 3 |  |  |  |  |  |  |  |  |  | 
Event 4 |  |  |  |  |  |  |  |  |  | 
Event 5 |  |  |  |  |  |  |  |  |  | 
Event 6 |  |  |  |  |  |  |  |  |  | 
Event 7 |  |  |  |  |  |  |  |  |  | 
Event 8 |  |  |  |  |  |  |  |  |  | 
Event 9 |  |  |  |  |  |  |  |  |  | 
Event 10 |  |  |  |  |  |  |  |  |  | 
Event 11 |  |  |  |  |  |  |  |  |  | 
Event 12 |  |  |  |  |  |  |  |  |  | 
Event 13 |  |  |  |  |  |  |  |  |  | 
Event 14 |  |  |  |  |  |  |  |  |  | 
Event 15 |  |  |  |  |  |  |  |  |  | 
Non-Res DA
Non-Res DO
*Shaded blocks represent event hours dispatched.
**HE19 is the reporting hour.

## Slide 28
SDG&E
Ex-Post Load Impacts
Applied Energy Group, Inc. | appliedenergygroup.com
Chart: MW
| May | Jun | Jul | Aug | Sep | Oct | May | Jun | Jul | Aug | Sep | Oct | Non-Res DA | Non-Res DO
Overall Dispatched | 1.1901 | 0.6945 | 0.6508 | 0.8048 | 1.0244 | 3.1655 | 3.1497 | 3.3402 | 3.3716 | 3.1292
HE19 Dispatched | 1.1026 | 0.6945 | 0.6508 | 0.8048 | 1.0244 | 3.1655 | 3.1497 | 3.3402 | 3.3716 | 3.1292
Ex-Post Impacts | 0.46866 | 0.12994 | -0.068097 | 0.28191 | 0.14455 | 1.4289 | 0.043351 | 1.2634 | 1.3169 | 1.1936
Program | Month | Ex-Post Estimate (MW) | Dispatched |  | HE19 Dispatched | 
 |  |  | MW | % Delivered | MW | Adj % Delivered
Non-Res DA | Avg. Event (2021) | 0.3 | 1.1 | 25% | 1.0 | 26%
 | Avg. Event (2020) | 0.4 | 0.6 | 71% | - | -
 | Avg. Event (2019) | 0.4 | 0.7 | 54% | - | -
Non-Res DO | Avg. Event (2021) | 1.0 | 3.4 | 30% | 3.4 | 30%
 | Avg. Event (2020) | 2.2 | 2.9 | 74% | - | -
 | Avg. Event (2019) | 3.6 | 3.6 | 101% | - | -

## Slide 29
SDG&E
Ex-Ante Forecast Assumptions
Applied Energy Group, Inc. | appliedenergygroup.com
 | Non-Residential Day Ahead & Day Of
Program Changes** | Adding new Elect product options for the 1-9 PM dispatch window
Nomination Forecast | Solicited aggregator feedback on participation outlook for new Elect options and existing Prescribed options; this included current participants in other DR programs that will likely shift to CBP Elect options.
Enrollment Forecast | 2% growth from 2022-2027 1% DO+TI growth from 2022-2023
Delivery Performance | 48% based on PY2020-21 Ex-Post
Impact Degradation Rate* | Based on PY2019-2021 historical data.
Max Load Impact | HE19 per-customer impacts from Ex-Post
*Represents how customers maintain impacts through events called for longer durations, similar to the 5-hour RA Window.
** Currently assumes existing Prescribed options are offered until 2032

## Slide 30: Ex-Ante Hourly Load Profiles
SDG&E
Non-Res DO
SDG&E 1-in-2, August Peak Day, 2022
Non-Res DA
SDG&E 1-in-2, August Peak Day, 2022

## Slide 31
SDG&E
Ex-Ante Load Impact Forecast
Applied Energy Group, Inc. | appliedenergygroup.com
SDG&E 1-in-2, August Peak Day
Program | Estimate | # of Accounts | Aggregate (MW) |  | Per-Customer (kW) |  | % Impact
 |  |  | Impact | Ref. Load | Impact | Ref. Load | 
Non-Res DA | PY2021 Forecast | 105 | 2.3 | 10.6 | 22.0 | 101.4 | 22%
 | PY2020 Forecast | 19 | 0.2 | 2.3 | 11.8 | 120.0 | 10%
Non-Res DO | PY2021 Forecast | 208 | 3.5 | 20.4 | 16.9 | 98.3 | 17%
 | PY2020 Forecast | 167 | 1.5 | 16.0 | 9.1 | 95.8 | 9%
Chart: Number of Participants
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
CBP-DA | 105 | 107.1 | 109.242 | 111.4268 | 113.6554 | 115.9285 | 115.9285 | 115.9285 | 115.9285 | 115.9285 | 115.9285
CBP-DO including new TI | 208.06 | 212.2212 | 214.3224 | 218.6088 | 222.981 | 227.2458 | 227.2458 | 227.2458 | 227.2458 | 227.2458 | 227.2458
Chart: Load Impacts (MW)
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
CBP-DA | 2.3134 | 2.3597 | 2.4069 | 2.455 | 2.5041 | 2.5542 | 2.5542 | 2.5542 | 2.5542 | 2.5542 | 2.5542
CBP-DO including new TI | 3.5223 | 3.5928 | 3.6283 | 3.7009 | 3.7749 | 3.85 | 3.85 | 3.85 | 3.85 | 3.85 | 3.85

## Slide 32
32
Key Findings

## Slide 33
Statewide Ex-Post Impacts
Applied Energy Group, Inc. | appliedenergygroup.com
  *Results shown for summer months only (May through October)
Program |  | Nominations |  | Overall Dispatched |  | Reporting Hour Dispatched |  | Ex-Post Analysis |  | 
 |  | # Accts | Capacity (MW) | # Accts | Capacity (MW) | # Accts | Capacity (MW) | Impact (MW) | % Delivered | Adj. % Delivered
PG&E | Res DA | 21 | XXX | 21 | XXX | 14 | XXX | XXX | XXX | XXX
 | Non-res DA | 879 | 50.1 | 365 | 13.5 | 345 | 12.4 | 13.0 | 96% | 105%
SCE | Non-res DA | 392 | 9.3 | 312 | 7.6 | 308 | 7.5 | 4.0 | 53% | 53%
 | Non-res DO | 270 | 3.8 | 203 | 2.9 | 198 | 2.8 | 2.0 | 70% | 71%
SDG&E | Non-res DA | 43 | 1.1 | 46 | 1.1 | 43 | 1.0 | 0.3 | 25% | 26%
 | Non-res DO | 131 | 3.2 | 133 | 3.4 | 133 | 3.4 | 1.0 | 30% | 30%

## Slide 34
Statewide System Peak Hour Sep 8, 2021 (HE18)
Applied Energy Group, Inc. | appliedenergygroup.com
Program |  | Dispatched Accounts | Dispatched MW | Ex-Post Impact MW | Ex-Post % Delivered | Event Temp (F)
PG&E | Res DA | 23 | XX | XX | XX | 76
 | Non-res DA | 9 | XX | XX | XX | 71
SCE | Non-res DA | 269 | 6.5 | 2.9 | 45% | 85
 | Non-res DO | - | - | - |  | -
SDG&E | Non-res DA | 18 | 0.5 | 0.7 | 140% | 85
 | Non-res DO | 11 | 0.3 | 0.2 | 66% | 77

## Slide 35
Statewide Ex-Ante Impacts
Applied Energy Group, Inc. | appliedenergygroup.com
  *Results shown for summer months only (May through October)
Program |  | Enrollment Forecast |  |  | Aggregate Impact Forecast (MW) |  | 
 |  | 2022 | 2023 | 2027-2032 (Each Year) | 2022 | 2023 | 2027-2032 (Each Year)
PG&E | Res DA | 0 | 6,972 | 6,972 | 0.0 | 1.3 | 1.3
 | Non-res DA | 1,505 | 1,505 | 1,505 | 37.1 | 37.1 | 37.1
SCE | Non-res DA | 410 | 410 | 410 | 4.2 | 4.2 | 4.2
 | Non-res DO | 290 | 290 | 290 | 1.7 | 1.7 | 1.7
SDG&E | Non-res DA | 105 | 107 | 116 | 2.3 | 2.4 | 2.6
 | Non-res DO | 208 | 212 | 227 | 3.5 | 3.6 | 3.8

## Slide 36: AEG Team
Kelly Marrin
Project Director
Abigail Nguyen
Project Manager
Xijun Zhang
Analysis Lead
Maggie Buffum
Analysis Support
Dexter Luu
Analysis Support

## Slide 37
Thank You.