## Slide 1: RA 2024 LSE Forecast Adjustments
Lynn Marshall, Energy Assessments Division
October 12, 2024

## Slide 2: RA 2024 Load Forecast Process Overview
This document describes the process and methods CEC staff used to develop LSE forecasts for the RA 2024 compliance obligations, include hourly forecasts for the Slice of Day (SOD) test year.
The process can be categorized as follows:
Develop reference forecasts for total CPUC-jurisdictional load in each TAC area from the adopted CEC forecast.
  Also develop reference forecasts for aggregate direct access loads.
Determine LSE monthly coincident peak forecasts
  CEC first followed the existing process for monthly coincident peak forecast determination, then used that as input into the Slice of Day hourly forecast development.
Develop LSE Hourly forecasts, adjusting LSE hourly forecast consistent with the adjusted monthly peaks and recorded LSE hourly coincident load patterns.
The aggregate forecast data is available in Excel on the RA Compliance webpage:
https://www.cpuc.ca.gov/industries-and-topics/electrical-energy/electric-power-procurement/resource-adequacy-homepage/resource-adequacy-compliance-materials

## Slide 3: Reference Forecast
The reference forecast for CPUC-jurisdictional LSE forecasts begins with the forecasted monthly TAC coincident peaks from the 2022 Integrated Energy Policy Report Planning Scenario (CEDU 2022). The SDG&E reference forecast equals the TAC area forecast.
https://www.energy.ca.gov/data-reports/reports/integrated-energy-policy-report/2022-integrated-energy-policy-report-update-2

## Slide 4: PG&E Monthly Peak Reference Forecast
Forecasts for PGE and SCE are disaggregated by jurisdiction type. Estimated POU loads are subtracted from the TAC forecast. Staff used CEC forecasts of pumping loads and recorded and forecast loads of other POUs to estimate hourly POU loads. The hourly reference forecast is included in the posted Excel file.

## Slide 5: SCE Monthly Peak Reference Forecast
The CEC forecast for the SCE TAC area is disaggregated by jurisdiction type.

## Slide 6: Monthly Peak Forecasts

## Slide 7: Monthly Peak Load Forecast Adjustment Process
Estimate and apply coincidence factors to LSE forecasts.
Develop benchmark peak demand estimate for LSEs based on available data.
Evaluate and apply LSE-specific adjustments.
Apply adjustments for demand-side credits
Apply pro-rata adjustments to bring the total of the forecasts to within 1% of the CEC service area forecast.
Evaluate the reasonableness of pro-rata adjustments and total forecast for each LSE and service area.
If step 6 indicates pro rata adjustment is too large (i.e., aggregate DA load significantly exceeds cap), review steps 1-6.

## Slide 8: Monthly Peak Coincidence Adjustment Methodology
Coincidence adjustments should represent expected LSE demand at the time of a 1-in-2 CAISO-wide system peak.
Composite loads of LSEs were constructed by compiling 2022 actual loads with migrating load.
CAISO hourly loads are ranked. For each high-load hour selected, an LSE and TAC-specific coincidence factor (CF) is calculated:
  CF= LSE recorded load in TAC at time of CAISO system peak demand / LSE monthly maximum demand in TAC
  Various statistics on the distribution of CFs are calculated, including median CF of the top 3 to 5 days and percentile distribution of top 10 hours in month (excluding hours before HE 17 PST.
  Load diversity declines as demand rises, so if the most recent year doesn’t include enough relatively high load days, diversity will be overestimated, leading to increased unallocated load.
  As an alternative, staff may select the CF from the peak hour, a neighboring month, or a previous year. For example, in RA 2023 , April and May 2021 system loads were quite low, so CFs from April/May 2020, when loads and temperatures were higher, were used for many LSEs.
CAISO posts load data used for this analysis annually at: http://www.caiso.com/planning/Pages/ReliabilityRequirements/Default.aspx#Historical
Dates and times used by CEC staff are posted on the RA compliance webpage.

## Slide 9: LSE-Specific Adjustments
LSE forecasts are evaluated using historic loads and temperatures, load factors, review of forecast assumptions, and comparison with CEC forecast assumptions
Staff uses weather-normalized loads, month-ahead forecasts, and reported load migration to construct a reference estimate for each LSE by service area:
  IOU departing load estimates are revised for consistency with CCA forecasts as adjusted by CEC, and CEC-estimated direct access load.
  ESP forecasts are evaluated against Direct Access Service Report (DASR) sales. The final forecasts used the July 2022 reports. Aggregate ESP forecasts are evaluated against the direct access reference estimate to identify need for further adjustments.
  CCA forecasts are evaluated using weather-normalized peaks, historic load factors, and load migration activity.
  IOU forecasts may also be revised for differences with CEC service area forecast.

## Slide 10: Load Modifier Adjustments
LSE forecasts are credited with a share of net additional achievable energy efficiency and fuel substitution (AAEE/FS) and some load modifying demand response (LMDR) to the extent that it is not accounted for in their forecasts
  LSE share of incremental AAEE/FS is netted against amounts reported in their forecasts
  CEC staff reviews other load modifiers (EE, BTM PV, fuel substitution, storage, or transportation electrification) in LSE forecasts for consistency with reference forecast.
  The SCE credits in non-summer months also include CPUC-directed procurement of specific front-of-the-meter storage resources that have not yet completed CAISO deliverability processes.
  Demand-Side Credits

## Slide 11: Pro-Rata Adjustment
If the sum of the adjusted forecasts differs from the service area reference forecast by more than 1%, the exceedance is allocated based on the share of an LSE’s adjusted forecast of total service area adjusted forecasts.
Monthly Coincident Peak Pro-Rata Adjustment Percent by TAC

## Slide 12: Summary of 2024 CPUC-Jurisdictional Forecast Adjustments

## Slide 13: Slice of Day Forecasts

## Slide 14: Hourly Results
CEC provided individual adjusted demand forecasts to LSEs including:
  Hourly and peak forecast file
  Month-ahead forecast template for reporting load migration and showing noncoincident monthly peaks for CAISO CRR allocations.
Aggregate adjustment results are posted on the CPUC RA compliance page.
  The hourly reference forecasts for Slice of Day are on the “1. TAC and CPUC Hourly Forecast” sheet.
  The aggregated LSE Slice of Day forecasts are on the “4. LSE Hourly Forecasts” sheet.

## Slide 15: Hourly Forecast Adjustment Process
  Apply transmission and UFE losses to submitted forecasts.
  Calculate hourly coincidence factors using historic loads. These account for differences between the LSE’s load shape on the system peak day and the LSE’s peak day.
  Apply a load-stretching algorithm to transform the LSE’s load shape (with hourly coincidence adjustment), to fit the adjusted monthly peak and energy from the monthly peak forecast evaluation.
    Coincidence factors were selected to reflect the LSEs’ typical load shape on high load days and can equal or exceed 1.
  Calibrate peak hours to the coincident peak hour forecast from monthly peak forecasts if needed.
  Apply hourly demand-side credits. This includes AAEE/FS, LMDR, and in SCE, IFOM storage as directed by CPUC.
  Apply pro-rata adjustment to within 1% of 2022 IEPR 1-in-2 hourly forecast for the monthly coincident peak day, by TAC.

## Slide 16: Hourly Coincidence and Load Shape Modification
From the monthly peak forecasts, staff used the adjusted noncoincident peak (including LSE-specific adjustments) and corresponding adjusted daily energy. Energy was calculated using the LSE’s peak-to-energy ratio; this will be reevaluated for the next cycle.
The selected hourly coincidence factors were applied to the LSE’s submitted load shape. Then a load-stretching algorithm was applied to transform the load shape to fit the targeted daily peak and average daily energy demand.
Resulting profiles were evaluated against LSE actual shapes on high load days.
  Coincidence factors often vary significantly depending on BTM PV output. Days consistent with CEC forecast assumptions were used when available.
In posted results, the field “Net Coincidence and LSE-Specific Adjustment” shows the combined effects of 1) adjusting to the targeted monthly peak and energy, and 2) adjusting for coincidence patterns relative to LSEs’ forecasted load shape.
  The transformed coincident load shape therefore equals:
“Submitted” +”Transmission & UFE” + ”Net Coincidence and LSE-Specific Adjustment”.
  .

## Slide 17: Aggregate Pro-Rata Percent Adjustment by Month and Hour
  Positive pro-rata adjustments (meaning load forecasts are increased) tend to be largest during morning hours.
  Negative mid-day adjustments (a reduction to load forecasts) largely reflect LSE’s forecasting less BTM PV than in the CEC forecast.

## Slide 18: Summary
CEC plans to follow a similar process next year, but will evaluate areas for improvement, including
  benchmarking for LSE peak-day energy
  process for hourly coincidence and shaping adjustments.
Improvements to the CEC TAC area hourly forecasts are underway or planned in the IEPR proceeding. This includes revised BTM PV shapes.
For demand forecast-related questions or comments contact CEC staff at rafiling@energy.ca.gov