## Slide 1: Rule 21 Interconnection Discussion Forum Large-Scale Net Energy Metering Rule 21 Interconnection Projects BA Concerns
Jeffrey Billinton
Director, Transmission Infrastructure Planning
Jill Powers
Infrastructure & Regulatory Policy Manager
June 24, 2020

## Slide 2: Concerns: Planning/Technical Interconnection/Operational

## Slide 3: Planning Concerns/Issues
Concerns with current lack of required coordination on large-scale NEM projects during study process
  Currently no obligation to be notified of projects studied under Rule 21 interconnection
  No tariff obligation to share study results to ensure system will see “no harm” from interconnection.
  CAISO unable to advise or inform PTOs on the studies until they are complete or until NEM generation is operational
  Lack of participation within CAISO coordination regarding affected systems

## Slide 4: Technical Interconnection Concerns/Issues
Gaps between CAISO’s Generator Interconnection Agreements (GIA) and Rule 21 Interconnection Agreements
  NEM generators would not be subject to CAISO GIAs
    Although transmission-connected
    Potential for large capacity generation on transmission system
  Not subject to CAISO’s requirements for inverter-based resources :
    Frequency ride-through and loss of synchronism
    Voltage control and reactive current requirements
    Voltage ride-through and momentary cessation ride-through requirements
    Diagnostic equipment and data retention requirements
    Anti-islanding provisions
    Plant controller/inverter control coordination
  Potential additional technical requirement gaps with these projects interconnecting under Rule 21

## Slide 5: System and Market Operation Concerns/Issues
Lack of visibility and controllability of real-time operation of the NEM generator and exported generation
  NEM generators would not be subject to CAISO Resource Interconnection or New Resource Implementation (NRI) processes
    Are not identified in the Resource Interconnection Management System (RIMS)
  Not subject to CAISO’s telemetry or metering requirements for operational visibility or situational awareness of large capacity generator
  Unknown level of NEM generation controllability (if needed)
    BA-to-TOP communication needed if shutdown required
  Unable to forecast generation or its impact
  Inability to model appropriately
    Load or gen? At what value?
  Impact of daily dynamic operation of NEM generator to transmission reliability and market operations

## Slide 6: Resolving current Rule 21 NEM interconnection technical gaps
Apply applicable interconnection and operational requirements based on voltage level of the interconnection
Opportunity exists to align IEEE 1547 (2018) requirements being adopted with what is in best interest of the grid, both transmission and distribution