## Slide 1
Resource Adequacy
Coincident Adjustment Factor Methodology
Miguel Cerrutti
Demand Analysis Office
Energy Assessments Division
R.14-10-010 Workshop
California Public Utility Commission
San Francisco, February 18, 2016

## Slide 2
The problem
Initiatives since 2014 RA year
Suggestions for process improvements
Coincidence factor (CF)
Best approaches for calculating CF
Outline

## Slide 3
LSE-specific year-ahead and month-ahead load peak forecasts for RA compliance
LSE-specific peak load contribution at the time of CAISO’s peaks
  Accuracy and unbiasedness
Transparency / consistency
The problem

## Slide 4
      Embedding DR impacts in submitted data
      Posting CAISO’s five top monthly coincident peak load dates and hours
      Exploring alternative methods
        be relatively stable over time
        easy to calculate / monitor / apply
      Validation - adjustment
        load migration
        variations in weather and load composition
        forecasting an art as much as a science
Initiatives since 2014 RA Year

## Slide 5
Potentially use OASIS data instead of EMS data
  OASIS data is not confidential and available sooner
  Staff will post five peaks per month for last three years and study use of OASIS data by April 8
Staff will republish manual with criteria on when to use 1, 3, or five peaks per month
  Staff will always use last three years of historical data. This translates to either 36 points, 108 points, or 180 points of data
  Primary objective is accuracy
    Transparency and standardization are secondary objectives
Suggestions for process improvements

## Slide 6
Ratio LSE’s peaks at time of CAISO coincident peaks (CP) to the LSE’s non-coincident peaks (NCP)
how close LSE’s peak dates/hours are to CAISO’s five top monthly peak dates/hours
        CAISO’s peaks strongly correlated with RES
        LSEs with most RES load - most coincident
  cross-subsidization - RES/COM/IND
CAISO’s peaks - capacity to be procured
  LSEs capacity obligation / costs
Coincidence factor (CF)

## Slide 7
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Time of Peak | 1
GS-2 (Medium Comm. & Industrial) | 0.46706 | 0.46069 | 0.45748 | 0.46064 | 0.48104 | 0.55042 | 0.68797 | 0.80946 | 0.93743 | 0.98741 | 1 | 0.98963 | 0.96987 | 0.95407 | 0.93491 | 0.88937 | 0.84552 | 0.84458 | 0.78274 | 0.73933 | 0.68417 | 0.6251 | 0.56712 | 0.5204
GS-1 (Small Comm.) | 0.51002 | 0.50118 | 0.50059 | 0.50118 | 0.50236 | 0.52476 | 0.57842 | 0.61085 | 0.81309 | 0.95755 | 1 | 0.99175 | 0.95578 | 0.94458 | 0.91804 | 0.89092 | 0.87795 | 0.91097 | 0.79422 | 0.71167 | 0.66274 | 0.59965 | 0.56486 | 0.53892
Residential | 0.575 | 0.525 | 0.52328 | 0.52069 | 0.5319 | 0.5819 | 0.69741 | 0.73621 | 0.66552 | 0.65345 | 0.62328 | 0.59914 | 0.58621 | 0.57931 | 0.57759 | 0.60345 | 0.6819 | 0.88534 | 0.97759 | 1 | 0.99138 | 0.90431 | 0.78017 | 0.66379
Load profile – January
Source: LM 2012

## Slide 8
LSEs’ load profiles display significant variation across time in load shapes and time of peaks
Hourly loads – time-series
    CAISO EMS/OASIS/five top monthly peaks
    CPUC jurisdictional/non-jurisdictional LSEs
  LSE-specific CF
  LSE-composite CF – ESPs/CCAs
    load migration and new ESPs/CCAs
Coincidence factor (CF)

## Slide 9
Historic approach
    CF in the most recent year
    CF over the previous 3 or 5 years / median
    CF weather normalized
    CF trends over time
Forward / forecast approach
    CF in the next year
Best approaches for calculating CF

## Slide 10
CF variation over time
  load composition – RES, COM, IND, H2O
    stable over time - limited migrating load
    heavily drives LSEs peak forecasts
    no easy to correlate to peak – granularity
  weather – temperature
    easy to correlate to peak
    best expected coincidence patterns
Best approach – historic approach

## Slide 11
  Evaluation rule – load profile stability over time and time of peaks
    CF in the most recent year - LSE’s stable load profile / not differ much from CAISO’s times
    CF over three to five previous years – LSE’s unstable load profile / differ much from CAISO’s times
Best approach – historic approach

## Slide 12
      CAISO’s five top monthly weather normalized (WN) coincident peaks
        Time-series multi-step regressive model
        historical weather / Monte Carlo simulation
        Probability of exceedance distribution
      LSEs CF - WN CAISO-coincident peaks
      WN factor - ratio of WN CAISO-coincident peaks and LSE’s median of five top coincident peaks
Best approach – Weather normalized

## Slide 13
      Forward
        new ESPs/CCAs-specific CF
        most recent hourly load shapes–service area
        forecast non-coincident peaks/growth rates
      Forecast – validation
        CF as a function of load factors
        forecast NCP / CP
          NCP / CP weather
          CF / weather differences at NCP/CP times
        forecast CP – WN POE50
          best forecasting practices / reviewing
          methodology adequately / reasonably CP
Best approach – Forward / forecast approach

## Slide 14
Preliminary results
LSE | Moy | CF 0ne-year | CF three-years | CF forward forecast | CF average | WN factor
LSE1 | 5 | .855 | .917 |  |  | 
LSE2 | 2 | .860 | .717 |  |  | 
New CCA | 7 |  |  | .922 | .841 | 
New CCA | 8 |  | .945 |  | .941 | 
 | 7 |  | .752 |  | .846 | 
LSE3 | 8 |  |  |  |  | 1.152
LSE4 | 8 |  |  |  |  | .802
 |  |  | CF RES | CF COM/IND |  | 
LSE5 | 7 | .985 | .985 | .865 | .955 | 

## Slide 15
And so if …