## Slide 1: SCE Plug-In Electric (PEV) Smart Charging Pilot
DRMEC Meeting
May 10-11, 2016

## Slide 2: PEV Smart Charging Pilot Background
Approved by the California Public Utilities Commission and funded by ratepayers as part the SCE 2012-2014 Demand Response (DR) Application (A.11-03-003).
Pilot Timeframe: June 2013 – December 2014
Pilot Objectives:
Evaluate and possibly recommend a variety of residential-based smart charging technologies that utilizes non-AMI communications, including the internet and standardized protocols
Objectives are to sub-meter EV charging, provide real time demand and interval energy data, manage EV loads, and enable customer control (opt-in/opt-out functionality)
Create a common set of requirements and technologies SCE can leverage for future EV or other load management pilots or programs

## Slide 3: Pilot Phases
Design
  Pilot design based on input from stakeholders
  RFI/RFP for technology solutions
  Procurement of equipment
Lab Testing
  Commissioning, Registration and Enrollment
  Demand Response, Load Control and Price Signals
  Measurement and Monitoring
  Managed Charging
  Human Machine Interface
Field Testing
  Eight pilot sites deployed
  Nine DR test events conducted

## Slide 4: Smart Charging Architecture
Two Communication Paths
  Business to Business
    A 3rd Party, such as an electric vehicle manufacturer, received an OpenADR 2 DR signal from SCE
    The 3rd Party relayed the DR information via telematics directly to the electric vehicle or using other Electric Vehicle Service Provider (EVSP) communications to Electric Vehicle Supply Equipment (EVSE)
    Charging was throttled or curtailed by the electric vehicle or EVSE
  Direct
    Utilized a prototype gateway device to receive a Smart Energy Profile (SEP) 2.0 DR signal from SCE
    The gateway maintained connections to a smart meter and EVSE
    DR signals communicated directly from SCE with EVSE to throttle or curtail charging

## Slide 5: Smart Charging Architecture
Smart Charging Pilot Architecture- This diagram depicts the communication paths (Business to Business at the top and Direct at the bottom), protocols, and technologies deployed in the Smart Charging Pilot Demonstration.

## Slide 6: Findings and Recommendations
SEP 2.0 Implementation
  As a new standard utilizing prototype devices, no gaps or issues were discovered
Demand Response Server/System (DRS)
  The cloud based DRS used during the pilot was a flexible and effective system
  Automated enrollment would be needed for a larger or production implementation
Automated Discovery and Registration
  SEP 2.0 discovery and registration of devices connected to the gateway worked as expected
DR Signal Types
  Load management events need to be carefully implemented since different equipment interpret DR signals differently

## Slide 7: Findings and Recommendations
Customer and DR Strategies
  Even with a small sample size, 22% of events experienced an opt-out
  This may point to more flexibility needed with EV load management programs
Signal Speeds
  DR signalling usually required several minutes when relying on the Internet and several communication hops to reach the EV
  Based on this latency EV’s may not be a good resource for real-time dispatch DR events

## Slide 8: Next Steps
Larger Pilots
  Larger pilots such as SCE’s Workplace Charging Pilot will provide additional learnings regarding customer behavior and real world implementations
New Charging Technology Exploration
  Explore DC fast charging and vehicle to grid options with EV’s
Sub-metering
  The Smart Charging Pilot utilized alternatives to traditional sub-metering that should be explored further
SEP 2.0 Testing and Certification
  A strong testing and certification program will be needed if SEP 2.0 continues to be used
Bring Your Own Device Options
  Explore options for utilizing more customer purchased devices for DR