## Slide 1: Statewide Load impact evaluation of California Capacity Bidding Programs
2019 DRMEC Load Impact Workshop ● April 26th, 2019
Abigail Nguyen, Project Manager

## Slide 2: Agenda
  Program Descriptions
  Confidentiality
  Ex Post Impacts
  Ex Ante Impacts
  Key Findings

## Slide 3: Program Description
IOUs: PG&E, SCE, and SDG&E
Program Basics:
    Statewide aggregator-managed DR program
    Operates May-Oct for PG&E and SDG&E and year-round for SCE
    Participants must meet eligibility requirements
    Participants receive monthly capacity payments based on nominated load + energy payments based on kWh reductions during events
    Capacity payments may be adjusted based on performance
    Participants receive the full monthly capacity payment according to their nomination if no events called for that month
    Dual enrollment in energy-only program with a different notification type is allowed

## Slide 4: Program Description
Events & Products – PG&E
  Only day ahead notice is offered
  Events may be called on non-holiday weekdays during May through October with a maximum of 30 hours per month
  Elect+ aggregators can participate in additional hours outside the minimum specified hours
  Events are determined by CAISO market awards
  Future Program Changes:
    Residential participation is expected to begin in 2019
Product | Event Duration Options | Operating Hours Options | Price Threshold
Prescribed DA | 1-4 Hours 2-6 Hours | 11am – 7pm | PG&E sets the CAISO market bid price
Elect DA | 1-4 Hours 2-6 Hours | 11am – 7pm 1pm – 9pm | Aggregator sets the CAISO market bid price
Elect+ DA | 1-4 Hours 2-6 Hours 1-24 Hours | 11am – 7pm 1pm – 9pm | Aggregator sets the CAISO market bid price

## Slide 5: Program Description
Events & Products – SCE
  Events may be called on non-holiday weekdays year-round with a maximum of 30 hours per month
  Events can be triggered by any of the following conditions: high temperatures, resource limitations, a generating unit outage, transmission constraints, a system emergency, an alert called by the CAISO, or market prices go above a given price threshold.
  Future Program Changes:
    Residential enrollment in CBP-DA is forecasted to begin in 2023
    SCE is proposing to change the dispatch window (currently at 1pm-7pm) to align with the RA window (4pm-9pm).
Notice Type | Event Duration | Operating Hours
Day Ahead | 1-6 Hours | 1pm – 7pm
Day Of | 1-6 Hours | 1pm – 7pm

## Slide 6: Program Description
Events & Products – SDG&E
  Events may be called on non-holiday weekdays during May through October with a maximum of 24 hours per month
  Events are triggered when the market price hits the threshold above (appropriate by product) or as utility system conditions warrant
  Future Program Changes:
    Effective Dec. 15, 2018, DA products’ day-ahead market price trigger is $80/MWh
    Beginning in 2019, dual enrollment will no longer be allowed in CBP. Customers dually enrolled prior to Oct. 1, 2018 will be grandfathered in.
Notice Type | Event Duration | Operating Hours | Price Threshold | Price Threshold Type
Day Ahead | 2-4 Hours | 11am – 7pm | $75/MWh | Day-ahead market price
 | 2-4 Hours | 1pm – 9pm | $75/MWh | 
Day Of | 2-4 Hours | 11am – 7pm | $95/MWh | Real time market price
 | 2-4 Hours | 1pm – 9pm | $110/MWh | 

## Slide 7: Confidentiality
A lot of the impacts for PG&E and SCE continue to be confidential.
Redactions are compliant with the 15/15 Rule (PUC § 583 D. 14-05-016)
  Fewer than 15 customers in a group or subgroup
  One customer makes up more than 15% of the total load in a group or subgroup
Information is also redacted if there is only one aggregator in the group or subgroup (General Order 66-C, Section 2.2(b) D.06-06-066)
The purpose of the redactions is to protect customer and/or aggregator confidentiality
SDG&E shows all program level impacts
  This is a result of guidance from SDG&E attorneys concluding that program level impacts are not confidential.

## Slide 8: Ex Post impacts
Program Dispatch and Event Summary
  PG&E: increased in number of events compared to 2017. Many events were focused on individual Sub-LAPs.
  SCE: DA events decreased while DO events are comparable to 2017.
  SDG&E: DA events are comparable while DO events decreased compared to 2017.
Utility | Day Ahead |  |  | Day Of |  | 
 | Number of event days | Hours of Availability | Actual Hours of Use | Number of event days | Hours of Availability | Actual Hours of Use
PG&E | 46 | 180 | 112 | - | - | -
SCE | 37 | 360 | 72 | 48 | 360 | 100
SDG&E | 26 | 144 | 86 | 3 | 144 | 15

## Slide 9: Ex Post impacts
Nomination and Participation
  *Counts shown for summer months May through October
  PG&E: event participation shows the focus on Sub-LAP events; ranging from 1 – 508 participants.
  SCE: event participation ranging 10 – 74 (DA) and 34 – 284 (DO)
  SDG&E: event participation ranging 1 – 66 (DA); DO only called events in August
Utility | Day Ahead |  | Day Of | 
 | Maximum Monthly Nomination Count | Average Event Participation Count | Maximum Monthly Nomination Count | Average Event Participation Count
PG&E | 551 (July) | 197 | - | -
SCE* | 74 (June) | 43 | 284 (August) | 214
SDG&E | 66 (July) | 27 | 199 (July) | 186

## Slide 10: Ex Post impacts
Average Summer Event (HE19)
  On average, only SCE DO aggregate impacts exceeded nominated capacity.
  *Note that the average event day is calculated using all events regardless of participant count and event timing. The results shown are for the common event hour HE19 or 6 PM – 7 PM, which is the hour wherein all events overlap.
Utility | Day Ahead |  |  | Day Of |  | 
 | Aggregate Impact (MW) | Nominated Capacity (MW) | Event Temp (˚F) | Aggregate Impact (MW) | Nominated Capacity (MW) | Event Temp (˚F)
PG&E | 8.8 | 9.2 | 77 |  |  | 
SCE | 2.1 | 3.0 | 81 | 4.9 | 4.5 | 83
SDG&E | 0.2 | 0.3 | 75 | 3.5 | 3.9 | 84
Notes: Data is confidential because of 15/15 rule and/or to protect aggregator confidentiality

## Slide 11: Ex Post Impacts
PG&E – Day Ahead
Average event day:
  1-13 Sub-LAPs
  1-508 Participants
  Events between 2pm and 9 pm
Highest impact achieved occurred during PG&E’s system peak
Second highest impact occurred during CAISO system peak (the hour after)
 | Date & Time | Accounts | Aggregate Impact (MW) | Event Temp (˚F)
Average Event Day | (HE19) | 197 | 8.8 (13%) | 77
Highest Impact & Utility System Peak | 7/25/2018 (HE18) | 508 | 25.2 (25%) | 89
CAISO/Statewide System Peak | 7/25/2018 (HE19) | 508 | 23.2 (23%) | 87
PG&E Day Ahead: Average Event Day

## Slide 12: Ex Post Impacts
SCE – Day Ahead & Day Of
 | Date & Time | Accounts | Aggregate Impact (MW) | Event Temp (˚F)
Day Ahead |  |  |  | 
Average Event Day | (HE19) | 43 | 2.1 (11%) | 81
Highest Impact | 7/6/2018 (HE17) | Confidential |  | 
Utility System Peak | 7/6/2018 (HE16) | Confidential |  | 
CAISO/Statewide System Peak | 7/25/2018 (HE19) | - |  | 
Day Of |  |  |  | 
Average Event Day | (HE19) | 214 | 4.9 (13%) | 83
Highest Impact | 8/7/2018 (HE17) | Confidential |  | 
Utility System Peak | 7/6/2018 (HE16) | Confidential |  | 
CAISO/Statewide System Peak | 7/25/2018 (HE19) | - |  | 
SCE Day Of: Average Event Day
SCE Day Ahead: Average Event Day

## Slide 13: Ex Post Impacts
SDG&E – Day Ahead
DA program experienced a drop in nomination in August (from 66 to 3 participants)
Highest impact achieved in July on HE16
  before nomination drop
  participants are mostly offices/hotels/financial svc
No events were called by SDG&E on HE17 of Aug 9th
 | Date & Time | Accounts | Aggregate Impact (MW) | Event Temp (˚F)
Average Event Day | (HE19) | 27 | 0.2 (3%) | 75
Highest Impact | 7/6/2018 (HE16) | 66 | 1.9 (9%) | 103
Utility System Peak | 8/9/2018 (HE17) | - |  | 
CAISO/Statewide System Peak | 7/25/2018 (HE19) | 66 | 0.1 (1%) | 78
SDG&E Day Ahead: Average Event Day

## Slide 14: Ex Post Impacts
SDG&E – Day Of
DO program only 3 events (all in August)
Achieved consistent responses despite calling events on 3 consecutive days
No events were called by SDG&E on HE17 of Aug 9th
 | Date & Time | Accounts | Aggregate Impact (MW) | Event Temp (˚F)
Average Event Day | (HE19) | 186 | 3.5 (14%) | 84
Highest Impact | 8/7/2018 (HE18) | 186 | 3.9 (16%) | 87
Utility System Peak | 8/9/2018 (HE17) | - |  | 
CAISO/Statewide System Peak | 7/25/2018 (HE19) | - |  | 
SDG&E Day Of: Average Event Day

## Slide 15: Ex Post Impacts
Statewide System Peak Hour – July 25, 2018 (HE18)
  Only PG&E’s and SDG&E’s DA programs called events during the CAISO peak hour
  PG&E’s DA program has the highest impact at 25.2 MW
Utility | Day Ahead |  | Day Of | 
 | Aggregate Impact (MW) | Event Temp (˚F) | Aggregate Impact (MW) | Event Temp (˚F)
PG&E | 25.2 | 89 | - | -
SCE | - | - | - | -
SDG&E | 0.6 | 82 | - | -

## Slide 16: Ex Ante Impacts
Methodology
  Use customer-specific regression models from ex post analysis
    Predict per-customer weather-adjusted reference loads for all subgroups
      Apply Utility and CAISO weather scenarios
    Predict per-customer impacts using most prevalent event hour called for each customer
      Most often HE19 for all three IOUs
      HE18 or HE20 for select customers
  Use enrollment forecasts from IOUs to forecast aggregate impacts
    Enrollment was derived based on
      2018 ex post per-customer impacts
      Contractual MW
      Historical performance

## Slide 17: Ex Ante Impacts
Non-Residential Enrollment Forecast, Month of August
  PG&E forecasts a moderate increase in enrollment in 2019, kept constant through the forecast horizon.
  SCE forecasts a large increase in enrollment for CBP DO and DA beginning in 2018 due to elimination of AMP.
  SDG&E forecasts CBP DA and DO enrollment will increase 3% per year (2019-2022), respectively, due to program improvements, and held constant starting 2022.
Number of Service Accounts |  |  |  |  |  |  | 
Utility | Notice | 2018 | 2019 | 2020 | 2021 | 2022 | 2023-2029 (each year)
PG&E | DA | 551 | 693 |  |  |  | 693
SCE | DA | 74 | 90 |  |  |  | 90
 | DO | 291 | 800 |  |  |  | 800
SDG&E | DA | 63 | 65 | 67 | 69 | 71 | 71
 | DO | 184 | 191 | 197 | 203 | 209 | 209
+3%
+3%
+3%
+3%
+3%
+3%
+25%
+22%
+175%
+3%
+4%
Notes: SDG&E CBP DO values include growth in Technical Incentives (TI) program (7%)

## Slide 18: Ex Ante Impacts
Comparison of current and previous non-residential forecast
  CBP DA
    PG&E increase – decreased enrollment but increased per-customer impacts.
    SCE – no change in enrollment.
    SDG&E decrease – decreased enrollment and per-customer impacts.
  CBP DO
    SCE decreased enrollment.
    SDG&E decrease – increased enrollment but decreased per-customer impacts.
 |  | Previous Forecast, 2019 |  | Current Forecast, 2019 | 
Utility | Notice | Accounts | Aggregate Impact (MW) | Accounts | Aggregate Impact (MW)
PG&E | DA | 700 | 21.0 | 693 | 27.9
SCE | DA | 90 | 6.2 | 90 | Confidential
 | DO | 1,250 | 23.1 | 800 | Confidential
SDG&E | DA | 71 | 0.7 | 65 | 0.2
 | DO | 183 | 3.4 | 191 | 2.7
Results are average event-hour impacts for August peak day in 2018; Utility Peak 1-in-2 weather conditions.

## Slide 19: Ex-Ante Impacts
Residential CBP impact forecast
Due to the expected influx of residential customers
  PG&E: constant 4 MW aggregate load impact through the forecast horizon starting 2019
  SCE: constant 3 MW aggregate load impact through the forecast horizon starting in 2023

## Slide 20: Key Findings
  CBP is now a more time- and/or geographically-targeted DR program, utilizing more localized events
  Each IOU’s product offerings earned mixed results in meeting/exceeding their capacity nominations
    Only SCE DO exceeded capacity nominations, on average at the program level
    PG&E: Elect met/exceeded capacity nominations; Prescribed did not
    SDG&E: DA and DO products operating between 1pm-9pm met/exceeded capacity nominations
  Customer retention from previous years is not as high as expected
    PG&E’s retention of previous DO participants was not as high as projected
    SCE’s retention of previous AMP participants was also not as high as projected
    SDG&E’s DA 11am-7pm may experience a similar retention issue with a mid-year drop in monthly nomination

## Slide 21: Project Contributors
Kelly Marrin
Project Director
kmarrin@appliedenergygroup.com
Abigail Nguyen
Project Manager
anguyen@appliedenergygroup.com
Xijun Zhang
Analyst
xzhang@appliedenergygroup.com
Gil Wong, PG&E
Overall Project Manager
GxWf@pge.com
Lizzette Garcia-Rodriguez, SDG&E
SDG&E Project Manager
LGarcia-Rodriguez@semprautilities.com
Edward Lovelace, SCE
SCE Project Manager
Edward.Lovelace@sce.com
IOU Contributors
AEG Contributors