## Slide 1: Statewide (PG&E and SCE) BIP PY2025 Load impact Evaluation
IOU LIP Workshop - May 5, 2026

## Slide 2: Agenda
PY2025 BIP Program Overview
Ex Post Evaluation Methodology
PY2025 Ex Post Results
Ex Ante Evaluation Methodology
Enrollment Forecasts
PY2026 – 2036 Ex Ante Results
Cross-year comparisons

## Slide 3: py2025 BIP - Base Interruptible Program
Program Overview
Non-Residential Emergency Program (TOU-BIP)
Participants select their FSL (Firm Service Level) and must drop load to their FSL during called events. Customers must commit to reduce at least 15% of their maximum electrical demand (minimum of 100 kW) during each event.
Day-Of Notifications
15 or 30 minute notification options
May occur any time of any day
Year-Round Operation
One event per day (up to six hours)
Up to 10 events per calendar month
Up to 180 hours per calendar year
Compensation
Earn monthly incentive for commitment to reduce load
Penalties given for failure to reduce to FSL during an event
Notes: Note that the FSL is somewhat similar to the ‘nomination’ component in other DR programs, but where nominations are typical an amount of load reduction one commits to (e.g., reducing load by 1MW regardless of current load) however, FSLs are a target amount of load to get to (e.g., regardless of current load, must reach a load of 100 kWh)

## Slide 4: Program Enrollment
Industry Type | PG&E BIP Participants | SCE BIP Participants
Agriculture, Mining and Construction | 66 | 31
Manufacturing | 66 | 203
Office, Hotels, Finance, Services | 7 | 6
Retail Stores | 1 | 1
Schools | 0 | 1
Wholesale, Transport, and other Utilities | 53 | 69
Other/Unknown | 0 | 15
Total | 193 | 326
Program Option | PG&E BIP Participants | SCE BIP Participants
BIP15 | 5 | 49
BIP30 | 188 | 277

## Slide 5: Event Information
IOU | Event Date | Program Options Deployed​ | Event Start and End Times | Event Duration (Hours) | Event Type​ | Customers Dispatched
PG&E | January 22nd | BIP30 | 3:00PM-5:00PM | 2 | Test Event | 6
 | February 12th | BIP30 | 3:00PM-5:00PM | 2 | Re-Test Event | 3
 | September 23rd | BIP15, BIP30 | 4:00PM-6:00PM | 2 | Test Event | 141
 | November 6th | BIP30 | 4:00PM-6:00PM | 2 | Re-test Event | 19
SCE | September 23rd | BIP15, BIP30 | 4:00PM-6:00PM | 2 | Test Event | 326
* Several historically well performing PG&E customers were not tested in any PY2025 event

## Slide 6: PY2025 Ex-Post Analysis

## Slide 7: Ex-Post Methodology Overview
Participant Analysis Perform data QC and weather sensitivity analysis
Proxy Day Selection Select non-event days with event-like conditions to use for model testing
Model Selection Select models based on proxy day prediction performance
Impact Estimation Use selected models to estimate event day baselines and load impacts
1
2
3
4
Hourly Models, Customer-Specific Regression Approach

## Slide 8: Ex-Post Methodology Overview
Hourly Models, Customer-Specific Regression Approach
Participant Analysis Perform data QC and weather sensitivity analysis
Model Selection Select models based on proxy day prediction performance
Impact Estimation Use selected models to estimate event day baselines and load impacts
Proxy Day Selection Select non-event days with event-like conditions to use for model testing
1
2
3
4
Identify which customers should have temperature variables included in their candidate model sets

## Slide 9: Ex-Post Methodology Overview
Hourly Models, Customer-Specific Regression Approach
Participant Analysis Perform data QC and weather sensitivity analysis
Model Selection Select models based on proxy day prediction performance
Impact Estimation Use selected models to estimate event day baselines and load impacts
Proxy Day Selection Select non-event days with event-like conditions to use for model testing
1
2
3
4
Select non-event non-holiday days based on a distance metric to event day temperatures
Select 12 weekdays and 6 weekend proxy days per season, per customer

## Slide 10: Ex-Post Methodology Overview
Hourly Models, Customer-Specific Regression Approach
Participant Analysis Perform data QC and weather sensitivity analysis
Model Selection Select models based on proxy day prediction performance
Impact Estimation Use selected models to estimate event day baselines and load impacts
Proxy Day Selection Select non-event days with event-like conditions to use for model testing
1
2
3
4
Iteratively hold out proxy days to predict load actual load on held out proxy day.
Select one model per customer per season per day type that:
Does not consistently generate significant event impact parameters on non-event
Has realistic coefficient magnitude and direction (e.x., weather coefficients should not be negative)
Minimizes bias and error

## Slide 11: Ex-Post Methodology Overview
Hourly Models, Customer-Specific Regression Approach
Participant Analysis Perform data QC and weather sensitivity analysis
Model Selection Select models based on proxy day prediction performance
Impact Estimation Use selected models to estimate event day baselines and load impacts
Proxy Day Selection Select non-event days with event-like conditions to use for model testing
1
2
3
4
Fit selected models for each hour and predict event day baselines

## Slide 12: Firm Service Level (FSL) Achievement Rate
Observed Impact
Baseline
Observed
FSL
FSL Achievement
Rate
=
Impact at FSL
* Hypothetical event day, not representative
of any PY2025 events or forecasts
Baseline
Observed
FSL
Event window
FSL Achievement Rate = 100% if event load exactly reaches FSL
FSL Achievement Rate = 0% if event load does not differ from baseline
Notes: One major output of our ex post analysis and a key input to the ex ante analysis is the FSL Achievement Rate

## Slide 13: Ex-Post impacts Overview
PG&E Ex-Post Results are Confidential

## Slide 14: Ex-Post impacts Overview
SCE
Event Date (2025) | Num. of Participants Dispatched | Aggregate (MWH/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MW) | FSL Achievement Rate (%)
 |  | Reference Load | Load Impact | Reference Load | Load Impact |  |  | 
September 23rd | 326 | 562.8 | 430.5 | 1,726.4 | 1,320.5 | 76% | 122.1 | 98%

## Slide 15: Ex-Post impacts
SCE 9/23/2025 Event Day, Aggregate Load Shape
Number of dispatched customers: 326
Event Hours: HE 17-18
Aggregate Impact during event: 430.5 MWh/h
Average impact per customer during event: 1,320 kWh/h
FSL Achievement Rate: 98%
Pct. Load Impact: 76%
FSL Achievement Rate = 100% if event load exactly reaches FSL
FSL Achievement Rate = 0% if event load does not differ from baseline

## Slide 16: Distribution of FSL achievement rates
SCE 09/23/2025 event

## Slide 17: PY2025 Ex-Ante Analysis

## Slide 18: Ex-Ante Methodology Overview
Develop Ex-Ante Drivers Includes ex-ante weather scenario data and all assumed event day characteristics (including presumed event hours)
Estimate Ex-Ante Per Capita Reference Loads Predict on the ex-ante drivers data using ex-post models when available
Estimate Ex-Ante Per Capita Impacts Apply historic FSL achievement rates with forecast baselines and updated FSL values
Apply Ex-Ante Forecast Roll together per capita impacts based on participant forecasts
1
2
3
4
Utilize Ex-Post models and FSL Achievement Rates

## Slide 19: Ex-Ante Methodology Overview
Develop Ex-Ante Drivers Includes ex-ante weather scenario data and all assumed event day characteristics (including presumed event hours)
Estimate Ex-Ante Per Capita Reference Loads Predict on the ex-ante drivers data using ex-post models when available
Estimate Ex-Ante Per Capita Impacts Apply historic FSL achievement rates with forecast baselines and updated FSL values
Apply Ex-Ante Forecast Roll together per capita impacts based on participant forecasts
1
2
3
4
Utilize Ex-Post models and FSL Achievement Rates
Assemble all data to use for baseline forecasting
Assume weekday, non-holiday event

## Slide 20: Ex-Ante Methodology Overview
Develop Ex-Ante Drivers Includes ex-ante weather scenario data and all assumed event day characteristics (including presumed event hours)
Estimate Ex-Ante Per Capita Reference Loads Predict on the ex-ante drivers data using ex-post models when available
Estimate Ex-Ante Per Capita Impacts Apply historic FSL achievement rates with forecast baselines and updated FSL values
Apply Ex-Ante Forecast Roll together per capita impacts based on participant forecasts
1
2
3
4
Utilize Ex-Post models and FSL Achievement Rates
Use ex-post models and ex-ante drivers to forecast weather adjusted ex-ante reference loads
Select additional models for new customers / for conditions where did not have an ex-post model
Validate reference loads by comparing to historic load shapes

## Slide 21: Ex-Ante Methodology Overview
Develop Ex-Ante Drivers Includes ex-ante weather scenario data and all assumed event day characteristics (including presumed event hours)
Estimate Ex-Ante Per Capita Reference Loads Predict on the ex-ante drivers data using ex-post models when available
Estimate Ex-Ante Per Capita Impacts Apply historic FSL achievement rates with forecast baselines and updated FSL values
Apply Ex-Ante Forecast Roll together per capita impacts based on participant forecasts
1
2
3
4
Utilize Ex-Post models and FSL Achievement Rates
Compute typical FSL achievement rates, utilizing historical performance where relevant
Multiply FSL achievement rates by the expected impacts at full FSL achievement to estimate impacts for one hour before presumed event through end of day

## Slide 22: Ex-Ante Methodology Overview
Develop Ex-Ante Drivers Includes ex-ante weather scenario data and all assumed event day characteristics (including presumed event hours)
Estimate Ex-Ante Per Capita Reference Loads Predict on the ex-ante drivers data using ex-post models when available
Estimate Ex-Ante Per Capita Impacts Apply historic FSL achievement rates with forecast baselines and updated FSL values
Apply Ex-Ante Forecast Roll together per capita impacts based on participant forecasts
1
2
3
4
Utilize Ex-Post models and FSL Achievement Rates
Apply participant forecasts to estimated impacts
To compute portfolio-level impacts, FSL achievement rates are capped at 100% for customers dual enrolled in ELRP (through program sunset in 2027)

## Slide 23: Ex-Ante Methodology
Assumed Event Duration
Event Assumptions
4-Hour
Assumed Event Hours
Weather Scenarios Modeled
First four hours of the RA Window
Includes 2027 Peak Hours
November through May:
HE 18-21
June through October:
HE 17-20
PG&E
SCE
4-Hour
6-Hour
Consistent across year
Includes 2027 Peak Hours
Four Hour Event:
HE 18-21
Six Hour Event:
HE 17-22
CAISO and Utility-specific weather scenarios
1-in-2 and 1-in-10
Monthly System Worst Day
CAISO and Utility-specific weather scenarios
1-in-2 and 1-in-10
Monthly System Worst Day
Notes: Assumed weekday non-holiday

## Slide 24: Enrollment Forecasts
PG&E
Does not differentiate between BIP15 and BIP30
Note: Participant counts are labeled for August of each year. Background color alternates by calendar year.
Notes: We see that PG&E is anticipating a growth in participation through the forecast horizon due to increased marketing and outreach efforts

## Slide 25: Ex-Ante Impacts Overview
PG&E August Monthly System Worst Day 2026 – Average over 4-hour event
Program
Weather Source | Weather Year | Event Dispatch (HE) | Number of Participants | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
CAISO | 1-in-10 | 17 - 20 | 204 | 217.3 | 168.3 | 1,065.0 | 825.0 | 77% | 58.2 | 106%
CAISO | 1-in-2 | 17 - 20 | 204 | 216.6 | 167.4 | 1,061.7 | 820.7 | 77% | 58.2 | 106%
Utility | 1-in-10 | 17 - 20 | 204 | 217.3 | 168.4 | 1,065.4 | 825.3 | 77% | 58.2 | 106%
Utility | 1-in-2 | 17 - 20 | 204 | 215.9 | 166.7 | 1,058.4 | 816.9 | 77% | 58.2 | 106%
Portfolio
Weather Source | Weather Year | Event Dispatch (HE) | Number of Participants | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
CAISO | 1-in-10 | 17 - 20 | 204 | 217.3 | 164.9 | 1,065.0 | 808.2 | 76% | 58.2 | 104%
CAISO | 1-in-2 | 17 - 20 | 204 | 216.6 | 164.2 | 1,061.7 | 804.8 | 76% | 58.2 | 104%
Utility | 1-in-10 | 17 - 20 | 204 | 217.3 | 165.0 | 1,065.4 | 809.0 | 76% | 58.2 | 104%
Utility | 1-in-2 | 17 - 20 | 204 | 215.9 | 163.5 | 1,058.4 | 801.5 | 76% | 58.2 | 104%

## Slide 26: Ex-Ante Load Shape
PG&E Program-level August 1-in-2 Monthly System Worst Day, 2026

## Slide 27: Ex-Ante Impacts Slice of Day Table
PG&E Program 1-in-2 System Worst Day 2026, Aggregate Hourly Impact (MWh/h)
Hour Ending | Jan. | Feb. | Mar. | Apr. | May | June | July | Aug. | Sept. | Oct. | Nov. | Dec.
16 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 108.1 | 104.5 | 105.3 | 106.4 | 103.1 | 0.0 | 0.0
17 | 92.1 | 98.3 | 94.7 | 110.2 | 111.2 | 167.9 | 164.8 | 167.0 | 171.8 | 163.1 | 98.3 | 90.2
18 | 167.6 | 176.5 | 164.2 | 186.6 | 182.4 | 164.6 | 159.7 | 162.4 | 171.8 | 160.3 | 177.5 | 167.8
19 | 161.5 | 171.9 | 163.8 | 186.4 | 186.4 | 167.7 | 163.9 | 167.4 | 178.2 | 160.1 | 172.4 | 165.3
20 | 159.0 | 169.6 | 165.4 | 189.8 | 190.4 | 171.0 | 166.9 | 169.8 | 177.3 | 154.0 | 171.0 | 164.5
21 | 157.9 | 167.5 | 163.2 | 189.1 | 190.6 | 112.6 | 113.2 | 113.6 | 113.9 | 102.7 | 170.8 | 163.8
22 | 112.4 | 118.5 | 115.8 | 123.8 | 124.9 | 67.2 | 65.0 | 63.7 | 65.0 | 59.7 | 116.8 | 112.0
23 | 65.5 | 69.9 | 65.8 | 70.4 | 70.2 | 58.7 | 56.9 | 55.3 | 56.0 | 51.7 | 65.1 | 64.3
24 | 57.5 | 59.7 | 56.9 | 60.0 | 61.1 | 55.5 | 52.9 | 52.0 | 51.8 | 47.7 | 56.2 | 53.8
Event hour in RA window
Non-event hour in RA window
Event Hour, 2027 CEC Peak Hour

## Slide 28: Ex-Ante Impacts Slice of Day Table
PG&E Program 1-in-2 System Worst Day 2027, Aggregate Hourly Impact (MWh/h)
Hour Ending | Jan. | Feb. | Mar. | Apr. | May | June | July | Aug. | Sept. | Oct. | Nov. | Dec.
16 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 111.4 | 107.9 | 109.5 | 110.8 | 107.3 | 0.0 | 0.0
17 | 93.4 | 100.7 | 97.6 | 113.8 | 114.6 | 173.4 | 170.3 | 174.1 | 179.2 | 170.3 | 98.0 | 91.3
18 | 169.8 | 180.3 | 169.3 | 192.8 | 187.9 | 169.8 | 164.7 | 169.2 | 179.0 | 167.3 | 177.5 | 170.6
19 | 163.7 | 175.4 | 168.6 | 192.3 | 191.6 | 172.8 | 168.9 | 174.2 | 185.4 | 167.1 | 171.9 | 168.2
20 | 161.2 | 173.1 | 170.5 | 195.8 | 195.5 | 176.2 | 172.1 | 176.7 | 184.5 | 160.8 | 171.6 | 169.4
21 | 160.0 | 170.9 | 168.1 | 195.0 | 195.6 | 115.8 | 116.4 | 118.0 | 118.5 | 107.2 | 171.1 | 168.1
22 | 113.9 | 120.9 | 119.1 | 127.6 | 127.9 | 68.9 | 66.7 | 65.6 | 66.9 | 61.7 | 111.8 | 111.8
23 | 66.4 | 71.3 | 67.5 | 72.4 | 71.8 | 60.1 | 58.4 | 56.8 | 57.5 | 53.4 | 57.9 | 59.7
24 | 58.2 | 61.1 | 58.4 | 61.6 | 62.5 | 56.6 | 54.0 | 53.2 | 53.1 | 49.2 | 46.9 | 47.2
Event hour in RA window
Non-event hour in RA window
Event Hour, 2027 CEC Peak Hour

## Slide 29: Ex-Ante Impacts Across the Forecast period
PG&E Program-level August Monthly System Worst Day
Max 251.3
Min 166.7

## Slide 30: Enrollment Forecasts
SCE
Participant forecast is the same across all years.
  50 BIP15
  279 BIP30
Note: Participant counts are labeled for August of each year. Background color alternates by calendar year.

## Slide 31: Ex-Ante Impacts Overview
SCE August Monthly System Worst Day 2026 – Average over 4-hour event
Program
Weather Source | Weather Year | Event Dispatch (HE) | Number of Participants | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
CAISO | 1-in-10 | 18 - 21 | 329 | 597.9 | 457.4 | 1,817.2 | 1,390.3 | 77% | 125.8 | 97%
CAISO | 1-in-2 | 18 - 21 | 329 | 596.4 | 456.1 | 1,812.9 | 1,386.4 | 76% | 125.8 | 97%
Utility | 1-in-10 | 18 - 21 | 329 | 597.7 | 457.3 | 1,816.8 | 1,389.8 | 76% | 125.8 | 97%
Utility | 1-in-2 | 18 - 21 | 329 | 597.3 | 456.9 | 1,815.4 | 1,388.7 | 76% | 125.8 | 97%
Portfolio
Weather Source | Weather Year | Event Dispatch (HE) | Number of Participants | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
CAISO | 1-in-10 | 18 - 21 | 329 | 597.9 | 453.9 | 1,817.2 | 1,379.5 | 76% | 125.8 | 96%
CAISO | 1-in-2 | 18 - 21 | 329 | 596.4 | 452.6 | 1,812.9 | 1,375.7 | 76% | 125.8 | 96%
Utility | 1-in-10 | 18 - 21 | 329 | 597.7 | 453.7 | 1,816.8 | 1,379.1 | 76% | 125.8 | 96%
Utility | 1-in-2 | 18 - 21 | 329 | 597.3 | 453.3 | 1,815.4 | 1,377.9 | 76% | 125.8 | 96%

## Slide 32: Ex-Ante Load Shape
SCE Program-level August 1-in-2 Monthly System Worst Day, 2026 through 2036

## Slide 33: Ex-Ante Impacts Slice of Day Table
SCE Program 1-in-2 System Worst Day 2026 to 2036, Aggregate Hourly Impact (MWh/h)
Hour Ending | Jan. | Feb. | Mar. | Apr. | May | June | July | Aug. | Sept. | Oct. | Nov. | Dec.
16 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
17 | 229.2 | 238.2 | 261.6 | 242.5 | 258.1 | 254.9 | 258.1 | 254.5 | 254.6 | 263.7 | 239.7 | 212.8
18 | 420.2 | 434.5 | 473.9 | 448.5 | 468.8 | 464.3 | 468.9 | 455.3 | 459.5 | 470.4 | 433.5 | 385.7
19 | 414.0 | 431.6 | 473.8 | 448.6 | 466.4 | 460.7 | 466.2 | 454.4 | 458.5 | 470.5 | 424.5 | 380.8
20 | 412.6 | 430.0 | 466.5 | 452.4 | 470.7 | 461.4 | 471.0 | 458.2 | 457.3 | 470.6 | 419.2 | 378.4
21 | 412.9 | 433.3 | 470.0 | 459.9 | 474.0 | 466.8 | 474.0 | 459.6 | 459.0 | 471.6 | 421.1 | 380.2
22 | 298.2 | 313.6 | 333.1 | 331.4 | 336.2 | 334.1 | 343.1 | 337.9 | 337.6 | 342.1 | 308.6 | 285.9
23 | 158.4 | 169.4 | 163.1 | 169.0 | 174.9 | 174.8 | 177.5 | 176.9 | 174.4 | 182.0 | 164.0 | 154.9
24 | 109.1 | 116.8 | 112.3 | 118.1 | 123.6 | 125.4 | 125.7 | 125.1 | 121.3 | 129.4 | 113.7 | 105.3
Event hour in RA window
Non-event hour in RA window
Event Hour, 2027 CEC Peak Hour

## Slide 34: Comparison of PY2025 and Prior Year results

## Slide 35: Previous Versus Current Ex-Post
Reminder that PY2024 impacts showed an improvement relative to PY2022 impact levels for per capita impacts and FSL achievement rates
  PY2023 was only a single, 5-minute event
Aggregate impacts were lower in PY2024 than in PY2022 due to reduced program enrollment
Customers who were tested in the main September event in both PY2024 and PY2025 showed statistically indistinguishable event day impacts.
* 2022 Load Impact Evaluation of California Statewide Base Interruptible Programs (BIP) for Non-Residential Customers: Ex-post and Ex-ante Report
** 2023 Load Impact Evaluation of California Statewide Base Interruptible Programs (BIP) for Non-Residential Customers: Ex-post and Ex-ante Report
Evaluation Year | Estimate Type | Number of Participants per Event | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
2022* | Sept. 6th | 258 | 203 | 149 | 787 | 577 | 73% | 51 | 98%
2023** | Avg. Event Day | 214 | 164 | 36 | 766 | 168 | 22% | 48 | 31%
2024 | Sept. 24th | 163 | 145 | 99 | 888 | 608 | 68% | 46 | 100%
2025 | Sept. 23rd | 141 | XXX | XXX | XXX | XXX | XXX | XXX | XXX
PG&E Ex-Post Results are confidential

## Slide 36: Previous Ex-Ante Versus Current Ex-Post
PY2025 ex-post impacts were lower than anticipated in the PY2024 forecast because several historically high performing customers were not re-tested in any PY2025 event
*Ex-ante estimates are based on program-level 1-in-2 utility-specific weather scenario
Evaluation Year | Estimate Type | Number of Participants per Event | Aggregate* (MWh/h) |  | Per Capita* (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
2024 | Ex-ante for 2025 | 173 | 187 | 132 | 1,079 | 765 | 71% | 55 | 101%
2025 | Ex-post Sept. 23rd | XXX | XXX | XXX | XXX | XXX | XXX | XXX | XXX
PG&E Ex-Post Results are confidential

## Slide 37: Previous Versus Current Ex-Ante
Aggregate impacts are forecasted to be 29 MW higher in PY2026 than previously anticipated
  The PY2025 participant forecasts include an increase in BIP enrollment for PY2026, based on observed enrollment patterns and increased marketing efforts.
Per capita impacts are forecast to be 57 kWh/h higher in PY2026 than previously anticipated
  This increase is largely driven by higher forecasted FSL achievement rates
*Ex-ante estimates are based on program-level 1-in-2 utility-specific weather scenario
Evaluation Year | Estimate Type | Number of Participants per Event | Aggregate* (MWh/h) |  | Per Capita* (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
2024 | Ex-ante for 2026 | 182 | 194 | 138 | 1,068 | 760 | 71% | 57 | 100%
2025 | Ex-ante for 2026 | 204 | 216 | 167 | 1,058 | 817 | 77% | 58 | 106%
PG&E

## Slide 38: Previous Versus Current Ex-Post
PY2025 aggregate impacts were 34 MWh/h higher than in PY2024
  The PY2025 event dispatched 12 more customers than the PY2024 event
Per capita load impacts in PY2025 were 58 kWh/h higher in PY2025 than in PY2024
  This difference is within 95% confidence intervals for these estimates
  While FSL achievement rates were lower in PY2025, FSL commitments were also substantially lower, leading to overall similar per capita impacts
Evaluation Year | Estimate Type | Number of Participants per Event | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
2024 | Sept. 24th | 314 | 536 | 396 | 1,705 | 1,262 | 74% | 146 | 102%
2025 | Sept. 23rd | 326 | 563 | 430 | 1,726 | 1,320 | 76% | 122 | 98%
SCE

## Slide 39: Previous Versus Current Ex-Post
SCE
Customers that were tested in the main test event in both PY2024 and PY2025 showed consistently strong performance on average

## Slide 40: Previous Ex-Ante Versus Current Ex-Post
The 53 kWh/h difference between ex-ante and ex-post per capita load impacts is within the typical uncertainty range for these estimates.
The 11MW difference between the forecast and realized aggregate load impacts are also statistically indistinguishable.
Evaluation Year | Estimate Type | Number of Participants per Event | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
2024 | Ex-ante for 2025 | 331 | 581 | 419 | 1,754 | 1,267 | 72% | 140 | 95%
2025 | Ex-post Sept. 23 | 326 | 563 | 430 | 1,726 | 1,320 | 76% | 122 | 98%
SCE
*Ex-ante estimates are based on program-level 1-in-2 utility-specific weather scenario

## Slide 41: Previous Versus Current Ex-Ante
Several factors contribute to the increase in forecasted impacts from PY2024 to PY2025.
  Higher Proportion of BIP15 Customers : The PY2025 forecast includes an additional two BIP15 customers relative to the PY2024 forecast. SCE BIP15 customers are expected to deliver significantly higher impacts than a typical BIP30 customer.
  Enrollment of New Large Customers/De-enrollment of Small Customers: At the end of PY2025, several new high baseline customers enrolled in the SCE BIP program, while several smaller baseline (and, thus, impact) customers de-enrolled.
  Commitments to Larger Load Reductions: The aggregate FSL for customers in the PY2025 forecast is 14MW lower than in the PY2024 forecast due to updated enrollments, de-enrollments, and FSL changes. This commitment to larger load reduction, in addition to the marginally higher forecast FSL achievement rate, is a major contributor to the increase in forecast impacts.
Evaluation Year | Estimate Type | Number of Participants per Event | Aggregate (MWh/h) |  | Per Capita (kWh/h) |  | Percent Load Reduction (%) | FSL (MWh/h) | FSL Achievement Rate (%)
 |  |  | Ref. Load | Load Impact | Ref. Load | Load Impact |  |  | 
2024 | Ex-ante for 2026 | 331 | 581 | 419 | 1,754 | 1,267 | 72% | 140 | 95%
2025 | Ex-ante for 2026 | 329 | 597 | 457 | 1, 815 | 1,389 | 76% | 126 | 97%
SCE
*Ex-ante estimates are based on program-level 1-in-2 utility-specific weather scenario

## Slide 42: Final Takeaways
Ex-Post
Cross-Year
Comparisons
Ex-Ante
PY2025 ex-post load impacts are confidential.
PG&E’s BIP is anticipated to provide an average hourly load reduction of between 166.7 MWh/h to 168.3 MWh/h during a four-hour dispatch of all customers in August 2026.
PY2025 forecast impacts for PY2026 exceed those from the PY2024 evaluation due to a combination of increased forecasted enrollment, lower average FSLs, and strong customer performance.
All 326 active BIP customers were dispatched for a test event on September 23rd. On average these customers provided 430 MWh/h of load reductions during event hours with an FSL achievement rate of 98%.
SCE’s BIP is anticipated to provide an average hourly load reduction of between 456.1 MWh/h to 457.4 MWh/h during a four-hour dispatch of all customers in August 2026.
Aggregate impacts in PY2026 are forecast to increase somewhat relative to the PY2025 ex-post event. However, these differences are within the error bounds for these estimates.
PG&E
SCE