## Slide 1: Load Impact Evaluation: PG&E’s Automated Response Technology (ART) Program
Xueting (Sherry) Wang
Michael Vigdor
Corey Goodrich
Mike Clark
DRMEC Spring Workshop
May 6, 2026

## Slide 2: Agenda:
Program Description
Ex-Post Analysis
Ex-Ante Analysis
Load Impact Reconciliation
Key Findings

## Slide 3
ART Program Description
The ART program is a voluntary residential demand response program for customers with smart home technologies such as
  Smart Communicating Thermostats (SCTs), Heat Pump Water Heaters (HPWH), Electric Vehicle (EV) chargers, Battery Storage (Battery)
Customers enroll in ART through a PG&E-contracted Provider.
  In PY2025, there is only one Provider, so all ex-post results are confidential.
PG&E
Pay for
Third-Party Providers
Dispatch Smart
Customers
Performance
Technologies

## Slide 4
ART Program Description (2)
By the end of PY2025 (October 2025), the only technology dispatched is smart thermostat, and many customers were transitioned from the Smart Thermostat Control Pilot (BYOT).
ART events may be called year-round for all hours and seven days a week for the following reasons:
  CAISO market award dispatch
  PG&E system emergencies or near-emergencies for distribution service
  Test event for the purpose of calculating incentive payments for third-party providers
Smart Thermostat Control Pilot 2022-2023
Official Launch of ART Sep 18, 2024
PY2025
Nov 2024 – Oct 2025

## Slide 5
ART Program Description (3)
A Daily Load-Shifting (DLS) strategy is required for customers on a time-varying rate, using the automated technology to adjust electricity use during the hours with time-varying rates.
  ART customers may opt out of the DLS strategy after 12 months.
  Many ART customers already had DLS implemented during the Smart Thermostat Control Pilot.
  DLS may have continued after the conclusion of the Pilot.

## Slide 6
ART PY2025 Participation
Participation Counts by Billing Rate

## Slide 7
Ex-Post Methodology – Event Day
Matched Control Group + Difference-in-Differences
Event-Like Non-Event Days
Select days that are the closest to the average temperatures of the event days
Separate matches for summer and non-summer months
Control pool: a sample of ~150,000 customers
Propensity score matching:
  Within the same sub-LAP and NEM status
  Match on load profiles on event-like non-event days, weather sensitivity, solar installation size, and battery storage
Control Group Matching
Difference-in-Differences
Intuitively, load impacts are the difference between the following:
  Event day loads between ART and control customers
  Non-event day loads between ART and control customers

## Slide 8
Ex-Post Load Impacts – Event Day
Date | Type of Event | Event Hours (p.m.) | Sub-Lap Dispatched | # Dis-patched | Avg. Temp (°F)
11/22/24 | Test | 5 - 6 | All | 16,852 | 59.7
12/20/24 | Test | 5 - 6 | All | 18,705 | 50.5
1/23/25 | Test | 4 - 5 | All | 18,704 | 65.0
2/26/25 | Test | 3 - 4 | All | 18,694 | 72.6
3/26/25 | Test | 6 - 8 | All | 19,001 | 60.3
4/20/25 | Test | 7 - 8 | All | 20,000 | 65.0
5/21/25 | Test | 7 - 8 | All | 21,212 | 71.3
6/26/25 | Test | 6 - 8 | All | 23,326 | 73.8
7/11/25 | Market Award | 4 - 6 | PGEB, PGF1, PGKN, PGNB, PGNP, PGP2, PGSB, PGSI, PGST, PGZP | 25,067 | 89.2
7/29/25 | Test | 4 - 6 | PGCC, PGHB, PGFG, PGNC, PGSF | 1,750 | 71.2
8/22/25 | Test & Market Award | 4 - 6 | All | 33,474 | 88.8
9/17/25 | Market Award | 4 - 6 | PGEB, PGF1, PGFG, PGKN, PGNB, PGNP, PGP2, PGSB, PGSI, PGST, PGZP | 36,648 | 90.2
9/23/25 | Test | 4 - 6 | PGHB, PGNC, PGSF, PGCC | 1,174 | 83.7
10/29/25 | Test | 4 - 6 | All | 41,872 | 77.7

## Slide 9
Ex-Post Load Impacts – August 22nd Event
The average temperature during the event was 88.8°F.
We observe statistically significant load reductions for most sub-LAPs.
We observe an increase in loads before and after the event hour, similar to the “pre-cooling” and “post-event snapback” observed in the Smart Thermostat Control Pilot study.
Customers on E-TOU-C rate (largest share of customers) had lower load reduction than customers on E-1 rate (non-TOU).
4-6 p.m.
Reference loads without Event
Illustrative Impacts on August 22nd

## Slide 10
Ex-Post Methodology – Daily Load-Shifting
Matched Control Group + Simple Difference
Mahalanobis distance matching:
  Within the same billing rate, NEM status, Battery and EV ownership
  Match on average monthly usage, average cooling and heating degree days, solar and battery installation size
  Separate matches for summer and non-summer months
Control Group Matching
Intuitively, load-shifting impacts are the difference between:
  Average loads between ART and control customers
We assume that there are no changes in overall consumption.
Simple Difference

## Slide 11
Ex-Post Load Impacts – Daily Load Shifting (August)
DLS strategy produced statistically significant load reductions during the TOU peak period for August average weekday.
There are increases in loads during early and late hours of the day.
Ecobee has the highest per-customer impacts across device manufacturers.
Rate E-TOU-D has the highest statistically significant per-customer impacts.
Rate E-TOU-C has the largest aggregate impacts.
5-8 p.m.
Reference loads without DLS
Illustrative Impacts on August 22nd

## Slide 12
Ex-Post Load Impacts – Combining the Two Impacts
For customers on TOU rates, on ART event days, both DLS and the event occurred.
To estimate both effects, we estimated the incremental DLS impacts on the event days using weather and parameters from the DLS regression model.
4-6 p.m.
Reference loads without DLS and Event
Illustrative Impacts on August 22nd

## Slide 13
Ex-Ante Methodology – Overview
Enrollment Forecast
Provided by PG&E
By technology
Per-Customer Reference Loads
Estimated based on interval data of existing customers
By sub-LAP
Per-Customer Load Impacts
By technology
Assumptions of load impacts based on the ex-post results or other studies.
By sub-Lap

## Slide 14
Ex-Ante Methodology – Develop Load Impacts
Technology | Assumed Impact | Adjustments
SCT | Observed impacts from PY2025 ex-post are used as the basis for ex-ante impacts | None.
Battery | During the assumed four-hour event, one-fourth of the battery’s total derated capacity is discharged in each hour. Battery capacity is assumed to be discharged evenly across all event hours. | Reference loads are based on loads of all battery customers, utilizing both controls and treatments in order to boost sample size.
 |  | A total derating of 25% is applied to batteries, consisting of a 5% adjustment to usable capacity and a 20% adjustment to reflect the recommended depth of discharge.
 |  | The distribution of battery capacities within the population is applied to the reference load to estimate delivered load impacts.
 |  | Load impacts are capped at the estimated reference load.
EV | 0.35 kWh/customer/hour | None.
HPWH | 0.05 kWh/customer/hour | None.
CEC Flex App | 0.05 kWh/customer/hour | None.

## Slide 15
Ex-Ante Per-Customer Load Impacts
Technology | Per-Customer Load Impacts
SCT | Confidential
Battery | 0.43 – 1 kWh/customer/hour
EV | 0.35 kWh/customer/hour
HPWH | 0.05 kWh/customer/hour
CEC Flex App | 0.05 kWh/customer/hour
RA Window Per-Customer Load Impacts,
PG&E 1-in-2 System Worst Days in 2026

## Slide 16: Enrollment Forecast – by Technology Type
Technology | 2026 | 2036
SCT | 86.6% | 68.6%
EV Charger | 4.0% | 18.5%
Battery | 2.1% | 2.6%
HPWH | 0.4% | 1.8%
CEC | 7.0% | 8.5%

## Slide 17: Ex-Ante Load Impacts – All Technologies
RA Window, PG&E 1-in-2 August System Worst Day
(2026-2036)
Year | # Enrolled | Per Customer |  | Aggregate | 
 |  | Event Load Impact (kWh/cust/hr) | Event Ref. Load (kWh/cust/hr) | Event Load Impact (MWh/hr) | Event Ref. Load (MWh/hr)
2026 | 75,299 | 0.45 | 1.89 | 33.67 | 142.66
2027 | 103,956 | 0.43 | 1.89 | 44.99 | 196.98
2028 | 129,081 | 0.43 | 1.89 | 55.00 | 244.57
2029 | 151,049 | 0.42 | 1.89 | 63.72 | 286.07
2030 | 171,302 | 0.42 | 1.89 | 71.81 | 324.39
2031 | 191,225 | 0.42 | 1.89 | 79.88 | 362.02
2032 | 210,812 | 0.42 | 1.89 | 87.91 | 399.02
2033 | 230,232 | 0.42 | 1.89 | 95.94 | 435.70
2034 | 249,272 | 0.42 | 1.89 | 103.97 | 471.63
2035 | 268,134 | 0.42 | 1.89 | 111.97 | 507.21
2036 | 286,818 | 0.42 | 1.89 | 119.97 | 542.48

## Slide 18: Ex-Ante Load Impacts – Hourly Load Impacts
Aggregate Hourly Loads and Load Impacts,
PG&E 1-in-2 August System Worst Day in 2026

## Slide 19: Ex-Ante Load Impacts – by LCA
RA Window Load Impacts by LCA,
PG&E 1-in-2 August System Worst Day in 2026

## Slide 20: Reconciliation
Current Ex-Post (October) vs Previous Ex-Post (October)
  Load impacts increased marginally in PY2025.
Current Ex-Ante vs Previous Ex-Ante
  For the August 2026 1-in-2 event, average level hourly load impacts are very similar year over year. Percentage load impacts decrease slightly due to increased estimated loads.
Current Ex-Post vs Previous Ex-Ante
  Confidential results
Current Ex-Post vs Current Ex-Ante
  Confidential results

## Slide 21
Key Findings and Recommendations
Ex-Post Load Impacts:
  Load impacts are largest during summer event hours, with diminishing responsiveness in shoulder months.
  DLS strategy produced statistically significant load reductions during the peak period, particularly for the summer months, for customers on TOU rates.
Ex-Ante Load Impacts:
  Increased enrollments lead to significant growth of aggregate load impacts over the forecast window from 2026-2036.
  Changing technology mix lowers per-customer impacts slightly.
Going Forward:
  We recommend calling events across sub-LAPs and varying weather conditions to help understand how performance varies by location and weather for each technology type.
  We also recommend scheduling shoulder-month events at different points within the month to assess how behavioral responses evolve.

## Slide 22: Questions?
Contact
Sherry Wang: swang@caenergy.com
608-216-7110
Corey Goodrich: crgoodrich@caenergy.com
608-216-7146
Christensen Associates Energy Consulting Madison, Wisconsin