## Slide 1: Load Impact Evaluation: SCE Demand Response Aggregator Contracts
Dan Hansen and Corey Goodrich
May 2026

## Slide 2: Presentation Outline
Resource Description
Ex-post Methodology
Ex-post Load Impacts
Ex-ante Methodology
Ex-ante Load Impacts

## Slide 3: 1. Resource Description
Two Demand Response Aggregators (DRAs) had active contracts during the 2025 program year:
  Hybrid Electric Building Technologies (Hybrid)
  Stem Energy (Stem)
Hybrid and Stem enrolled commercial and industrial customers to provide demand response within SCE’s service territory
  DRAs nominate customers on a monthly basis
  SCE dispatched the contracts according to the associated terms
  DRA is responsible for meeting the contract obligations

## Slide 4: 2. Ex-post Methodology
Estimated customer-specific regression models with the customer’s hourly usage as the dependent variable
Two models are used to simulate reference loads that would have occurred in the absence of events, one for weekday events and another for weekend events
The explanatory variables include:
  Temperatures, expressed in several ways (e.g., current hour, average daily, maximum daily)
  Irradiance
  Holiday and near holiday (only in weekend model)
  Hour of day
  Day of week
  Month of year
  A morning load variable (average load from midnight to 10 a.m., except for customers with early event hours)

## Slide 5: 2. Ex-post Methodology (2)
October 2024 through September 2025 data included in the model
  Exclude event hours plus at least 3 hours following the event
    If the event starts at 5 p.m. or later, the rest of the day is excluded
    Needed to include some event-day data to improve estimates for contracts with a high frequency of events
  Exclude data prior to the customer’s first nominated month, which ensures that storage is in place (if applicable)
Model validation
  Estimated a common specification excluding ~15% of the data (randomly selected non-event days)
  Compared predicted and observed values on withheld days and adjusted the customer’s regression specification as needed
Estimated load impact = the model’s predicted load for the event hour minus the observed load

## Slide 6: 3. Ex-post Results
Due to confidentiality (only two DRAs), we are unable to report ex-post load impacts

## Slide 7: 4. Ex-ante Methodology
SCE provided a forecast of monthly capacity commitments by contract
  Replaces the enrollment forecast typically used in a load impact study
Simulate customer-specific reference loads for all required scenarios (by month and weather scenario)
  Same as ex-post weekday regression model but omitting the morning load and irradiance variables
  Ex-ante results include only 1-in-2 weather scenarios

## Slide 8: 4. Ex-ante Methodology (2)
Ex-ante load impacts are a straightforward translation of the ex-post estimates
  No weather effect on load impacts, so no statistical modeling is needed
  Use average impacts across four-hour events from HE17-20 or HE18-21
  Hourly forecast impacts are built up from contract-level estimates
Forecast contract quantities matched ex-post contract quantities, so no adjustment was needed for that
Contracts have a maximum four-hour event duration, whereas the Resource Adequacy window is five hours long
  Average RA-window impacts are calculated only over the four called hours
  Simulate HE17-20 events from June-October and HE18-21 for other months

## Slide 9: 5. Ex-ante Load Impacts Comparison of PY2024 to PY2025 forecasts for Aug. 2026
There was a small change in methodology this program year
  The August RA window is now HE 17-20, whereas it was HE 18-21 in the previous program year’s forecast
While the contract achievement percentage is slightly lower in the current study, the MW load impact (not shown due to confidentiality) is slightly higher.

## Slide 10: Questions?
Contact
Dan Hansen Christensen Associates Energy Consulting Madison, Wisconsin
  dghansen@CAEnergy.com
  (608)231-2266