## Slide 1: Group D Evaluations
California Public Utilities Commission – Energy Division
April 2025

## Slide 2: SEM PY2023 Evaluation
CPUC Lead: Lisa Paulo
Ismail Omar
Project Manager

## Slide 3: Study team
Ismail Omar
David Bluestein
NTG Lead
Project Manager
Chad Telarico
Project Sponsor
Susan Haselhorst
SME
CPUC:
Lisa Paulo, Study Manager, Group D Contract Manager Leanne Hoadley, ED Planning and Forecasting Supervisor
DNV:
Ismail Omer Chad Telarico Kaylee Schrickel Susan Haselhorst Amit Kanungo
Guidehouse:
David Bluestein

## Slide 4: Agenda
01 | Background and research objectives
02 | Methodology
03 | Findings
04 | Conclusions and recommendations
05 | Questions

## Slide 5: Background and research questions
01

## Slide 6: Study background
The PY2023 SEM Impact Evaluation:
  Is the third impact evaluation conducted by the CPUC since the program began in 2018
  Includes SEM projects that completed a full 2-year cycle in program year PY2023
  Will account for the savings claims from the first year of the cycle reported in 2022 or earlier
  Represents the first half of a 2-year evaluation cycle
  Includes MCE, SCE, and SCG
Results from this study will be combined with PY2024 results to produce an update to program gross realization rate (GRR) and net-to-gross ratios (NTGRs).
  Will include PG&E and SDG&E
Main study purpose
Develop first-year and lifecycle evaluated net and gross savings for the SEM program.
Develop meaningful and actionable recommendations to improve program performance in delivering energy efficiency savings.

## Slide 7: Research questions
What are the SEM annual and lifecycle GRR and kWh, peak kW, and therms savings? | What factors are driving the GRR? | How can realization rates be improved?
Are there any gaps in the planned EM&V activities for SEM programs? | What are the recommended changes to the SEM M&V guide and SEM program design? | What is the SEM NTGR?
What factors are driving free-ridership and support the SEM NTGR? | How well does the SEM program adhere to the SEM design and SEM M&V guides? | What are the remaining or new primary challenges, lessons learned, and potential best practices for key program components and related research questions?

## Slide 8: Methodology
02

## Slide 9: Summary of gross methods
Sample confidence and precision target of 90/14 at the statewide level for PY2023 (Part 1)
  90/10 when combined with PY2024 in next year’s report (Part 2)
Reviewed 13 gross sample points:
  8 electric and 6 gas (1 site had both)
Evaluation approach varies based on applicant savings approach.
  Top-down model: model validation
  Bottom-up calculation: M&V of the energy improvements with the appropriate level of rigor
Gross evaluation process:
  Custom core template (CCT) and M&V plans developed for each gross impact sampled site
  Recruiting and data collection
  Savings analysis

## Slide 10: Summary of net methods
For capital measures: self-reported attribution (SRA)
Well suited to assessment of capital measures that typically entail installation of equipment. Similar approach to custom measures under CIAC with a structured survey of key decision maker(s). DNV adapted SRA survey instruments and methods approved in the PY2021/2022 evaluation with some streamlining.
For non-capital/BRO measures: theory-driven attribution (TDA)
Well suited to assessing whether the program activities are impacting organizational behavior changes to produce persistent ongoing savings through a series of prescribed activities. DNV adapted the 2018–2019 TDA evaluation methods and survey instruments for this evaluation.
Notes: This evaluation cycle employed two evaluation methods, one for capital measures and another for the non-capital/BRO measures.
The NTGR results from the two methods are combined proportional to savings.

## Slide 11: Summary of data collection
Net sample was fully embedded with the gross sample
Energy Champion and Executive Sponsor interviews included a NTGR battery for capital measures
TDA battery, tailored for each interviewee type, confirms the activities delivered to the customer and the level of customer engagement
Interviewee type | Interview purpose | Method | Completed
Energy Champion Responsible for the success of the SEM program at the site. Coordinates with the SEM Coach and internally. | Feedback confirmed evaluated capital projects, and informed NTG algorithms, TDA delivery and engagement scores, and process findings. | TDA and SRA | 13
Executive Sponsor Highest-level manager available at the site (typically the facility manager). Ensures resources for success. | Feedback informed TDA delivery and engagement scores and process findings for improving the SEM program. | TDA and SRA | 5
Energy Coach Lead staff member from the implementation team in charge of interacting with the Energy Champion at each site and driving SEM engagement. | Feedback informed TDA delivery and engagement scores and the process findings for how well the program is working in CA. | TDA only | 8 coaches, covering 14 sites

## Slide 12: Findings
03

## Slide 13: Overview of gross results – MMBtu
PA | First year |  |  |  | Lifecycle |  |  | 
 | Forecasted savings | Evaluated savings | GRR | Relative precision | Forecasted savings | Evaluated savings | GRR | Relative precision
Energy (MMBtu) |  |  |  |  |  |  |  | 
MCE | 18,033 | 8,457 | 46.9% | ±11% | 90,167 | 43,961 | 48.8% | ±42%
SCE | 100,379 | 61,293 | 61.1% | ±48% | 501,894 | 324,412 | 64.6% | ±44%
SCG | 82,126 | 105,068 | 127.9% | ±46% | 410,629 | 542,167 | 132.0% | ±45%
Aggregate | 200,538 | 174,818 | 87.2% | ±33% | 1,002,690 | 910,540 | 90.8% | ±31%
These 2023 results will be combined in the 2024 evaluation cycle to develop a combined 2023–2024 realization rates for future application.
Table 4-3

## Slide 14: Overview of gross results – electric
PA | First year |  |  |  | Lifecycle |  |  | 
 | Forecasted savings | Evaluated savings | GRR | Relative precision | Forecasted savings | Evaluated savings | GRR | Relative precision
Energy (MWh) |  |  |  |  |  |  |  | 
MCE | 471 | 473 | 100.3% | ±0% | 2,357 | 2,622 | 111.2% | ±0%
SCE | 29,418 | 17,963 | 61.1% | ±48% | 147,091 | 95,076 | 64.6% | ±44%
Aggregate | 29,890 | 18,436 | 61.7% | ±47% | 149,448 | 97,698 | 65.4% | ±42%
Demand (MW) |  |  |  |  |  |  |  | 
MCE | 0.1 | 0.1 | 100.3% | ±0% | 0.4 | 0.4 | 111.2% | ±0%
SCE | 3.6 | 2.0 | 55.2% | ±57% | 18.0 | 10.6 | 58.6% | ±51%
Aggregate | 3.7 | 2.1 | 56.1% | ±55% | 18.4 | 11.0 | 59.7% | ±49%
These 2023 results will be combined in the 2024 evaluation cycle to develop a combined 2023–2024 realization rates for future application.
Table 4-1

## Slide 15: Overview of gross results – gas
PA | First year |  |  |  | Lifecycle |  |  | 
 | Forecasted savings | Evaluated savings | GRR | Relative precision | Forecasted savings | Evaluated savings | GRR | Relative precision
Natural gas (therms/1000) |  |  |  |  |  |  |  | 
MCE | 164 | 74 | 45.1% | 9.5% | 821 | 383 | 46.6% | 42.5%
SCG | 821 | 1,051 | 127.9% | 46.3% | 4,106 | 5,422 | 132.0% | 45.4%
Aggregate | 986 | 1,125 | 114.1% | 42.5% | 4,928 | 5,804 | 117.8% | 42.5%
These 2023 results will be combined in the 2024 evaluation cycle to develop a combined 2023–2024 realization rates for future application.
Table 4-2

## Slide 16: Gross FY & LC results – PY19-23
Chart: Gross FY Electric Realization Rate
| Statewide | MCE | PG&E | SCE | SDG&E
PY2019/20 | 0.99607 | 0 | 0.95011 | 1.0568 | 1.1493
PY2021/22 | 0.98356 | 0.90446 | 1.0164 | 0.90303 | 0.93055
PY2023 | 0.6168 | 1.0027 | 0 | 0.61062 | 0
Chart: Gross FY Gas Realization Rate
| Statewide | MCE | PG&E | SCG | SDG&E
PY2019/20 | 0.71502 | 0 | 0.70431 | 0.74074 | 0.84961
PY2021/22 | 0.78965 | 0.44166 | 0.83404 | 0.79791 | 0.9843
PY2023 | 1.1412 | 0.45055 | 0 | 1.2793 | 0
Chart: Gross LC Electric Realization Rate
| Statewide | MCE | PG&E | SCE | SDG&E
PY2019/22 | 1.1237 | 0 | 1.0109 | 1.0198 | 6.0131
PY2021/22 | 1.0789 | 0.95511 | 1.0633 | 1.0073 | 1.3554
PY2023 | 0.65373 | 1.1125 | 0 | 0.64638 | 0
Chart: Gross LC Gas Realization Rate
| Statewide | MCE | PG&E | SCG | SDG&E
PY2019/20 | 1.2324 | 0 | 1.3102 | 0.6846 | 4.248
PY2021/22 | 0.93307 | 0.55069 | 1.0302 | 0.83914 | 0.9843
PY2023 | 1.1779 | 0.46601 | 0 | 1.3203 | 0

## Slide 17: Summary of MMBtu gross findings – discrepancy review
Discrepancy factor | Description
SEM-specific discrepancies | Differences attributed to annualization errors, non-routine adjustments, long-term and short-term operational changes, incremental savings adjustment.
Tracking data | Differences attributed to inconsistencies between savings claimed and savings calculated in the provided models and/or completion report. This also includes discrepancies in savings due to unexplained or non-documented changes.
Inoperable measure | Differences attributed to measures that were removed and were no longer in operation. This includes measures that were not installed, failure of installed equipment, and business closure.
Inappropriate baseline | Represents a difference in evaluated and reported baseline, including any baseline periods adjustment in the models used to estimate forecasted and evaluated savings. This also includes any savings deviation due to a different ISP, code, or pre-existing baseline.
Operating conditions | Collected trend data or photographs of setpoints informs different operating parameters, including hours of use, setpoints, efficiency, etc.
Calculation methods | Differences attributed to changes in calculation methodology between that used for forecasting savings and evaluation analysis. The evaluator only changed analysis methodology when necessary to accurately calculate savings such as employing an 8760 model.
Table 4-4

## Slide 18: Summary of MMBtu gross findings – discrepancy review
Table 4-5

## Slide 19: Overview of net results – MMBtu
The TDA sample included only two MCE sites, both of which participated in the gas SEM program, and reported having trouble engaging fully with the program.
Feedback from one site significantly drove down the NTGR, as the participant reported that the only opportunity identified through the program was their old HVAC system—an upgrade the Energy Champion had already planned independently, without influence from the SEM program.
PA | First year |  |  |  | Lifecycle |  |  | 
 | Evaluated gross savings | Net savings | NTGR | Relative precision | Evaluated gross savings | Net savings | NTGR | Relative precision
Energy (MMBTU) |  |  |  |  |  |  |  | 
MCE | 8,457 | 5,828 | 68.9% | 18.5% | 43,961 | 23,396 | 53.2% | 48.5%
SCE | 61,293 | 60,806 | 99.2% | 0.8% | 324,412 | 320,625 | 98.8% | 1.2%
SCG | 105,068 | 104,242 | 99.2% | 0.9% | 542,167 | 535,425 | 98.8% | 1.5%
Statewide | 174,818 | 170,876 | 97.6% | 0.9% | 910,540 | 879,446 | 96.3% | 1.7%
Table 4-8

## Slide 20: Overview of net results – electric
PA | First year |  |  |  | Lifecycle |  |  | 
 | Forecasted savings | Evaluated savings | GRR | Relative precision | Forecasted savings | Evaluated savings | GRR | Relative precision
Energy (MWh) |  |  |  |  |  |  |  | 
MCE | 473 | 469 | 99.2% | ±0.8% | 2,622 | 2,592 | 98.8% | ±1.2%
SCE | 17,963 | 17,820 | 99.2% | ±0.8% | 95,076 | 93,966 | 98.8% | ±1.2%
Aggregate | 18,436 | 18,289 | 99.2% | ±0.8% | 97,698 | 96,558 | 98.8% | ±1.2%
Demand (MW) |  |  |  |  |  |  |  | 
MCE | 0.1 | 0.1 | 99.6% | ±0.6% | 0.4 | 0.4 | 99.1% | ±1.3%
SCE | 2.0 | 2.0 | 99.6% | ±0.6% | 10.6 | 10.5 | 99.1% | ±1.3%
Aggregate | 2.1 | 2.1 | 99.6% | ±0.6% | 11.0 | 10.9 | 99.1% | ±1.3%
NTGR electric results based on SCE sites only
Table 4-6

## Slide 21: Overview of net results – gas
PA | First year |  |  |  | Lifecycle |  |  | 
 | Forecasted savings | Evaluated savings | GRR | Relative precision | Forecasted savings | Evaluated savings | GRR | Relative precision
Natural gas (therms/1000) |  |  |  |  |  |  |  | 
MCE | 74 | 51 | 68.9% | ±18.5% | 383 | 204 | 53.2% | ±48.5%
SCG | 1,051 | 1,042 | 99.2% | ±0.9% | 5,422 | 5,354 | 98.8% | ±1.5%
Aggregate | 1,125 | 1,093 | 96.9% | ±1.3% | 5,804 | 5,558 | 95.2% | ±2.5%
These 2023 results will be combined in the 2024 evaluation cycle to develop a combined 2023–2024 realization rates for future application.
Table 4-7

## Slide 22: Comparison with other NTG Research Results
Similar results to the previous evaluations
Program and year | Electric NTGR | RP | NG NTGR | RP
SEM 2023 preliminary interim results | 99.1% | 0.9% | 96.9% | 1.3%
Capital only, information only | 0.95 |  | 0.75 | Not calculated
Recommended value | 1.0 |  | 1.0 | 
SEM 2021/2022 | 98.4% | 0.6% | 98.0% | 2.5%
Capital only, information only | 0.80 |  | 0.74 | Not calculated
Recommended value | 1.0 |  | 1.0 | 
SEM 2018/2019 | 1.0 |  | 1.0 | 
Core NTGR, info only | 0.61 | Not calculated | 0.61 | Not calculated
Table 4-9

## Slide 23: Site-specific TDA
Table 4-12
Site ID | Vendor | Delivery score | Engagement score | Combined TDA score | Final TDA NTGR score | Capital project SRA NTG | BRO project SRA NTG
SCE_01 | Cascade | 0.98 | 0.95 | 0.97 | 1 | 0.64 | 0.9
SCE_02 | Cascade | 0.94 | 0.98 | 0.96 | 1 | 0.93 | 0.97
SCE_03 | Cascade | 0.99 | 0.83 | 0.91 | 1 | No Cap | 0.73
SCE_04 | Cascade | 0.94 | 0.88 | 0.91 | 1 | 1.00 | 0.97
SCE_05 | Cascade | 0.92 | 0.74 | 0.83 | 1 | No Cap | 0.53
SCE_06 | Cascade | 0.88 | 0.75 | 0.82 | 1 | 0.75 | 1.0
SCE_07 | Cascade | 0.79 | 0.76 | 0.78 | 1 | No Cap | 
SCE_SCG_011 | Cascade | 0.90 | 0.93 | 0.91 | 1 | No Cap | 1.0
SCE Summary |  | 0.92 | 0.85 | 0.89 | 1.00 | 0.83 | 
SCG_01 | Cascade | 0.84 | 0.88 | 0.86 | 1 | 0.90 | 1.0
SCG_02 | Cascade | 0.91 | 0.79 | 0.85 | 1 | 1.00 | 0.61
SCG_03 | Cascade | 0.86 | 0.83 | 0.84 | 1 | 0.77 | 
SCE_SCG_011 | Cascade | 0.90 | 0.93 | 0.91 | 1 | No Cap | 0.83
SCG Summary |  | 0.88 | 0.86 | 0.87 | 1 | 0.89 | 
MCE_012 | CLEAResult | 0.65 | 0.74 | 0.70 | 1 | 0.17 | No BRO
MCE_02 | CLEAResult | 0.60 | 0.71 | 0.66 | 1 | 0.72 | 0.7
MCE Summary |  | 0.63 | 0.73 | 0.68 | 1.00 | 0.45 | 0.7
1 No gross evaluated savings due to missing data. 2 Commercial site |  |  |  |  |  |  | 
The two MCE gas SEM program sites reported:
One site: "glorified steam trap program“ ... not able to identify deeper opportunities.
One site: claimed the capital measure (an HVAC end of life replacement) was well in progress at SEM enrollment
Notes: Table provides the average Delivery and Engagement scores by individual project
  A Final TDA NTGR using the 50% POE standard is shown, all of which are 1.0
  The Final two columns present the capital NTGR and an informal non-capital BRO

## Slide 24: Program TDA Results
50% POE
Figure 4-1
50% threshold for POE
Could be shifted higher using the new TDA scoring methodology to define the minimum threshold of a successful SEM program.

## Slide 25: Conclusions and recommendations
04

## Slide 26: Conclusions and recommendations – overall
Conclusion
Program reporting and tracking data The unique structure of the SEM program allows a single participant to submit multiple claims over several years—typically within a 2-year cycle. However, there have been instances where the cycle extends to 3 years, such as when a site pauses SEM participation for a year due to unexpected circumstances like turnovers or temporary shifts in priorities and resources.
Recommendation(s)
PAs should continue working in collaboration with CPUC staff to enhance SEM program reporting and data tracking.
PAs should continue to review, refine, and implement improvement opportunities for program tracking identified in prior CPUC studies and statewide discussions. This includes consistently reporting the cycle, reporting period, and program year of each claim.
PAs should internally track and report the analysis methodology used for each claim, indicating whether it was based on top-down modeling or bottom-up calculations.

## Slide 27: Conclusions and recommendations – gross-specific
Conclusion
Gross savings analysis methods We observed a decline in the use of the top-down modeling approach, with fewer sites adopting it and a decrease in the percentage of savings from top-down models for electric and gas compared to PY21/22. The SEM M&V Guide designates top-down modeling as the preferred methodology for calculating SEM savings. While bottom-up calculations are allowed and justified in certain situations, they may obscure zero or negative savings—particularly at sites beyond the first reporting cycle, where SEM-related savings could regress.
Recommendation(s)
Implementers should provide justifications for using bottom-up calculations that are site-specific and reasonable, and PAs must conduct thorough reviews of root causes noted in bottom-up justifications before approving.
For sites using bottom-up calculations to claim savings beyond the first reporting cycle, implementers should collect and provide evidence and documentation of savings persistence from the previous cycle and include it in the project files package.

## Slide 28: Conclusions and recommendations – gross-specific
Conclusion
Savings annualization discrepancies Savings annualization refers to prorating the savings calculated within a short period of time to represent a full year of savings. Overall, the use of annualization based on insufficient or unrepresentative periods of facility operation in PY2023 resulted in a 6% decrease in total forecasted savings, compared to an 8% decrease in PY2021/22, reflecting significant improvement from PY2021/2022. This improvement is primarily due to sites using longer periods for annualization in PY2023.
Recommendation(s)
If SEM participants decide to use bottom-up calculations for the second reporting period after using the top-down modeling approach in the first, implementers should consider recalculating the savings from the first reporting period using the bottom-up calculations and truing up the savings at the end of the cycle.

## Slide 29: Conclusions and recommendations – gross-specific
Conclusion
Top-down model discrepancies Our top-down models corrections resulted in a 10% decrease in total forecasted savings, compared to a 4% decrease in PY2021/22. We reviewed all top-down models used by SEM participants to calculate savings for projects implemented in PY2023. These corrections included removing variables that showed no impact on energy consumption, adjusting changepoints of weather variables to better reflect impact of weather conditions on facilities’ energy consumption, and excluding non-routine events (NREs).
Recommendation(s)
Implementers should continue to follow the SEM M&V guidelines on creating top-down models and assessing their validity. This includes excluding variables that have no impact on energy consumption and identifying non-routine events, then recalibrating the model to neutralize their influence on the savings estimates.
Implementers should investigate further when savings from either top-down modeling or bottom-up calculations are inaccurate or disproportionate to the measures installed and consider using the alternative savings calculation approach if the disparity cannot be explained or resolved.

## Slide 30: Conclusions and recommendations – gross-specific
Conclusion
Bottom-up calculation discrepancies We reviewed all submitted bottom-up calculations for sampled projects and corrected savings calculation methodologies, inputs, and parameters, based on in-depth engineering reviews and as-found data collected from facility personnel. Overall, these adjustments to the bottom-up calculations led to a 3% increase in forecasted savings.
Recommendation(s)
Implementers should continue using measure- and site-specific parameters with documented references and substantiation for all inputs, to the extent feasible. This will result in more accurate savings estimations.
Implementers should continue normalizing baseline production and occupancy profiles based on as-built operations so that calculated savings only reflect installed measures and improvements.
Implementers should include any trend or metered data used for forecasted savings estimation in project files as well as any invoices, photographs, and other relevant documentation.

## Slide 31: Conclusions and recommendations – net-specific
Conclusion
SEM NTGR methods The DNV team optimized the SEM SRA instrument and adapted the 2018–2019 TDA instruments for the 2023 evaluation. TDA is an essential method for assessing whether the SEM activities are being delivered and producing desired outcomes. However, TDA does not directly produce a NTGR. SEM projects should also meet a minimum standard of compliance to be considered a SEM delivery warranting the SEM NTGR.
Recommendation(s)
Evaluators should use the SRA and TDA survey instruments developed in this impact evaluation for the PY2024 evaluation.
Evaluators should develop a non-capital, BRO-oriented SRA NTGR battery to provide additional perspectives on program influence. This will provide an alternate source of NTGR should a PA fail to demonstrate a high level of influence on program outcomes.
The CPUC should require evaluators to investigate an alternate algorithm for converting a TDA score to a NTGR score for applications after the 2024 evaluation to better align NTGR outcomes with the Expansion Study recommendations.

## Slide 32: Questions
05

## Slide 33: Questions
Contacts: | Ismail Omar ismail.omer@dnv.com
 | Chad Telarico chad.telarico@dnv.com
 | Susan Haselhorst susan.haselhorst@dnv.com
Study link: | XX
Comments due: | XX

## Slide 34: Thank you!

## Slide 35: NTGR of capital
PA | Total MMBtu | Percent of capital MMBtu | Total kWh savings | Percent of capital kWh | Total therm savings | Percent of capital therm | Avg. SRA
SCE | 32,706 | 18% | 1,682,073 | 18% | - | 0% | 0.83
SCG | 60,336 | 13% | - | 0% | 75,693 | 13% | 0.89
MCE | 6,820 | 77% | 27,125 | 19% | 51,297 | 81% | 0.44
Statewide | 99,862 | 19% | 1,709,198 | 18% | 126,990 | 19% | -
Table 4-10
Capital measures constitute about 19% of 2023 tracking savings, compared to 16% in 2021/2022
  PAs are doing a good job accurately recording capital measures in the Opportunity Register
  MCE’s low NTGR was due to an HVAC upgrade that had been in-progress prior to SEM participation

## Slide 36: TDA results
Requirements | Component | Average SCE Score n=8 | Average SCG Score n=4 | Average MCE Score n=2
1 – Kick-off meeting. Introducing SEM to the site, defining the roles at the facility, and laying out a program schedule. | Delivery | 3.0 | 3.0 | 2.5
 | Engagement | 2.3 | 2.5 | 2.0
2 – Energy Management Assessment (EMA). Assessing the site’s current energy use policies and procedures. The implementer conducts these assessments each year of the program and has the option of sharing the results with the facility. | Delivery | 3.0 | 3.0 | 3.0
 | Engagement | 3.0 | 3.0 | 3.0
3 – Energy Use Mapping. Detailed mapping of any and all energy consumption at the facility. | Delivery | 2.8 | 2.5 | 1.5
 | Engagement | 2.8 | 2.8 | 3.0
4 – Energy Treasure Hunt. Walking the entire facility searching for ways to reduce energy waste either through capital project upgrades or process and behavioral changes. | Delivery | 2.6 | 2.8 | 2.1
 | Engagement | 2.5 | 2.8 | 2.5
5 – Action Plan and Support. Identifying and creating action plans to meet SEM requirements including meetings, trainings, and workshops. | Delivery | 2.5 | 2.4 | 1.6
 | Engagement | 2.8 | 2.8 | 1.5
6 – Energy Management Information System (EMIS). Developing a system to manage energy use and model energy savings across the entire facility. | Delivery | 2.8 | 3.0 | 1.5
 | Engagement | 2.6 | 2.8 | 2.3
7 – Future Planning. Creating a plan for meeting program requirements in future program years as well as how to continue to pursue energy efficiency after program participation ends | Delivery | 2.6 | 1.8 | 1.0
 | Engagement | 2.1 | 1.5 | 1.0
Average Delivery |  | 2.8 | 2.6 | 1.9
Average Engagement |  | 2.6 | 2.6 | 2.2
Table 4-11
Notes: Scoring results across the seven Guide requirements in the area of Delivery and Engagement
Engagement and Delivery scores were low for MCE which tracks with other impact outcomes