## Slide 1: LSE Forecast Adjustments 2022 Resource Adequacy
June 18, 2021
Lynn Marshall
Lynn.Marshall@energy.ca.gov
Energy Assessments Division
California Energy Commission

## Slide 2: Resource Adequacy Load Forecast Adjustment Process
Develop reference forecast for IOU service areas and direct access
Estimate and apply coincidence factors to LSE forecasts.
Develop reference current peak demand estimate for LSEs based on available data.
Evaluate need for LSE-specific adjustments.
Apply adjustments for incremental effects of demand side programs.
Apply pro-rata adjustments to bring the total of the forecasts to within 1% of the CEC service area forecast.
Evaluate the reasonableness of pro-rata adjustments and total forecast for each LSE and service area.
If step 7 indicates pro rata adjustment is too large, review steps 2-7.

## Slide 3: Comparison of RA 2022 v. RA 2021 Monthly TAC Area Coincident Peak Forecast
  Source:2020: https://efiling.energy.ca.gov/GetDocument.aspx?tn=236297-1&DocumentContentId=69272;
  2021: https://efiling.energy.ca.gov/GetDocument.aspx?tn=231551&DocumentContentId=63367
PGE TAC summer peak loads increase
SCE and SDGE decrease slightly

## Slide 4: Service Area Reference Forecast
Reference forecast for CPUC-jurisdictional LSE forecasts begins with forecasted monthly TAC coincident peaks from the 2020 Integrated Energy Policy Report Update mid-demand, mid-AAEE case demand forecast.
CEC evaluates hourly loads and forecasts for all CAISO LSEs.
SDG&E reference forecast equals the TAC area forecast
SCE and PG&E TAC forecasts are disaggregated to CPUC and non-CPUC jurisdictional using CEC service area forecast, and LSE forecasts and hourly loads.
  Service Area Annual (noncoincident) Peak Demand
  Source: CED 2020 Managed Forecast - LSE and BA Tables Mid Demand - Mid AAEE Case, Form 1.5b
  https://efiling.energy.ca.gov/GetDocument.aspx?tn=237319&DocumentContentId=70504

## Slide 5: Disaggregation of PG&E TAC Forecast to CPUC and POU Load
POU loads are about 10% of the TAC. With proportionately more pumping and industrial load, POU loads have a flatter profile across months.

## Slide 6: Disaggregation of SCE TAC Forecast to CPUC and POU Forecast
POU loads are about 11% of the SCE TAC

## Slide 7: Comparison of CPUC-Jurisdictional RA 2020-2022 Forecasts
Differences parallel changes in the TAC and service area annual peak forecasts

## Slide 8: Direct Access Reference Estimate
Adjustments to ESP forecasts should be consistent with the cap on enrollment, as reflected in recent loads plus expected 2021 and 2022 increases.
For each TAC area, historic hourly ESP loads were summed to find the 3-year median of the top 5 coincident peaks,
Increase is estimated using sales of load scheduled to switch to direct access service in January 2021 and 2022, historic DA load factors, and DA coincidence factors.

## Slide 9: Coincidence Adjustments
Coincidence adjustments should represent expected LSE demand at the time of a 1-in-2 CAISO-wide system peak.
Composite loads of LSEs were constructed by compiling 2020 loads of current and migrating load
Median coincident factor during the top 5 peak days is typically used when the month includes a sufficient number of high load days:
  Load diversity declines as demand rises, so if sample doesn’t include enough relatively high load days, diversity will be overestimated, leading to increased unallocated load.
  Large amounts of demand response, outages, or intra-month load migration can skew statistics
  For 2020, also evaluated the distribution of coincidence factors for top 10 peak hours.
CAISO posts load data used for this analysis annually at:
http://www.caiso.com/planning/Pages/ReliabilityRequirements/Default.aspx#Historical

## Slide 10: Demand Modifier Adjustment
LSE forecasts are credited with a share of AAEE and some load modifying demand response (LMDR) to the extent that it is not accounted for in their forecasts
  LSE share is netted against amounts reported in their forecasts
  CEC staff reviews other load modifiers (EE, BTM PV, storage, or transportation electrification) in LSE forecasts for consistency with reference forecast.
  The 2021 IEPR forecast will also include some amount of building electrification
  If LSEs are planning other types of load-modifying strategies, they should include it in their forecast submitted to the 2021 IEPR.
  2022 Incremental Additional Achievable Energy Efficiency

## Slide 11: LSE-Specific Adjustments
Staff uses historic loads and temperatures, month-ahead forecasts, and DASR activity to construct a reference estimate for each LSE by service area:
  Reference estimates were adjusted to allow for economic trends given LSE sector mix
  A 5% percent deviation is a flag for additional review.
LSE forecasts are evaluated using historic loads and temperatures, evaluation of forecast assumptions, and comparison with CEC forecast assumptions
  IOU departing load estimate are revised for consistency with CCA forecasts as adjusted by CEC, and CEC-estimated direct access load.
  Aggregate ESP forecasts are evaluated against the direct access reference estimate to identify need for further adjustments
  IOU forecasts may also be revised for differences with CEC service area forecast

## Slide 12: Pro-Rata Adjustment
If the sum of the adjusted forecasts differs from the service area reference forecast by more than 1%, the exceedance is allocated on the share of an LSE’s adjusted forecast of total service area adjusted forecasts.
If sum of adjusted ESP forecasts after pro-rata differs from the DA reference estimate by more than 5 percent, individual ESP forecasts are further reviewed.
Draft Pro-Rata Adjustment Percent by TAC

## Slide 13: Preliminary Estimates of RA 2022 Forecast Adjustments
Staff is continuing to review and adjust individual forecasts which could reduce pro-rata adjustments.

## Slide 14: Next Steps
  Final review of individual forecasts is ongoing
    For LSE-specific questions contact CEC staff
  CEC transmits September 2022 load ratio shares to CAISO by June 30 for import and local reliability area capacity allocations
  Final forecasts due in August should be revised only for load migration