## Slide 1: Resource Tracking Data
Data current as of January 2026

## Slide 2: Notes on Resource Tracking Data
  Notes on Online MWs data
    All data are derived from CAISO Master Generating Capability List, and CPUC NQC Lists with online dates between Jan 1, 2020 – January 28, 2026.
    Nameplate Capacity is shown as “Net Dependable Capacity” in the CAISO Master Generating List file.
    Data shown excludes imports, except where specified.
    NQC values are “Estimated September NQC” and subject to change based on counting rules or changes to resource configurations.
    Data showing “Number of Projects” is derived by counting each unique CAISO resource ID as a project.
    “Natural Gas” includes Alamitos Unit 7 (675 MW) and Huntington Beach (674 MW), online in Feb 2020.
  Notes on Expected New MWs
    All data are from LSE self-reported contracting for projects expected to come online between 2026 and 2029.
    Data are subject to change as the CPUC gets updated information from LSEs, IOU interconnection departments, developers and others.
    CPUC staff continue to refine the data included herein. Data in this presentation are current up until January 2026 and any subsequent postings will supersede prior postings.
    Data included here are only the projects under contract to CPUC jurisdictional LSEs, and do not include all resources being developed in the state nor the CAISO footprint.
  Notes on Differences between Resource Tracking Data and IRP Compliance
    Due to numerous differences, such as varied baselines and resource eligibility for compliance, data on New MW Online plus New MW Expected do not exactly match progress towards IRP compliance orders. For information on compliance with IRP Procurement orders, see compliance updates at IRP Procurement Track (ca.gov).
  Notes on Updates and Questions
    For the most up-to-date data publicly available, please visit the CPUC's Summer Reliability page.
    For any questions about the data, please contact irpdatarequest@cpuc.ca.gov

## Slide 3: Part 1: New MW Online
New Resources Online from 1/1/2020 to 1/28/2026
  By Nameplate, NQC, and Number of Projects
New Resources Online by Year and Resource Type
  By Nameplate and NQC
New IRP Procurement Resources Online by Year and Resource Type
  By Nameplate and NQC

## Slide 4: New MWs - Key Takeaways
 | Nameplate Capacity (MW) | Estimated Sept. Net Qualifying Capacity (NQC) MW | Number of Projects by Resource IDs
New SB100 Resources, IN-CAISO | 27,201 | 17,635 | 410
New Resources, IN-CAISO (includes Natural Gas) | 28,752 | 19,133 | 429
Total New Reliability Resources, including Imports | 31,097 | 20,555 | 452
 | Nameplate Capacity (MW) | Estimated Sept. Net Qualifying Capacity (NQC) MW | Number of Projects by Resource IDs
Battery Energy Storage Systems (BESS) Projects (Including Standalone BESS & Hybrids) | 15,852 | 14,783 | 231 (incl. 33 hybrids)
Data includes projects online as of January 28, 2026
Total New MW Online between 1/1/2020 - 1/28/2026
Total Storage Online (all time)
Note: MW only include storage portion of hybrids. Includes CAISO imports.
Note: SB100 resources include all eligible renewable energy resources and zero-carbon resources for compliance with California's SB 100 clean energy targets.

## Slide 5: New Energy Resources Online
Technology Type | Nameplate Capacity MW | Estimated Sept. Net Qualifying Capacity (NQC) MW | Number of Projects
STORAGE | 14,419 | 13,422 | 188
SOLAR | 9,398 | 2,460 | 155
HYBRID (STORAGE/SOLAR) | 2,172 | 1,473 | 30
WIND | 1,128 | 249 | 23
GEOTHERMAL | 41 | 31 | 1
BIOGAS, BIOMAS, HYDRO | 44 | 0.1 | 13
Subtotal Total New SB100 Resources, IN-CAISO | 27,201 | 17,635 | 410
NATURAL GAS, incl. Alamitos & Huntington Beach | 1,551 | 1,498 | 19
Total New Resources, IN-CAISO | 28,752 | 19,133 | 429
New Imports, Pseudo-Tie or Dynamically Scheduled | 2,345 | 1,423 | 23
Total New Resources, including Imports | 31,097 | 20,555 | 452
New Resources Additions, January 1, 2020 – January 28, 2026, Cumulative
Notes: All data shown derived from CAISO Master Generating Capability List, and CPUC NQC Lists.
Nameplate Capacity is shown as “Net Dependable Capacity” in the CAISO Master Generating List file. Data shown excludes imports, except where specified. All NQC values are “September NQC” and subject to change based on counting rules and additions to monthly CPUC NQC Lists. “Project” is defined as a unique CAISO resource ID. “Natural Gas” includes Alamitos Unit 7 (675 MW) and Huntington Beach (674 MW) added in Feb 2020. SB100 resources include all eligible renewable energy resources and zero-carbon resources for compliance with California's SB 100 clean energy targets.
Data includes projects online as of January 28, 2026
Notes: This slide shows the unprecedented quantity of new clean energy resources that have come online in under two years.
So, Let’s just take a quick look at this data together. We are showing both the nameplate and Sept. net qualifying capacity (NQC). The NQC reflects the amount a particular resource can count towards meeting the reliability requirements.
The first row shows the huge amount of new energy storage that has come online since January 2020. This is really the big story in the transformation of the energy fleet. While we have been expecting storage to provide reliability for most of the past decade – here we can see it has finally arrived – it is now here. So, Prior to 2020 we had just barely begun to see a few hundred MWs of energy storage online to serve the CAISO markets – and most of the storage was providing just ancillary services. But the storage that you see here now reflects a truly new reliability resource – and these storage MWs are providing energy and capacity on a daily basis. There is also some storage shown in the “Hybrid” line – so together, there is over 4,000 MW of new storage regularly serving the CAISO market at this time. (And growing monthly)
Of course these storage MWs need energy to charge – so the wind and solar MWs that were added in the past two years – can help provide that energy.
In addition to the Clean New Resources shown, our possibly last new gas plants came online in Feb 2020 so they are included here as part of the data set of new resources. Also, some of our new resources serving the CAISO do so as imports, so there are some new imports shown on this chart as well.
All of the new resources support reliability in different ways.

## Slide 6: New MWs Online - Nameplate By Year and Resource Type
Technology Type | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | Total MW | # Projects
SOLAR | 1,300 | 1,048 | 913 | 2,482 | 2,227 | 1,426 | 3 | 9,398 | 155
STORAGE | 101 | 1,703 | 1,907 | 2,528 | 3,553 | 4,536 | 92 | 14,419 | 188
HYBRID (SOLAR + STORAGE) | 0 | 26 | 890 | 354 | 503 | 399 | 0 | 2,172 | 30
WIND | 16 | 304 | 367 | 154 | 260 | 27 | 0 | 1,128 | 23
GEOTHERMAL | 0 | 0 | 0 | 0 | 41 | 0 | 0 | 41 | 1
HYDRO | 26 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 4
BIOMASS | 0 | 2 | 3 | 3 | 0.5 | 3 | 0 | 11 | 5
BIOGAS | 1 | 0 | 2 | 3 | 0 | 2 | 0 | 8 | 4
Subtotal Total New SB100 Resources, IN-CAISO | 1,444 | 3,083 | 4,082 | 5,521 | 6,584 | 6,393 | 95 | 27,201 | 410
NATURAL GAS, incl. Alamitos & Huntington Beach | 1,448 | 17 | 12 | 0 | 63 | 13 | 0 | 1,551 | 19
Total New Resources, IN-CAISO | 2,892 | 3,100 | 4,094 | 5,521 | 6,647 | 6,406 | 95 | 28,752 | 429
New Imports, Pseudo-Tie or Dynamically Scheduled | 695 | 807 | 49 | 50 | 282 | 459 | 0 | 2,345 | 23
Total New Resources, including Imports | 3,587 | 3,907 | 4,143 | 5,571 | 6,928 | 6,865 | 95 | 31,097 | 452
Data includes projects online as of January 28, 2026

## Slide 7: New MWs Online - Sept NQC By Year and Resource Type
Technology Type | 2020 | 2021 | 2022 | 2023 | 2024 | 2025* | 2026* | Total MW | # Projects
SOLAR | 444 | 435 | 318 | 606 | 499 | 157 | 0 | 2,460 | 155
STORAGE | 100 | 1,607 | 1,906 | 2,448 | 3,499 | 3,863 | 0 | 13,422 | 188
HYBRID (SOLAR + STORAGE) | 0 | 15 | 569 | 243 | 331 | 316 | 0 | 1,473 | 30
WIND | 3 | 65 | 80 | 33 | 63 | 6 | 0 | 249 | 23
GEOTHERMAL | 0 | 0 | 0 | 0 | 31 | 0 | 0 | 31 | 1
HYDRO | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4
BIOMASS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5
BIOGAS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4
Subtotal Total New SB100 Resources, IN-CAISO | 548 | 2,122 | 2,872 | 3,329 | 4,424 | 4,341 | 0 | 17,635 | 410
NATURAL GAS, incl. Alamitos & Huntington Beach | 1,448 | 15 | 11 | 0 | 12 | 11 | 0 | 1,498 | 19
Total New Resources, IN-CAISO | 1,995 | 2,137 | 2,883 | 3,329 | 4,436 | 4,352 | 0 | 19,133 | 429
New Imports, Pseudo-Tie or Dynamically Scheduled | 390 | 387 | 33 | 50 | 201 | 362 | 0 | 1,423 | 23
Total New Resources, including Imports | 2,385 | 2,524 | 2,916 | 3,379 | 4,637 | 4,714 | 0 | 20,555 | 452
*Note: Some new projects have not yet made it onto the CPUC’s monthly NQC list and have not yet been assigned NQC. Future reports will include updated NQC amounts for these resources.
Data includes projects online as of January 28, 2026

## Slide 8: New MWs Online - Sept NQC By Year and Transmission Access Charge (TAC) Area
TAC Area | 2020 | 2021 | 2022 | 2023 | 2024 | 2025* | 2026* | Total MW | # Projects
EAST CENTRAL (SOUTHERN CALIFORNIA EDISON COMPANY) | 1,766 | 1,221 | 2,049 | 1,976 | 3,322 | 2,716 | 0 | 13,049 | 268
NORTH (PACIFIC GAS AND ELECTRIC) | 230 | 724 | 715 | 1,082 | 758 | 708 | 0 | 4,216 | 118
SOUTH (SAN DIEGO GAS AND ELECTRIC) | 0 | 192 | 120 | 271 | 356 | 929 | 0 | 1,868 | 43
Total New Resources, IN-CAISO | 1,995 | 2,137 | 2,883 | 3,329 | 4,436 | 4,352 | 0 | 19,133 | 429
New Imports, Pseudo-Tie or Dynamically Scheduled | 390 | 387 | 33 | 50 | 201 | 362 | 0 | 1,423 | 23
Total New Resources, including Imports | 2,385 | 2,524 | 2,916 | 3,379 | 4,637 | 4,714 | 0 | 20,555 | 452
*Note: Some new projects have not yet made it onto the CPUC’s monthly NQC list and have not yet been assigned NQC. Future reports will include updated NQC amounts for these resources.
Data includes projects online as of January 28, 2026

## Slide 9: New MWs Online January 2026 Additions
Technology Type | Nameplate Capacity MW | Estimated Sept. Net Qualifying Capacity (NQC) MW | # Projects
STORAGE | 92 | 0* | 1
SOLAR | 3 | 0* | 2
Total New Resources, IN-CAISO | 95 | 0* | 3
New Imports, Pseudo-Tie or Dynamically Scheduled | 0 | 0* | 0
Total New Resources, including Imports | 95 | 0* | 3
IRP Procurement
*Note: New projects have not yet made it onto the CPUC’s monthly NQC list and have not yet been assigned NQC. Future reports will include updated NQC amounts for these resources.
Technology Type | Nameplate Capacity MW | Estimated Sept. Net Qualifying Capacity (NQC) MW | # Projects
STORAGE | 92 | 0* | 1
SOLAR | 1 | 0* | 1
Total New Resources, IN-CAISO | 93 | 0* | 2
New Imports, Pseudo-Tie or Dynamically Scheduled | 0 | 0* | 0
Total New Resources | 93 | 0* | 2
Data includes projects online as of January 28, 2026

## Slide 10
Note: Data shown here shows a snapshot of new resources added to the CAISO grid Q12020 – Q1 2026, including specified CAISO imports. "Other" resources include geothermal, biomass, biogas, and hydropower. Hybrids include some storage, and some other (usually solar) technology. "IRP Procurement Order Resources" refer to resources claimed for compliance with IRP Procurement Orders; "Non-IRP Resources" include resources that are not counting towards IRP Procurement order compliance, which occurs for a variety of reasons such as the resource was in development prior to IRP orders, the resource is energy-only, the resource is not under contract to a CPUC jurisdictional entity, etc.
NQC = Net qualifying capacity (NQC) and represents the amount the resource contributes to reliability; NQC can vary over time, and for each month of the year; the values shown are indicative of September NQC values for the resources.
Total New Procurement By Year and Resource Type
Data includes projects online as of January 28, 2026

## Slide 11
Note: Data shown here shows a snapshot of new resources added to the CAISO grid Q1 2020 – Q1 2026, including specified CAISO imports. Hybrids include some storage, and some other (usually solar) technology. MW shown here only include the storage portion of hybrids.
Total Storage Online By Year
Installed to date: Nearly 16,000 MW of storage nameplate capacity is online serving the grid as of January 2026, including imports.
  Includes ~150 MW of storage added prior to 2020
  Includes standalone battery storage and the storage component of hybrid resources
Expected future installs: An additional 13,000 MW of storage resources is under contract and expected to come online by 2029.
Data includes projects online as of January 28, 2026

## Slide 12: Part 2: Integrated Resource Planning Compliance
New IRP Procurement MW by Year and Resource Type- Nameplate
New IRP Procurement MW by Year and Resource Type – NQC

## Slide 13
Note: Data shown here shows a snapshot of new resources added to the CAISO grid Q1 2020 – Q1 2026 for compliance with Integrated Resource Planning (IRP) procurement orders, including specified CAISO imports. "Other" resources includes geothermal, biomass, biogas, and hydropower. Hybrids include some storage, and some other (usually solar). Additional resources have come online for other reasons in this time period but are not included in these figures.
See: IRP Procurement Track (ca.gov) for more information about IRP Procurement Order Compliance.
New IRP Procurement By Year and Resource Type
Data includes projects online as of January 28, 2026

## Slide 14: Part 3: Expected New MWs based on LSE Contracts to date
Expected New MW by Year and Resource Type- Nameplate
Expected New MW by Year and Resource Type – NQC
Total New Energy Resources Online and Under Contract - Nameplate

## Slide 15
Data includes projects expected/under contract
as of January 8, 2026
New MWs Expected - Nameplate By Year and Resource Type, including imports
Over 22,000 MW nameplate of future contracts are expected to meet CPUC’s procurement order obligations.
Majority of new resource MWs are expected to be battery storage and solar.
Other types of resources are eligible to meet orders and may be contracted in the future.
Resource Type | 2026 | 2027 | 2028 | 2029 | Total
Solar | 1,814 | 1,603 | 1,131 | 605 | 5,152
Battery Storage | 3,319 | 3,487 | 2,101 | 545 | 9,451
Paired/Hybrid | 1,663 | 1,782 | 623 | 50 | 4,118
Wind | 2,446 | - | 80 | - | 2,526
Geothermal | 115 | 174 | 514 | 30 | 833
Biomass/Biogas | 10 | 3 | - | - | 13
Totals | 9,366 | 7,048 | 4,449 | 1,230 | 22,094

## Slide 16
Data includes projects expected/under contract
as of January 8, 2026
New MWs Expected - NQC By Year and Resource Type, including imports
Resource Type | 2025 | 2026 | 2027 | 2028 | Total
Solar | 273 | 261 | 155 | - | 689
Battery Storage | 2,746 | 3,303 | 3,219 | 895 | 10,163
Paired/Hybrid | 497 | 925 | 856 | 33 | 2,311
Wind | 16 | 398 | 84 | 4 | 502
Geothermal | 9 | 139 | 173 | 445 | 766
Biomass/Biogas | 10 | - | - | - | 10
Totals | 3,551 | 5,026 | 4,487 | 1,378 | 14,441
Nearly 15,000 MW NQC of future contracts are expected to meet CPUC’s procurement order obligations.
Majority of new resource MWs are expected to be battery storage.
Other types of resources are eligible to meet orders and may be contracted in the future.
Resource Type | 2026 | 2027 | 2028 | 2029 | Total
Solar | 555 | 929 | 18 | 234 | 1,735
Battery Storage | 2,936 | 3,387 | 2,050 | 545 | 8,917
Paired/Hybrid | 963 | 1,253 | 385 | 74 | 2,676
Wind | 650 | - | 80 | - | 730
Geothermal | 112 | 170 | 502 | 27 | 811
Biomass/Biogas | 10 | 0 | - | - | 10
Totals | 5,225 | 5,739 | 3,036 | 880 | 14,879

## Slide 17
Note: Data shown here shows a snapshot of new resources added to CAISO grid Q12020 – Q1 2026, including specified CAISO imports. Also shown is a projection of future new resources based on contracts in place by January 2026. "Other" resources includes geothermal, biomass, biogas, and hydropower.
Total New Energy Resources Online and Under Contract

## Slide 18: Links to Other Key References on New Resource Development

## Slide 19: References to Related Information
Tracking Energy Development Task Force – Tracking Energy Development (ca.gov)
Joint Agency Reliability Planning Assessments – pursuant to SB 846
  May 2024 Report
  August 2024 Report
  March 2025 Report
  May 2025 Report
  August 2025 Report
California Energy Commission’s Energy Almanac - Energy Almanac (ca.gov)
CAISO Key Energy Statistics: Media resources | California ISO (caiso.com)
Overview of CPUC IRP Procurement Orders – IRP Procurement Track (ca.gov)
Overview of CPUC Jurisdictional LSE Procurement in Compliance with IRP Procurement Orders
  California Public Utilities Commission (CPUC) Staff Review of Load-Serving Entities’ (LSEs’) Compliance with the Mid-Term Reliability (MTR, D.21-06-035) and Supplemental MTR (SMTR, D.23-02-040) Decisions, 7/10/2025
  Procurement in Compliance with D.19-11-016 and Mid Term Reliability (D.21-06-035) per December 1, 2023, 10/9/2024
  Procurement in Compliance with D.19-11-016 and Mid Term Reliability (D.21-06-035) per August 1, 2023, 4/22/2024
  Procurement in Compliance with D.19-11-016 and Mid Term Reliability (D.21-06-035) per February 1, 2023, 11/2/2023
  Procurement in Compliance with D.19-11-016 per August 1, 2022 Fillings, 2/13/2023
  Procurement in Compliance with D.19-11-016 per February 1, 2022 Filings, 7/22/2022
  Procurement in Compliance with D.19-11-016 per February 1, 2021 Filings, 8/23/2021
  For any questions about the data, please contact irpdatarequest@cpuc.ca.gov