## Slide 1: Utility Role in Addressing PEV Infrastructure CPUC VGI and Financing Workshop Mark Duvall Director, Electric Transportation and Energy Storage December 4th, 2013

## Slide 2: PEV Adoption Increasing Sharply in CA
Chart: Plug in electric vehicle market share
| 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 2010 | 2011 | 2012 | 2013*
Chevrolet Volt | 0.00025569 | 0.00094111 | 0.0015514 | 0.0016159 | 0.001618 | 0.0016475 | 0.0015701 | 0.0013323 | 0.00088536 | 0.00084509 | 0.0012459 | 0.001423 | 0.0012423 | 0.0010556 | 0.0011532 | 0.0021225 | 0.0029174 | 0.0028017 | 0.0030933 | 0.0040194 | 0.0050699 | 0.0061809 | 0.0072975 | 0.0074077 | 0.0059999 | 0.004957 | 0.0042082 | 0.0038958 | 0.0040623 | 0.0042491 | 0.004916 | 0.0057482 | 0.0062994 | 0.0068092 | 0.0070515
Nissan LEAF | 5.272e-06 | 0.00013869 | 0.00034732 | 0.00069646 | 0.0016226 | 0.0034043 | 0.006066 | 0.0073074 | 0.0061579 | 0.0055423 | 0.0049761 | 0.0035282 | 0.0026784 | 0.0023461 | 0.0017754 | 0.001311 | 0.0011275 | 0.0010952 | 0.001179 | 0.0011453 | 0.0010964 | 0.0014237 | 0.0027109 | 0.0044038 | 0.0044479 | 0.003414 | 0.0024845 | 0.0028919 | 0.0045264 | 0.0051827 | 0.0049421 | 0.0049392 | 0.0047899 | 0.0047825 | 0.0054048
Toyota Prius Plug-in | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.7426e-05 | 0.0010813 | 0.0037773 | 0.0062567 | 0.00585 | 0.0041115 | 0.0034461 | 0.004486 | 0.0066057 | 0.0074371 | 0.0055466 | 0.0034726 | 0.0024731 | 0.0022227 | 0.0020102 | 0.0016569 | 0.0014895 | 0.001427 | 0.0014808 | 0.0022764 | 0.003815
Tesla Model S | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.5043e-05 | 4.7872e-05 | 9.0737e-05 | 0.00024987 | 0.00068982 | 0.0014357 | 0.0027252 | 0.0038556 | 0.0044008 | 0.0057521 | 0.0062469 | 0.0048497 | 0.005143 | 0.005703 | 0.0040697 | 0.0039695 | 0.0057395
Ford C-MAX Energi | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.1021e-05 | 0.00048069 | 0.0011197 | 0.0012642 | 0.0010656 | 0.0010208 | 0.0010312 | 0.00098973 | 0.00098818 | 0.0011233 | 0.0015707 | 0.0022573
Ford Fusion Energi | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00030845 | 0.00087946 | 0.0011775 | 0.00114 | 0.0011322 | 0.0012886 | 0.0017065 | 0.0023268
Remaining PHEVs | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.6374e-05 | 0.00012857 | 0.00024106 | 0.00023046 | 0.00019368 | 0.00018965 | 0.00014367 | 0.00010266 | 9.6816e-05 | 9.8797e-05 | 8.8291e-05 | 6.5971e-05 | 8.5804e-05 | 0.0001402 | 0.00019718 | 0.0002641 | 0.00026295 | 0.00023951 | 0.00025974 | 0.00026653 | 0.00025991
Remaining BEVs | 0.00014498 | 0.00011145 | 0.00010034 | 0.00013528 | 0.00021025 | 0.00025977 | 0.00022187 | 0.00015837 | 0.00013392 | 0.00016397 | 0.00022677 | 0.00043275 | 0.0011164 | 0.0015393 | 0.0011555 | 0.00079673 | 0.00083707 | 0.00080184 | 0.0007691 | 0.00082304 | 0.00062381 | 0.00043969 | 0.00069587 | 0.001215 | 0.0015363 | 0.0014404 | 0.0012165 | 0.0012637 | 0.0013768 | 0.0012667 | 0.0014568 | 0.0024906 | 0.0036177 | 0.0040617 | 0.0045271

## Slide 3: Total Cost of Vehicle Ownership – PEVs Can Be Competitive, Today
Recent price drops in some PEVs have caused TCO to improve—however pricing is regionally variable.
Nissan Leaf Comparison

## Slide 4: California has mandated 1.5 Million Zero Emission Vehicles by 2025 (3.3M including seven other states)
Fuel Cell Vehicles
Plug-In Electric Vehicles
We Are Here

## Slide 5: From ‘Transportation Electrification – A Technology Overview’ in 2011
There are about five models for owning and operating charging equipment
Municipally owned and operated for public benefit, similar to traffic signals, street lights, etc. Supported through municipal budgets.
Utility owned and operated for public benefit. Supported in the utility rate base.
Employer owned and operated as an employee benefit
Privately owned primarily to enhance an unrelated business—retail shopping, hotels, restaurants, private parking facilities, etc.
Privately owned and operated for the sole purpose of providing charging services to PEV owners.
Source: EPRI Technical Report 1021334

## Slide 6: Understanding and Planning Charging Infrastructure
Build Today’s Infrastructure Today
Infrastructure is expensive
  ~ $1500 home, $2500+ public
Focus on Residential
  95% of vehicles end day at home
  Costs can exceed $2200 - $2500
  Cost and lead time minimization
Workplace
  Fleet education and certainty of costs
Public Charging
  Critical vs. convenience
  Viable business models
  Long-term sustaining of infrastructure
Residential
Workplace
Public

## Slide 7: What Have We Learned to Date?
Residential issues
  Multi-unit and tenant dwellings
  Relatively high initial costs
  High adoption of Level 1 at very low cost
Workplace
  Potential has grown—see as driver of adoption
  High installation costs, scaling issues
Public Charging
  Clustering – need to build out networks
  Long-term sustainability of infrastructure
  Underestimated difficulties of locating infrastructure
Residential
Workplace
Public

## Slide 8: Calculating the Type and Number of Public and Workplace EVSEs is Relatively Straightforward

## Slide 9: Customer Expectations of Their Utility Survey results from Southern California
Expectations Of The Utility
Base: General Market (n=602)
Q. 40a How can your electric utility company best help you stay informed about plug-in hybrid electric vehicles?
Q.40b If you were planning on purchasing or leasing a plug-in hybrid electric vehicle, which of the following services would you want from your electric company?

## Slide 10: Ireland – eCar Ireland Project
Public chargers Ireland
  All towns with population of 1500+
  National Plan 1000 (654 to date)
Public Chargers Northern Ireland
  320 in Northern Ireland (installed)
Fast Chargers every 60km on Key interurban routes
  Original Plan 40
    30 (Ire); 9 (NI)
  Revised Plan
    100 (Ire); 14 (NI)
Home/ Workplace
  First 2000 installed free (IRL)
  656 installed to date
Operated by ESB Networks
Source: ESB Networks
Notes: 10

## Slide 11: San Antonio – CPS Energy Public EV Infrastructure Strategy
126 public chargers, most in banks of 4 for installation cost efficiency
Highly traveled, mixed-use sites
Own the infrastructure, but partnered with private property owners for optimal locations
Provided the stations and the network; split the cost of installation with the property owners
Installed separate meters where cost efficient; contracted to reimburse the property owner where behind the meter
Set the pricing and developed a monthly flat rate for public charging
Source: CPS Energy

## Slide 12: Expectations of Two Utilities’ Customers for PEV Services
Chart: 
| Offer home audits | Provide for in-home display of ongoing charging | Provide information about EVs | Offer charging station installation and maintenance | Develop a public charging infrastructure
 | 0.44845 | 0.4741 | 0.45692 | 0.63295 | 0.65324
 | 0.43361 | 0.40732 | 0.44106 | 0.30589 | 0.27965
 | 0.11794 | 0.11858 | 0.10202 | 0.06116 | 0.06711
Chart: 
| Offer home audits | Provide for in-home display of ongoing charging | Provide information about EVs | Offer charging station installation and maintenance | Develop a public charging infrastructure
 | 0.40552 | 0.46589 | 0.47114 | 0.59005 | 0.62427
 | 0.44265 | 0.38207 | 0.37735 | 0.30601 | 0.29136
 | 0.15183 | 0.15204 | 0.15151 | 0.10394 | 0.084363
Develop a public charging infrastructure
Offer charging station installation and maintenance
Provide information about Electric Vehicles
Provide for in-home display of on-going charging
Offer home audits
Important
Somewhat Important
Not Important
CenterPoint Energy
CPS Energy
Notes: Having respondents’ utility develop a public infrastructure is the most important to respondents in San Antonio and Houston. The second most important thing to respondents is for the utility to offer charging station installation and maintenance. These results indicate that San Antonio and Houston residents have substantial expectations regarding their electric utility’s role in supporting PEVs.
Date slide was prepared: 6/6/2012 – weighted
Sample Size: 1,072
Question Number: 1040
Question: Assume you will purchase or lease a Plug-In Hybrid Electric or Battery-Only Electric vehicle. In that case, how important would it be for your electric company to provide the following services?
Utility Version: CenterPoint

## Slide 13: CA PEV Sales – 2013

## Slide 14: CA PEV Sales – 2013 Existing Public EVSE

## Slide 15: CA PEV Sales – 2013 Regional Networks

## Slide 16: Together…Shaping the Future of Electricity