## Slide 1: PG&E SmartAC™ Load Impact Evaluation
May 11, 2016
Jonathan Cook
2016 DRMEC Workshop

## Slide 2: Program Overview
  AC load control through installation of control devices that limit the duty cycles of AC units
    Two types of devices: Switches and PCTs
    Only switches are currently offered for new customers
  Residential and small/medium businesses (SMB)
    151,651 residential accounts and 4,616 SMB accounts at end of summer 2015
    No SMB events since 2011
  Events can be called for testing purposes or in response to emergency conditions
    Events occur between May 1st and October 31st, for up to 6 hours or less in each event
    Program Availability
      100 hours of availability (38 actual)
      No maximum number of events (11 called in 2015)

## Slide 3: Ex Post

## Slide 4: SmartAC Experimental Design
Randomized Control Trial (RCT) for each event
    SmartAC population randomly divided into ten groups of approximately equal size based on the last digit of a device’s serial number
    On a typical event day, some groups are called to have their A/C units cycled (treatment group)
    The groups that are not called serve as a control group whose load can be compared to the treatment group to estimate load impacts
Why does it work?
    Serial number is unrelated to any features of A/C or home that determine energy use
    Because serial number is effectively random, usage of the uncalled groups provide an unbiased estimate of what usage would have been for the controlled devices had they not been called (counterfactual)

## Slide 5: 2015 Test Events
Event Date | SmartRate Day | Weekend Event | “Cascading” Event | Treatment Groups | Start Time | Stop Time
June 25 | Yes | No | Yes | 8 | 1:00 pm | 3:00 pm
 |  |  |  | 3 | 3:00 pm | 6:00 pm
June 30* | Yes | No | No | 7 | 7:00 pm | 8:00 pm
July 1 | Yes | No | No | 9 | 4:00 pm | 7:00 pm
July 28 | Yes | No | No | 0, 1, 5, 7 | 4:00 pm | 7:00 pm
July 29 | Yes | No | No | 9 | 1:00 pm | 5:00 pm
August 15 | No | Yes | No | 8 | 4:00 pm | 6:00 pm
August 17 | Yes | No | Yes | 2 | 12:00 pm | 1:00 pm
 |  |  |  | 4 | 1:00 pm | 2:00 pm
 |  |  |  | 3 | 2:00 pm | 3:00 pm
 |  |  |  | 6 | 3:00 pm | 6:00 pm
 |  |  |  | 8 | 6:00 pm | 7:00 pm
 |  |  |  | 9 | 7:00 pm | 9:00 pm
September 8 | No | No | No | 3 | 1:00 pm | 3:00 pm
September 9 | Yes | No | No | 0, 1, 5, 7 | 4:00 pm | 7:00 pm
September 10 | Yes | No | No | 8 | 4:00 pm | 7:00 pm
September 11 | Yes | No | No | 2 | 3:00 pm | 6:00 pm
* June 30 was PG&E’s system peak day, but the SmartAC event occurred after the peak hour (HE 18)

## Slide 6: Summary of Ex Post Impacts for 4-5 PM
Event Date | Customers Called | Ref Load (kW) | Avg. Impact (kW) | % Impact | Agg. Impact (MW) | Avg. Temp (°F)
6/25 | 12,095 | 2.53 | 0.57 | 23% | 7.0 | 97.3
7/1 | 12,485 | 2.45 | 0.40 | 16% | 5.0 | 94.5
7/28 | 48,168 | 2.42 | 0.49 | 20% | 23.8 | 98.5
7/29 | 12,390 | 2.90 | 0.66 | 23% | 8.1 | 99.3
8/15 | 16,767 | 2.20 | 0.39 | 18% | 6.6 | 96.6
8/17 | 11,124 | 2.85 | 0.63 | 22% | 7.0 | 99.1
9/9 | 48,613 | 2.57 | 0.50 | 19% | 24.3 | 100.3
9/10* | 12,689 | 2.79 | 0.53 | 19% | 6.8 | 99.2
9/11 | 12,410 | 2.52 | 0.45 | 18% | 5.6 | 95.9
Avg. | 20,749 | 2.58 | 0.51 | 20% | 10.5 | 97.9
* The average load impact during HE 17 on 9/10 (CAISO peak) was 0.54 kW and the aggregate impact was 6.8 MW.
Note: The June 30 and September 8 events are not included because they were called from 7 to 8 PM and 1 to 3 PM, respectively.

## Slide 7: Impacts are lower than previous years at comparable temperatures

## Slide 8: Reference Loads are Lower
Notes: A lot of this is solar, but not all of it.

## Slide 9: ExpressStat PCTs aren’t functioning properly
Chart: Hour Ending
LCR | 0.020783 | 0.028077 | 0.019209 | 0.011071 | 0.005445 | 0.0054819 | 0.0026054 | 0.0012301 | -0.0052162 | -0.0023455 | 0.003683 | 0.023194 | 0.14914 | 0.39776 | 0.52892 | 0.6677 | 0.77325 | -0.11222 | -0.26292 | -0.22865 | -0.19198 | -0.14969 | -0.10953 | -0.074082
Zero | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ExpressStat | -0.033659 | -0.074136 | -0.078029 | -0.044322 | -0.031915 | -0.07253 | -0.069074 | -0.039258 | -0.0085262 | -0.0014915 | -0.040845 | -0.065589 | -0.00056324 | 0.031997 | 0.023209 | 0.15581 | -0.015158 | 0.01678 | -0.0068007 | -0.13626 | -0.18678 | -0.15252 | -0.20467 | -0.1663
UtilityPro | 0.058354 | 0.018479 | 0.0019126 | -0.0013045 | -0.0077553 | 0.0029833 | -0.011954 | 0.0081992 | 0.054777 | 0.057656 | 0.13947 | 0.16518 | 0.20169 | 0.35877 | 0.49855 | 0.5916 | 0.61992 | 0.025721 | -0.10174 | -0.095342 | -0.034443 | -0.034523 | -0.025284 | -0.020229

## Slide 10: Older switches aren’t as reliable as newer ones
Communication Failure Rate
Physical Connectivity
Chart: Switch Vintage
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
 | 0.893 | 0.911 | 0.886 | 0.937 | 0.893 | 0.939 | 0.958 | 0.978 | 0.966

## Slide 11: Ex Ante

## Slide 12: Four Fundamental Steps to Produce Ex Ante Forecasts
Estimate the relationship between load impacts and weather conditions for each hour in the resource adequacy window and all subsequent hours (snapback) using historical ex post results (2011-2015)
Estimate relationship between usage and temperature on event days and hot, non-event days (to expand the number of observations) for control customers to predict reference loads under ex ante weather conditions
Combine reference loads with impact estimates to infer load shapes for SmartAC participants
Scale up average customer impacts to aggregate impacts using forecasted enrollment provided by PG&E

## Slide 13: Enrollment Forecast
LCA | Residential |  |  | SMB |  |  | 
 | 2015 | 2016 | 2017 to 2026 | 2015 | 2016 | 2017 | 2026
Greater Bay Area | 51,533 | 50,086 | 49,320 | 1,542 | 1,391 | 1,309 | 753
Greater Fresno | 17,823 | 17,729 | 17,719 | 462 | 413 | 388 | 224
Humboldt | 916 | 925 | 920 | 37 | 34 | 32 | 18
Kern | 7,985 | 8,351 | 8,432 | 246 | 225 | 197 | 122
Northern Coast | 8,629 | 8,629 | 8,483 | 492 | 450 | 394 | 243
Other | 32,461 | 33,067 | 32,805 | 1,103 | 919 | 864 | 497
Sierra | 17,020 | 16,907 | 16,834 | 347 | 317 | 299 | 172
Stockton | 15,284 | 15,492 | 15,511 | 387 | 351 | 330 | 190
Total | 151,651 | 151,186 | 150,024 | 4,616 | 4,100 | 3,856 | 2,220

## Slide 14: Residential Ex Ante Forecasts (2017)
LCA | 2015 Ex Post (4-6 PM, Aug. 15) |  |  | 2015 Ex Ante (1-6 PM, PG&E Aug. 1-in-2) |  |  | 2014 Ex Ante (1-6 PM, PG&E Aug. 1-in-2) |  | 
 | Enrollment | Per Customer (kW) | Aggregate (MW) | Enrollment | Per Customer (kW) | Aggregate (MW) | Enrollment | Per Customer (kW) | Aggregate (MW)
Greater Bay Area | 51,533 | 0.45 | 2.0 | 49,320 | 0.36 | 17.8 | 53,993 | 0.41 | 22.2
Greater Fresno | 17,823 | 0.50 | 0.8 | 17,719 | 0.68 | 12.1 | 17,466 | 0.71 | 12.4
Humboldt | 916 | 0.57 | 0.1 | 920 | 0.15 | 0.1 | N/A | N/A | N/A
Kern | 7,985 | 0.65 | 0.5 | 8,432 | 0.65 | 5.5 | 8,068 | 0.74 | 5.9
Northern Coast | 8,629 | 0.52 | 0.4 | 8,483 | 0.30 | 2.6 | 8,988 | 0.29 | 2.6
Other | 32,461 | 0.42 | 1.3 | 32,805 | 0.55 | 18.0 | 34,336 | 0.58 | 20.1
Sierra | 17,020 | 0.30 | 0.4 | 16,834 | 0.48 | 8.1 | 16,947 | 0.53 | 8.9
Stockton | 15,284 | 0.39 | 0.6 | 15,511 | 0.56 | 8.6 | 14,736 | 0.60 | 8.9
Total | 151,651 | 0.40 | 6.6 | 150,024 | 0.48 | 72.7 | 154,534 | 0.52 | 81.0

## Slide 15: Residential Ex Ante Forecasts (2017)
LCA | 2015 Ex Post (4-6 PM, Aug. 15) |  |  | 2015 Ex Ante (1-6 PM, PG&E Aug. 1-in-2) |  |  | 2014 Ex Ante (1-6 PM, PG&E Aug. 1-in-2) |  | 
 | Enrollment | Per Customer (kW) | Aggregate (MW) | Enrollment | Per Customer (kW) | Aggregate (MW) | Enrollment | Per Customer (kW) | Aggregate (MW)
Greater Bay Area | 51,533 | 0.45 | 2.0 | 49,320 | 0.36 | 17.8 | 53,993 | 0.41 | 22.2
Greater Fresno | 17,823 | 0.50 | 0.8 | 17,719 | 0.68 | 12.1 | 17,466 | 0.71 | 12.4
Humboldt | 916 | 0.57 | 0.1 | 920 | 0.15 | 0.1 | N/A | N/A | N/A
Kern | 7,985 | 0.65 | 0.5 | 8,432 | 0.65 | 5.5 | 8,068 | 0.74 | 5.9
Northern Coast | 8,629 | 0.52 | 0.4 | 8,483 | 0.30 | 2.6 | 8,988 | 0.29 | 2.6
Other | 32,461 | 0.42 | 1.3 | 32,805 | 0.55 | 18.0 | 34,336 | 0.58 | 20.1
Sierra | 17,020 | 0.30 | 0.4 | 16,834 | 0.48 | 8.1 | 16,947 | 0.53 | 8.9
Stockton | 15,284 | 0.39 | 0.6 | 15,511 | 0.56 | 8.6 | 14,736 | 0.60 | 8.9
Total | 151,651 | 0.40 | 6.6 | 150,024 | 0.48 | 72.7 | 154,534 | 0.52 | 81.0

## Slide 16: Residential Ex Ante Forecasts (2017)
LCA | 2015 Ex Post (4-6 PM, Aug. 15) |  |  | 2015 Ex Ante (1-6 PM, PG&E Aug. 1-in-2) |  |  | 2014 Ex Ante (1-6 PM, PG&E Aug. 1-in-2) |  | 
 | Enrollment | Per Customer (kW) | Aggregate (MW) | Enrollment | Per Customer (kW) | Aggregate (MW) | Enrollment | Per Customer (kW) | Aggregate (MW)
Greater Bay Area | 51,533 | 0.45 | 2.0 | 49,320 | 0.36 | 17.8 | 53,993 | 0.41 | 22.2
Greater Fresno | 17,823 | 0.50 | 0.8 | 17,719 | 0.68 | 12.1 | 17,466 | 0.71 | 12.4
Humboldt | 916 | 0.57 | 0.1 | 920 | 0.15 | 0.1 | N/A | N/A | N/A
Kern | 7,985 | 0.65 | 0.5 | 8,432 | 0.65 | 5.5 | 8,068 | 0.74 | 5.9
Northern Coast | 8,629 | 0.52 | 0.4 | 8,483 | 0.30 | 2.6 | 8,988 | 0.29 | 2.6
Other | 32,461 | 0.42 | 1.3 | 32,805 | 0.55 | 18.0 | 34,336 | 0.58 | 20.1
Sierra | 17,020 | 0.30 | 0.4 | 16,834 | 0.48 | 8.1 | 16,947 | 0.53 | 8.9
Stockton | 15,284 | 0.39 | 0.6 | 15,511 | 0.56 | 8.6 | 14,736 | 0.60 | 8.9
Total | 151,651 | 0.40 | 6.6 | 150,024 | 0.48 | 72.7 | 154,534 | 0.52 | 81.0

## Slide 17: Ex Post by Segment

## Slide 18: Device Type
Chart: Hour Ending
LCR | 0.020783 | 0.028077 | 0.019209 | 0.011071 | 0.005445 | 0.0054819 | 0.0026054 | 0.0012301 | -0.0052162 | -0.0023455 | 0.003683 | 0.023194 | 0.14914 | 0.39776 | 0.52892 | 0.6677 | 0.77325 | -0.11222 | -0.26292 | -0.22865 | -0.19198 | -0.14969 | -0.10953 | -0.074082
Zero | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ExpressStat | -0.033659 | -0.074136 | -0.078029 | -0.044322 | -0.031915 | -0.07253 | -0.069074 | -0.039258 | -0.0085262 | -0.0014915 | -0.040845 | -0.065589 | -0.00056324 | 0.031997 | 0.023209 | 0.15581 | -0.015158 | 0.01678 | -0.0068007 | -0.13626 | -0.18678 | -0.15252 | -0.20467 | -0.1663
UtilityPro | 0.058354 | 0.018479 | 0.0019126 | -0.0013045 | -0.0077553 | 0.0029833 | -0.011954 | 0.0081992 | 0.054777 | 0.057656 | 0.13947 | 0.16518 | 0.20169 | 0.35877 | 0.49855 | 0.5916 | 0.61992 | 0.025721 | -0.10174 | -0.095342 | -0.034443 | -0.034523 | -0.025284 | -0.020229

## Slide 19: Single Family vs. Multi-family
Chart: Hour Ending
Single-family | 0.00013675 | 0.0005835 | 0.0041906 | 0.0059313 | 0.003559 | 0.0024483 | 0.0077154 | 0.0065078 | -0.0011992 | -0.0040601 | -0.012076 | -0.0061867 | -0.014983 | -0.015576 | -0.0098153 | 0.15166 | 0.52608 | 0.58468 | 0.5847 | -0.28075 | -0.34522 | -0.19962 | -0.10332 | -0.058804
Zero | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Multi-family | -0.0041678 | 0.00018072 | -0.003773 | 0.0052385 | 0.0020411 | 0.0040157 | 0.00036464 | 0.011855 | 0.0090925 | 0.028316 | 0.051273 | 0.03164 | 0.03044 | 0.034804 | 0.014177 | 0.15559 | 0.39047 | 0.40906 | 0.38842 | -0.20993 | -0.22079 | -0.15936 | -0.089772 | -0.067882

## Slide 20: Marketing Strategy
Chart: Hour Ending
New | -0.0095331 | -0.012002 | 0.0013871 | 0.0026097 | -0.0023626 | -0.002201 | -0.00751 | -0.015051 | -0.011735 | 0.0073895 | 0.011566 | -0.0033674 | -0.0321 | -0.038201 | -0.037698 | 0.15081 | 0.6538 | 0.71964 | 0.68476 | -0.48248 | -0.45346 | -0.25991 | -0.13865 | -0.069651
Zero | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Old | -0.0038729 | -0.0013301 | -0.0013422 | -0.0027908 | -0.0011996 | -0.0080768 | -0.006233 | -0.004127 | -0.0036344 | -0.017816 | -0.035593 | -0.0050455 | -0.0012324 | -0.008735 | -0.011781 | 0.1651 | 0.56947 | 0.62556 | 0.61443 | -0.31854 | -0.39885 | -0.23246 | -0.10636 | -0.074784

## Slide 21: Operability Analysis

## Slide 22: Physical Switch Connectivity
Chart: Switch Vintage
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
 | 0.893 | 0.911 | 0.886 | 0.937 | 0.893 | 0.939 | 0.958 | 0.978 | 0.966

## Slide 23: Communications Failures

## Slide 24: Overall Operability
Switch Vintage | # of Switches in SmartAC Population | % of Total Switches | Physical Failure Rate | Communications Failure Rate | Overall Failure Rate
2007 | 8,912 | 6% | 11% | 25% | 33%
2008 | 44,132 | 30% | 9% | 10% | 18%
2009 | 14,549 | 10% | 11% | 12% | 22%
2010 | 17,643 | 12% | 6% | 10% | 15%
2011 | 22,275 | 15% | 11% | 13% | 23%
2012 | 8,827 | 6% | 6% | 10% | 15%
2013 | 12,307 | 8% | 4% | 12% | 16%
2014 | 10,765 | 7% | 2% | 10% | 12%
2015 | 10,204 | 7% | 3% | 10% | 13%
All | 149,615 | 100% | 8% | 12% | 19%

## Slide 25: Conclusions and Recommendations
  Downward trend in impacts that was first noticed in 2014 evaluation was exacerbated in 2015
    ExpressStat PCTs
    Decline in reliability of older switches
    Declining reference loads?
      Additional analysis needed to understand PG&E’s options going forward
  Additional information about program performance by new segments
    Single family impacts larger than multi-family
    New marketing strategy increases impacts
    Inconclusive comparisons between CARE and Non-CARE

## Slide 26
Contact Information:
Jonathan Cook
jonathancook@nexant.com
202-974-0615
Questions and Discussion