## Slide 1: PG&E Proposals for Refinements to the Resource Adequacy (RA) Program Compliance Year 2017
RA Workshop
February 18, 2016

## Slide 2: Modification to QC Methodology

## Slide 3: PG&E Proposal to Modify the Qualifying Capacity (QC) Calculation for ‘Pre-Dispatch’ Resources
Problem Statement
Proposed Solution
The Commission should calculate the NQC of ‘pre-dispatch’ resources based on submitted economic bids and self-schedules for resources instead of CAISO-scheduled MWs.
Justification for Proposal
Appropriately recognizes the value of capacity offered by all cogeneration facilities to the CAISO market.
Encourages economic bidding of resources, thereby providing more operational flexibility to the CAISO.
Helps prevent over-procurement.
Reduces costs to customers.
The 2016 RA decision adopted by the Commission “directed that QCs for QF cogeneration resources be based on the amount the facility is able to schedule in the day ahead market.”
The Commission should expand the scope of last year’s proposal to apply not only to QF cogeneration facilities, but also to biomass, biogas and cogeneration facilities that are not QFs.
The decision narrowly applies to QF cogeneration resources. A broader application for all ‘pre-dispatch’ resources would provide greater benefits to the grid and better value to customers.
This may undervalue the capacity that is being made available to the CAISO because, due to resource economics, the resource could be scheduled by CAISO at an amount lower than the amount bid in.

## Slide 4: Illustrative Impact of Economic Bidding on a Cogeneration Resource’s Qualifying Capacity
Chart: 2012: Market Prices and Resultant Dispatch for Hypothetical Cogen Resource
Market Clearing Price | 25 | 25 | 25 | 25 | 25 | 30 | 35 | 35 | 30 | 25 | 25 | 25 | 25 | 30 | 30 | 35 | 35 | 40 | 45 | 45 | 40 | 30 | 25 | 25
Unit Bid Price | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30
Chart: 2015: Market Prices and Resultant Dispatch for Hypothetical Cogen Resource
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Market Clearing Price | 25 | 25 | 25 | 25 | 25 | 30 | 35 | 30 | 25 | 20 | 20 | 20 | 20 | 25 | 25 | 30 | 35 | 40 | 45 | 45 | 40 | 30 | 25 | 25
Unit Bid Price | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30
Calculating the QC based on historic CAISO schedules may penalize a resource that provides operational flexibility to the grid through economic bidding or self-scheduling only at times where the resource is economic
  In both examples above, the resource offers its full P-max into the day-ahead market
  However, the resource is scheduled for fewer hours in 2015 compared to 2012, due to lower mid-day prices
Bid at P-max
Scheduled for 13 hours
Scheduled for 10 hours

## Slide 5: Flexible Capacity Requirements Allocation

## Slide 6: PG&E Proposal to Modify the CPUC’s Flexible RA Requirements Allocation Methodology
Problem Statement
The current CPUC methodology used in allocating flexible RA requirements does not reflect cost causation because it is based on a load-serving entity’s (LSE) load ratio share rather than its contribution to the system’s largest 3-hour ramps.
Proposed Solution
The Commission should modify the methodology for allocating flexible RA requirements to its LSEs so that the flexible RA requirements are allocated in proportion to the LSEs’ contribution to the CAISO’s monthly net-load ramps.
Justification for Proposal
Better reflects cost causation.
Aligns the Commission’s and the CAISO’s allocation approaches.
Sends better market signals to developers and LSEs.

## Slide 7: Flexible RA Allocation and Cost Causation
CPUC Allocation Methodology
Based on peak load ratio share (consistent with allocation of system and local RA requirements)
CAISO Allocation Methodology
Based on contribution to the maximum three-hour net load ramp
LSE
Obligation
=
LSE Coincident Peak Load
ISO Coincident Peak Load
x
Total Flexible
Capacity
Requirement
Flexible
Capacity
Need*
=
Δ Load – Δ Wind – Δ Solar PV – Δ Solar Thermal + 3.5% x Expected Peak x Peak Load Ratio Share
Allocating flexible RA requirements based on net load ramp contributions instead of peak load ratio share accomplishes the following:
  Fairness and cost causation: Reflects an individual LSE’s contribution to ramping needs
  Correct market signals: Incentivizes LSEs to reduce ramping needs
  Regulatory consistency: Aligns CPUC and CAISO allocation methodologies
* The delta in each of these terms represents the average percent contribution during the top five greatest 3-hour ramps. For load, this calculation uses historical data. For renewable generation, this calculation uses forecasted data.