## Slide 1: Overview of 3rd Draft VGI Glossary: Terms and Definitions
Dean Taylor
Southern California Edison
June 12, 2017

## Slide 2: Overview
Three industries and several regulators need to come together, understand each other and share a common customer
Existing glossaries were used as much as possible, but could be missing several
3rd Draft is a work-in-progress – sent to google-groups and posted on google-drive on June 11
  Since May 30 meeting
    Received request to define about 90 new terms.
    Added large section explaining the standards
    Added about 60 definitions
Glossary should be living document
Send e-mail to Dean.Taylor@sce.com to join subgroup
Future drafts to be posted on the google-groups site and separate folder on the google-drive site

## Slide 3: New definitions still to be added
Late on June 9, the subgroup was provided new reports and glossaries to review
  IDER Competitive Solicitation Framework Working group final report (CPUC August 2016)
  Storage Multi-Use Application CPUC whitepaper (May 2017)
  CAISO glossary 2016 (Business Practice Manual for Definitions and Acronyms)
Over the weekend many new definitions were provided, but they have not been added to the 3rd draft
After draft 4 we’ll have a call of the subgroup the week of June 19 to review and add a few definitions

## Slide 4: Possible Frameworks / Structures for Organizing Use Cases / Deliverables
VGI white paper framework (CPUC 2013)
Adam Langton’s framework (to be updated based on June 8 call)
Abigail Tinker’s framework
Storage Multi-Use Application whitepaper (May 2017 CPUC)
3rd Draft Glossary has five more frameworks (see slides 9 to 11)
E3’s framework (see next slides)

## Slide 5: E3’s VGI Benefit Matrix
Drawn from energy storage, electric vehicle and smart grid frameworks
Not exhaustively comprehensive, but intended to emphasize:
  Mutually exclusive definitions
  Focus on high value benefits
  Different approaches to quantifying benefit value
Capital Expansion Planning Model with Operational Requirements | Stochastic Production Simulation | Integrated Distributed Energy Resource modeling | Distribution/Power Flow Modeling | Individual Asset Dispatch Optimization

## Slide 6: E3 VGI Benefits Framework: Planning & Capacity
Category | VGI Services |  |  |  | 
 | Customer/ Driver | Distribution | Transmission | Generation | Renewable and GHG
Planning & Procurement |  | Reduce Long-term Distribution Resource Plan Costs | Reduced procurement of Ancillary Services | Reduced portfolio procurement costs to meet forecasted load and reliaiblity targets | Reduced portfolio procurement costs to meet RPS and GHG targets
Reliability | Improve Customer Reliability/Back-up Power | Distribution Investment Deferral (Reliability) | Reduce NERC N-1 Contingency |  | 
 | Islanding |  |  |  | 
Capacity |  | Broad reduction of load growth related infrastructure upgrade costs |  | System Generation Capacity (Reduce LOLP) | Renewable Firming (Increase NQC/ELCC)
 |  | Targeted placement for high value deferrals (e.g. Non-Wires Alternatives and Local Integrated Resource Plans) |  | Local Generation Capacity (Reduce LOLP) | 
 | Demand Charge Reduction |  | Transmission Access Charge Reduction |  | 
 |  |  |  | Flexible Capacity | 
 |  | Option Value (Modularity) |  |  | 
Important distinction between utility planning and policy goals
Targeted Deployment

## Slide 7: E3 VGI Benefits Framework: Operational
Category | VGI Services |  |  |  | 
 | Customer/ Driver | Distribution | Transmission | Generation | Renewable and GHG
Time Shfit | TOU Energy Charge Reduction | Distribution Peak Shaving | Reduce Transmission Congestion | Wholesale Time Shift/Arbitrage | Renewable Generation Time Shift
 | Option value (Volatility) |  |  | Option value (Volatility) | 
 |  | Backflow Prevention |  |  | Reduce Renewable Curtailment
 |  |  |  | Unit Commitment/Start Up Cost Reduction | 
Generation Operation |  |  |  | Efficiency Improvement/ Emissions Reduction | 
 |  |  |  | Reduce System Production Cost | 
 |  | O&M Reduction/Equipment Life Extension |  |  | 
 |  | Loss Reduction |  |  | 
Transmission & Distribution Operations |  | Voltage Support |  |  | Renewable Power Smoothing
 | Customer Power Factor Improvement | VAR Support |  | Power Factor Improvement/Loss Reduction | Renewable Generation Power Factor Improvement
 | Improve Customer Power Quality | Distribution Investment Deferral (Power Quality) |  |  | 
 |  |  |  |  | Increase Renewable DG Hosting Capacity
$ values for T&D operating benefits have been hard to generalize and small relative to other categories

## Slide 8: E3 VGI Benefits Framework: Operating AS
Category | Service | Description
Operating Ancillary Services | Inertial Frequency Response | Inherent in the system due to rotating characteristic of conventional generation (synchronous generators). The Inertial Frequency Response provides counter response within seconds to arrest the frequency deviation.
 | Primary Frequency Response | The instantaneous proportional increase or decrease in real power output in response to system frequency deviations. The Primary Frequency Response is generally delivered completely within 14 seconds.
 | Fast/Accurate Frequency Regulation | Provide AGC frequency regulation in AS markets that is faster and more accurate than traditional generation resources
 | Frequency Regulation (Secondary) | Executed by Automatic Generation Control (AGC) . The AGC system deploys regulating reserves to restore the frequency closer to scheduled frequency. AGC action can take anywhere from seconds to minutes depending on the resource
 | Real-Time/Balancing Energy | Energy dispatched directed by the grid operator every 5-10 minutes to balance load and generation within the hour
 | Ramp (MW/min) | Ability to rapidly increase or decrease output (measured in MW/Min) to manage uncertainty and forecast error for generation and load
 | Load Following (5 - 60 minutes) | balancing load and generation in the 5-60 minute time frame between 5 minute imbalance energy and hourly real-time energy markets (e.g. CAISO Flexi-Ramp and FRAC-MOO)
 | Hour to Hour Ramp | Increase generation over multiple hours, typically considered for morning and evening hours when large increases/decreases in net load are expected over several hours.
Existing Markets (for loads)

## Slide 9: E3 VGI Benefits Framework: Contingency AS
Category | Service | Description
Contingency Reserves | Sync/Spinning Reserve | Generation (or responsive load) that is ready to respond immediately, in case a generator or transmission line fails unexpectedly. Spinning reserve begins to respond immediately and must fully respond within ten minutes. ISO rules differ on whether 10 minute reserves must be synchronized to the grid
 | Non-spinning Reserve | Similar to spinning reserve, except that the resource is not necessarily required to be synchronized to the grid and the response does not need to begin immediately. Full response is generally required within 10 to 30 minutes.
 | Replacement Reserve | An additional reserve required in some regions. It begins responding in 30 to 60 minutes.
Mutually exhaustive definitions
Focus initially on high value benefits that easily generalized
Define how $ benefits are to be quantified

## Slide 10: VGI Benefit Groupings – Draft Option 1
Wholesale market services (ISO / RTO): 1) frequency regulation, 2) spinning, non-spinning and supplemental reserve, 3) load following / ramping support for renewables 4) capacity markets 5) Demand Response Auction Mechanism 6) real-time and day-ahead energy markets 7) energy arbitrage 8) black start, 9) voltage and/or reactive power support
Distribution infrastructure benefits: 1) distribution upgrade deferral 2) local distributed generation support 3) peak load shedding: 4) resource adequacy?
DSO / utility market benefits: 1) DERMS, 2) ADMS; 3) Rule 21 smart inverter management
Customer facing benefits: 1) retail energy time shift with rates, 2) demand leveling with rates or controls, 3) power quality, 4) power reliability, 5) monetizing of GHG and air pollution reduction benefits, 6) maximizing customer use of renewable generation 7) demand leveling with BMS or parking lot EVEMS 8) back-up power
Societal benefits: 1) adoption of EVs, 2) low-cost reductions in GHG and air pollutants, 3) low cost of EV ownership, 4) net jobs

## Slide 11: Other Draft Options for Grouping VGI
VGI Beneficiary groupings (option 2) by level
  Site host / customer benefits - includes commercial and residential situations including homes
  All utility customer benefits – TBD
  ISO whole sale market benefits - TBD
  DSO / utility markets – TBD
  Societal benefits – TBD
VGI grouping (option 3)
  Wholesale market solutions TBD
  DSO / utility markets – TBD
  Non-market solutions – TBD
VGI benefit grouping (option 4) by value category
  Reducing energy generation cost - TBD
  Reducing site hosts and EV driver’s electric bills - TBD
  Deferring distribution upgrades - TBD
  Improving reliability - TBD
  Aligning EV load with renewable integration - TBD
  Measuring fuel switching – gasoline to EV (required by Low Carbon Fuel Standard for non-residential charging)

## Slide 12: Another grouping option (6) VGI types
Charging level incentives (foundational)
  Tools include rebates for lower level charging, modifying current allowance policy, demand charge design
TOU Rate Design and Adoption Policy (foundational)
  Tools include TOU rate design and policies to require or encourage TOU rate adoption for EVs
V1G (or managed or controlled charging): Unidirectional power flow under central or customer control enabling vehicles to charge and provide wholesale market services. Includes varying the charge rate at the charging station, EV management system, parking lot EV Energy management system or building management system in order to provide demand response, ancillary services or other market services.
V2G Similar to V1G but bidirectional power flow to the grid. (we have two lengthy alternative definitions in glossary)

## Slide 13: Thank you

## Slide 14: Appendix

## Slide 15: Used Existing Glossaries to large extent
VGI White paper, CPUC Energy Division
California VGI Roadmap, Cal-ISO with CPUC & CEC
Modern Distribution Grid 2017, Vol 1, USDOE
Electrical Energy Storage, CPUC Planning and Policy Division report
2020 Strategic Analysis of Energy Storage in CA, CEC
Energy Storage Phase 2 Interim Staff Report, CPUC Energy Division
Battery Storage Economics, Rocky Mountain Institute
Engaging Utilities in TE in the U.S., Europe and China, E3
Glossary of Definitions, North America Energy Reliability Council

## Slide 16: More 3rd draft terms and definitions
Short-dwell or opportunity charging locations: locations where a vehicle is parked for a few minutes or few hours and can charge. An EV may or may not need a charge at these locations. Examples include charging at restaurants, retail, rest-stops, gas stations, doctors, dentists and similar service providers
Long-dwell charging locations: locations where vehicles are typically parked for more than four hours and can charge. Examples includes homes, workplaces, fleets, destination centers and mixed-use locations
Fleet charging: charging stations for a business’s own commercial EVs
Workplace Charging: charging stations for a employees, staff, students, teachers, professors (but not visitors)
Destination Center Charging: Charging stations located at sites that attract longer distance trips including, but not limited to, hotels, resorts, theme parks, major malls, parks, beaches, theaters, sports centers, concert halls, casinos
Multi-unit dwelling charging: refers to charging stations in common areas of condos and apartments (usually a commercial account for a utility)

## Slide 17: More 3rd draft terms and definitions
Single family home charging: Charging stations in driveways, carports or garages in residences designed for individuals or a family. Includes both attached and detached homes, but excludes large apartment and condo complexes without individual garages or carports near the home.
Urban DC fast charging plaza: large cluster of away-from-home, public-access, DC fast charge stations in urban and suburban areas (could be on a travel corridor or not)
Corridor DC fast charging plaza: large cluster of away-from-home, public –access, DC fast charge stations away-from urban areas along travel corridors
Restaurant, retail and rest-stop charging (can be level 1, 2 or DC) –includes small clusters of charging at those locations but excludes large scale charging plazas
Mixed use charging: charging where multiple types of users typically charge. For example, city parking structures used by residents of MUDs, workplaces, city fleet vehicles and visitor to regional destination centers
Street or curbside charging: Charging stations (AC or DC) on a curb

## Slide 18: “Use case” draft definition
Use case: Defines a grid problem that can be solved with one or more solutions (technical and/or non-technical) and describes the solutions. Use cases are generally vision documents that help clarify a goal or vision of a project or a solution including its usefulness. Use Case is a list of actions or event steps, typically defining the interactions between Actor(s) or Role(s) and a system, to achieve a goal” means that each use case has to be tied to a specific value it is providing (i.e. describe how it is producing that value). Typically VGI use case questions include:
  Is VGI operationally viable for this use?
  What are the potential benefits of VGI in this use case? Can these benefits be monetized via existing market structure? If not, how should they be valued?
  Is VGI cost-effective for this use?
  What barriers or trade-offs are preventing or slowing deployment of VGI in this use?
  What are the policy options to address the identified barriers or trade-offs encountered by VGI implementation?
  Should procurement targets or other policies to encourage VGI be considered for this use?
  Note – above definition was modified from #6: Energy Storage Phase 2 staff report

## Slide 19: 1st Draft terms and definitions
Charging station manufacturer: company that makes the charging station
Charging station maintainer: company that provides repair and maintenance service to the charging stations and may only provide that service
Charging station installer: company that provides installation service and may only provide that service
Charging infrastructure provider: company or companies that provides the electrical and civil work associated with the make-ready and utility side infrastructure for the charging station
Charging station services provider: provides services to the owner of the charging station but the number of services may depend on the package selected or vary between different companies in the market
Charging Station Operator (CSO): the charging station operator installs, operates and maintains the EVSE to facilitate a reliable charging experience for PEV owners. (aka Charge Spot Operator or charge point operator) (from glossary #8)
Charging network operator: provides services including ISO wholesale market services

## Slide 20: 1st Draft Terms and Definitions
Charging station / device: The off-board-the-EV unit that contains a charging connector that is used to insert into the EV. This is a broad term that may include AC, DC, inductive (e.g. wireless) or conductive charging and may include or exclude the charger
Charging plaza or center: is large collection of public-access charging stations
Make-ready: refers to the behind-the-meter infrastructure up-to stub, but not including charging station or the utility side equipment. It typically the does not utility meter or charging station, but may include hardware (panel, trenching, wiring) and civil work (trenching, planning, installation)
Traditional utility distribution service equipment or utility side-of-the meter infrastructure: includes the meter, overhead or underground service to the meter, transformer upgrade, etc.
Charging infrastructure includes the make-ready and the utility-side-of the meter infrastructure, but not include charging station

## Slide 21: High level 1st draft terms and definitions
VGI Vehicle Grid Integration
  very broad term that encompasses the many ways in which an EV can provide benefits or services to the grid and bring benefit to society
  optimizing EV interaction with the grid
Technical solutions:
  VGI solutions that need a communication protocol.
Non-Technical or foundational solutions:
  VGI solutions that do not need a communication protocol (e.g. rates, charging station rebates, allowances, fuel switching measurement)
Market services:
  TBD - probably means ISO wholesale market and DSO / utility market
Non-market services and benefits:
  TBD - probably same as non-technical