## Slide 1: OVGIP VGI Use Case Summary Reference: EPRI Report 3002005994 Dated December 2015
VGI Use Case Sub Working Group
22 June 2017
George Bellino, EPRI

## Slide 2: USE CASES apply to the Open Vehicle Grid Integration Platform (OVGIP)

## Slide 3: OVGIP Use Cases Correlate with CPUC VGI Roadmap Priorities
1 Automated Utility Electricity Rate Tariff Processing
2 Aggregation: Demand Response/Balancing Resource
3 Interface with Home Energy Management System / ESI
4 Interface with Building Energy Management System
5 Pricing Signal Events: Real Time/Dynamic Pricing
7 Optimized Load Management (ISO/IEC 15118)
8 Vehicle Roaming
9 EVSE Networking Functionality
6 Interface with EVSE Network Provider
10 Metering and Data Exchange
VGI Use Case Priorities
OVGIP Use Cases

## Slide 4: Utility Programs & Related Use Cases

## Slide 5: Use Case 1: Automated Tariff Processing
Description:
  PEV owner’s Utility Residential Electricity Rate Tariffs are accessible from the utility for automated download through the OVGIP to the OEM PEVs.
  Applies to residential owners in single and multiple unit dwellings whereby PEV charging is associated to and measured by the whole house meter or residential unit meter for MUDs.
Primary Actors:
  Utility, OVGIP, OEM Servers, PEV
Objective
  PEV owner has the ability to automatically schedule, through the PEV, charging to occur during the most economical periods of the day and night according to the residential owner’s selected residential/PEV electricity rate schedule
    i.e. Whole House Standard Rate (Tiered?), Whole House TOU Rate, PEV Rate (separately metered PEV charging), Whole House with PEV TOU Rate, CPP with optional TOU Rate, etc.
  Requires standardized formatting of Utility Rate Tariffs for automated transmission

## Slide 6: Use Case 2: Aggregation: Locational DR / CPP / Renewables Load Balancing
Description:
  OVGIP is the OEM central server for PEV aggregation grid services
    Capable of receiving DR event signals from the utility or other ESP/Aggregator entity, and processing signals to the OEM Servers which are to identify vehicles plugged-in, availability (opt in), and increase/decrease load capacity per the DR event.
Primary Actors:
  ISO/Utility/ESP, Aggregator/OVGIP, OEM Servers, PEV, Customer
Objective:
  Functionality includes capability to decrease or increase load according to the ISO or Utility load versus supply imbalance conditions (i.e. renewables over/under generation or intermittency)
  OEMs may be required to provide day ahead DR capacity projections for collective/aggregated bidding per prescribed regional segments through the OVGIP for ISO/Utility related energy market and capacity bidding programs.
  Consideration for prioritization per primacy rules: i.e. When facility is DR Program participant – controls PEV load according to facility EMS load control strategy.
  OEM servers are able to define the available load capacity of PEVs plugged-in within the regional or locational parameters of the DR event message, available capacity (increase/decrease load capacity), determines opt in/opt out based on customer preferences.
  OVGIP allocates capacity for OEMs to execute the DR command and reports aggregated PEV capacity to the requesting source.

## Slide 7: Use Case 3: Interface with Home EMS
Description:
  OVGIP interfaces and communicates with the Home Energy Management System, ESI, or other gateway within the residence for the purpose of residential owner monitoring and managing of the PEV charging load including response to DR and Dynamic Pricing signals.
  Example is whole house DR programs – customer determines priorities for curtailing house hold loads including PEV charging.
Primary Actors:
  Utility, HEMS, OVGIP/OEM Servers, PEV
Objective:
  The OVGIP receives load management information and signals from the residential energy management system (Home Area Network), ESI gateway or other home gateway device.
    Residential customer has direct control of PEV charging schedule and preferences.
    Communications can be open source API or adapts protocols of major HEMS suppliers such as Google Thread, Samsung Smartthings, Tendril, IControl, and Apple HomeKit.

## Slide 8: Use Case 4: Interface with Building EMS
Description:
  OVGIP interfaces and communicates directly with the Building Energy Management System within the facility for the purpose of integrating, monitoring and managing the PEV charging load (i.e. Demand Charge Mitigation, Load shedding/shifting, DR response, etc.)
Primary Actors:
  Utility, BMS, OVGIP, OEM Servers, PEV
Objective:
  OVGIP will adapt to the facilities' BMS communications protocol and establish an interoperable API to receive commands and information from the BMS to the individual OEM servers
  OVGIP establishes two way communications with the BMS in order to integrate the PEV drivers’ preferences and PEV charge power/time requirements/information for the BMS automated load control determinations
  Expectation is the major BMS suppliers may adapt to or become interoperable with IEEE2030.5

## Slide 9: Use Case 5: Interface with EVSE Network Provider
Description:
  OVGIP interfaces and communicates with the location's EVSE Network Provider for the purpose of monitoring and managing the PEV charging load.
Primary Actors:
  EVSE Network Provider, OVGIP/OEM Servers, PEV
Objective:
  OVGIP is to have bidirectional communications with the EVSE Network Provider and the capability to receive and process load management information and signals with the location's responsible EVSE Network Provider.
  Communications relationship between the OVGIP and the EVSE Network Provider is to ensure the information about the PEV Driver's preferences and the PEV charge status / requirements (load request) are transmitted to the EVSE Network Provider
    Purpose to ensure the PEV load allocation determinations by the EVSE Network Provider based on PEV driver preferences.
    Emphasis is on ensuring the PEV Driver's transportation needs are met

## Slide 10: Use Case 6: Dynamic Pricing Signal Events
Description:
  OVGIP receives Real Time Price (RTP) or Dynamic Price signals from utility or other energy service provider (ESP) and processes price signals to the OEM servers to the PEV
Primary Actors:
  Utility/ESP, OVGIP/OEM Servers, PEV, Customer
Objective:
  Provide automated processing of RTP or other dynamic pricing signals by the OVGIP from the Utility or ESP or Aggregator to the OEM Servers to the PEV.
  OEM servers are to define the PEVs plugged-in within the applicable region or group affected by the pricing signal and communicates the pricing event to the PEV.
  Intent is the PEV Driver will be able to set price thresholds in the PEV, and based on time charge is needed the PEV can determine to stop, curtail, or continue charging.

## Slide 11: Use Case 7: Optimized Load Management (ISO/IEC 15118)
Description:
  OVGIP provides interoperability for processing price tariffs per the ISO/IEC 15118 protocol.
  OVGIP receives energy market and pricing signals from ISO, utility, or other ESP and processes tariff table through the web application to the eMobility Operator
Primary Actors:
  Utility/ESP, OVGIP, eMobility Operator
Objective:
  OVGIP to perform automatic authentication/authorization process
  OVGIP provides DCH functionality to process Utility or ESP tariff tables to the eMobility Operator which is to be provided to the SECC (EVSE) to the EVCC (PEV) as part of the EVSE/PEV negotiation process for determining charge session profile under the provisions of the ISO/IEC 15118 protocol
  OVGIP receives energy (maximum power etc.) and pricing (peak loads etc.) signals from utility and process the tariff table to eMobility Operators then to EVSEs or directly to EVSEs.
  PEV drivers input (or preset) departure time according to their own traveling need.
  Tariff tables transferred through SECC to EVCC via ISO15118
  PEV charging according to agreed charge profile (with ability to reengage negotiation when new tariff tables are sent)

## Slide 12: Use Case 8: Vehicle Roaming Scenario A
Description:
  OVGIP will provide Clearing House function for tracking Roaming transactions between eMobility Operators and/or EVSE Network Providers for consolidated billing to the customer
Primary Actors
  OVGIP/OEM Servers, eMobility Operators, EVSE Network Providers
Objective:
  Establish the capability for the OVGIP to reconcile and confirm authentication between EVSE network providers and multiple eMobility Operators.
  The OVGIP is to communicate through broadcast signals with eMobility Operators to validate customer contracts when the associated EVSE or charge point provider does not recognize the PEV contract ID.
  The OVGIP determines the cognizant eMobility Operator and provides information to the EVSE associated eMobility Operator to allow charging.
  OVGIP provides clearing house function to reconcile the customer costs between eMobility Operators at the end of the month to be able to include in customer’s

## Slide 13: Use Case 8: Roaming Scenario B
Description:
  OVGIP provides clearing house function for intra utility roaming transactions
  PEV roams between utility service territories but wants all PEV charging costs credited to primary residential utility account
Primary Actors
  Utilities, OVGIP, EVSE Network Providers, Customers
Objective:
  Provide customer ability to enroll in multiple utility PEV charging programs and consolidate into customer’s primary residence utility account.
  Provide clearing house function for collecting customer data on PEV charging sessions (consumption, date, time duration) from across multiple utility service territories for intra utility consolidated billing

## Slide 14: Use Case 9: EVSE Networking Functionality
Description:
  OVGIP provides standard EVSE Networking functionality for interfacing and interacting with EVSEs from multiple manufacturers and distributors.
Primary Actors
  Utilities, OVGIP, EVSE, Customers
Objective:
  OVGIP is to provide EVSE manufacturers and distributors with networking functionality to monitor and manage their EVSE location, status and utilization.
  Networking functionality is to provide customer resource management for authentication and authorization of customer account IDs and recording of customer charge session electricity consumption.
  Site hosts have the ability to replace EVSEs and/or the network provider in a plug and play manner, without losing their OVGIP access or functionality.
  Provides association between EVSE and PEV through OVGIP

## Slide 15: Use Case 10: Metering and Data Exchange
Description:
  California CPUC has initiated proceedings to allow use of 3rd party owned sub meters specifically for PEV charging measurement. Under the guidelines for 3rd Party ownership, the owner is responsible to engage with a MDMA to provide the association data binding the PEV submeter to a premise or primary meter and the related electric consumption data from the submeter to the utility for subtractive billing processing.
Primary Actors
  Utility, OVGIP/OEM Servers, EVSE Sub Meter Owners, Customer
Objective:
  Access and exchange energy usage data, as a proxy of PEV energy use, using: (a) premise or primary meter, and (b) PEV/EVSE sub-meter.
  Use meter data for monitoring energy-use, measurement and verification (M&V) of DR settlement, characterizing baseline, and real-time monitoring of customer response.
  Utility networks (e.g., AMI, Green Button/ESPI, SEP 2.0) shall be used to access premise or primary meter data.
  Sub-meter energy usage data shall be accessible using Green Button/ESPI standardized data format for ease of access and integration with utility’s back-end MDMS.
  Utility DR reporting standards (e.g., OpenADR 2.0b) shall be supported for ease of access and integration with utility’s back-end DR management systems (DRMS)..